## Slide 1: IP Basics
Unix/IP Preparation Course
July 19, 2009
Eugene, Oregon, USA
hervey@nsrc.org

## Slide 2: Layers
Complex problems can be solved using the common divide and conquer principle. In this case the internals of the Internet are divided into separate layers.
Makes it easier to understand
Developments in one layer need not require changes in another layer
Easy formation (and quick testing of conformation to) standards
Two main models of layers are used:
OSI (Open Systems Interconnection)
TCP/IP

## Slide 3: OSI Model

## Slide 4: OSI
Conceptual model composed of seven layers, developed by the International Organization for Standardization (ISO) in 1984.
Layer 7 – Application (servers and clients etc web browsers, httpd)
Layer 6 – Presentation (file formats e.g pdf, ASCII, jpeg etc)
Layer 5 – Session (conversation initialisation, termination, )
Layer 4 – Transport (inter host comm – error correction, QOS)
Layer 3 – Network (routing – path determination, IP[x] addresses etc)
Layer 2 – Data link (switching – media acces, MAC addresses etc)
Layer 1 – Physical (signalling – representation of binary digits)
Acronym: All People Seem To Need Data Processing

## Slide 5: TCP/IP
Generally, TCP/IP (Transmission Control Protocol/Internet Protocol) is described using three to five functional layers. We have chosen the common DoD reference model, which is also known as the Internet reference model.
Process/Application Layer consists of applications and processes that use the network.
Host-to-host transport layer provides end-to-end data delivery services.
Internetwork layer defines the datagram and handles the routing of data.
Network access layer consists of routines for accessing physical networks.

## Slide 6: TCP/IP model – the “hourglass”
Browser
MUA
HTTP
SMTP
TCP
UDP
DNS
RTSP
Video
Player
ICMP
PING
IP
802.11
WiFi
Ethernet
PPP
Copper
Fiber
Pigeons
Air :)

## Slide 7: OSI and TCP/IP

## Slide 8: Encapsulation & Decapsulation
Lower layers add headers (and sometimes trailers) to upper layers packets
Application
Transport
Network
Data Link
Data
Data
Header
Transport Packet
Header
Data
Header
Header
Network Packet
Data
Header
Header
Header
Header
Trailer
Trailer

## Slide 9: Frame, Datagram, Segment, Packet
Different names for packets at different layers
Ethernet (link layer) frame
IP (network layer) datagram
TCP (transport layer) segment
Terminology is not strictly followed
we often just use the term “packet” at any layer

## Slide 10: Summary
Networking is a problem approached in layers.
OSI Layers
TCP/IP Layers
Each layer adds headers to the packet of the previous layer as the data leaves the machine (encapsulation) and the reverse occurs on the receiving host (decapsulation)

## Slide 11: So what is an IPv4 address anyway?
32 bit number (4 octet number) can be represented in lots of ways:
133
27
162
125
10000101
00011011
10100010
01111101
85
1B
A2
7D

## Slide 12: More to the structure
Hierarchical Division in IP Address:
Network Part (Prefix)
describes which network
Host Part (Host Address)
describes which host on that network
Boundary can be anywhere
used to be a multiple of 8 (/8, /16/, /24), but not usual today
Network
Host
205 . 154 . 8
1
11001101 10011010 00001000 00000001
Mask

## Slide 13: Network Masks
Network Masks help define which bits are used to describe the Network Part and which for hosts
Different Representations:
decimal dot notation: 255.255.224.0 (128+64+32 in byte 3)
binary: 11111111 11111111 111 00000 00000000
hexadecimal: 0xFFFFE000
number of network bits: /19 (8 + 8 + 3)
Binary AND of 32 bit IP address with 32 bit netmask yields network part of address

## Slide 14: Sample Netmasks
137.158.128.0/17 (netmask 255.255.128.0)
1000 1001
1001 1110
1 000 0000
0000 0000
1111 1111
1111 1111
1 000 0000
0000 0000
1100 0110
1000 0110
0000 0000
0000 0000
1111 1111
1111 1111
0000 0000
0000 0000
1100 1101
0010 0101
1100 0001
10 00 0000
1111 1111
1111 1111
1111 1111
11 00 0000
198.134.0.0/16 (netmask 255.255.0.0)
205.37.193.128/26 (netmask 255.255.255.192)

## Slide 15: Allocating IP addresses
The subnet mask is used to define size of a network
E.g a subnet mask of 255.255.255.0 or /24 implies 32-24=8 host bits
2^8 minus 2 = 254 possible hosts
Similarly a subnet mask of 255.255.255.224 or /27 implies 32-27=5 host bits
2^5 minus 2 = 30 possible hosts

## Slide 16: Special IP Addresses
All 0’s in host part: Represents Network
e.g. 193.0.0.0/24
e.g. 138.37.128.0/17
e.g. 192.168.2.128/25 (WHY ?)
All 1’s in host part: Broadcast (all hosts on net)
e.g. 137.156.255.255 (137.156.0.0/16)
e.g. 134.132.100.255 (134.132.100.0/24)
e.g. 192.168.2.127/25 (192.168.2.0/25) (WHY ?)
127.0.0.0/8: Loopback address (127.0.0.1)
0.0.0.0: Various special purposes (DHCP, etc.)

## Slide 17: Networks – super- and subnetting
/24
/25
/27
....
By adding one bit to the netmask,
we subdivide the network into two
smaller networks. This is subnetting.
i.e.: If one has a /26 network (32 – 26 =
6 => 2^6 => 64 addresses), that network
can be subdivided into two subnets, using
a /27 netmask, where the state of the last
bit will determine which network we are
addressing (32 – 27 = 5 => 2^5 => 32
addresses). This can be done recursively
(/27 => 2 x /28 or 4 x /29, etc...).
Example: 192.168.10.0/25 (.0 - .127) can
be subnetted into 192.168.10.0 / 26 and
192.168.10.64 / 26
/27
/27
/27
/27
/27
/27
/27
/26
/26
/26
/26
/25

## Slide 18: Networks – super- and subnetting
/24
/25
/25
Inversely, if two networks can be
“joined” together under the same netmask,
which encompasses both networks, then
we are supernetting.
Example:
Networks 10.254.4.0/24 and 10.254.5.0/24
can be “joined” together into one network
expressed: 10.254.4.0/23.
Note: for this to be possible, the networks
must be contiguous, i.e. it is not possible
to supernet 10.254.5.0/24 and 10.254.6.0/24
/26
/26
/26
/26

## Slide 19: Numbering Rules
Private IP address ranges (RFC 1918)
10/8 (10.0.0.0 – 10.255.255.255)
192.168/16 (192.168.0.0 – 192.168.255.255)
172.16/12 (172.16.0.0 – 172.31.255.255)
Public Address space available from AfriNIC
Choose a small block from whatever range you have, and subnet your networks (to avoid problems with broadcasts, and implement segmentation policies – DMZ, internal, etc...)

## Slide 20: Linux IP related settings
Files
/etc/network/interfaces
/etc/hosts
/etc/hostname (optional)
Commands
ifconfig eth0 196.200.218.x/24
route add default gw 192.200.218.254
hostname pc1.cs.uoregon.edu

## Slide 21: Routing
Every host on the internet needs a way to get packets to other hosts outside its local network.
This requires special hosts called routers that can move packets between networks.
Packets may pass through many routers before they reach their destinations.

## Slide 22: The route table
All hosts (including routers) have a route table that specifies which networks it is connected to, and how to forward packets to a gateway router that can talk to other networks.
A simple route table (as might be shown by route -n):
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U eth0
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0

## Slide 23: What do route table entries mean?
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U eth0
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
The destination is a network address.
The gateway is an IP address of a router that can forward packets (or 0.0.0.0, if the packet doesn't need to be forwarded).
The genmask is a netmask.
Flags indicate the type of route.
The interface is the network interface that is connected to that network.

## Slide 24: How the route table is used
A packet that needs to be sent has a destination IP address.
For each entry in the route table (starting with the first):
Compute the logical AND of the destination IP and the genmask entry.
Compare that with the destination entry.
If those match, send the packet out the interface, and we're done.
If not, move on to the next entry in the table.

## Slide 25: Reaching the local network
Suppose we want to send a packet to 128.223.143.42 using this route table.
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U eth0
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
In the first entry:
128.223.143.42 AND 255.255.254.0 = 128.223.142.0
This matches the destination of the first routing table entry, so send the packet out interface eth0.
That first entry is called a network route.

## Slide 26: Reaching other networks
Suppose we want to send a packet to 72.14.213.99 using this route table.
Destination Gateway Genmask Flags Interface
128.223.142.0 0.0.0.0 255.255.254.0 U eth0
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
72.14.213.99 AND 255.255.254.0 = 72.14.212.0
This does not match the first entry, so move on to the next entry.
72.14.213.99 AND 0.0.0.0 = 0.0.0.0
This does match the second entry, so forward the packet to 128.223.142.1 via eth0.

## Slide 27: The default route
Note that this route table entry:
Destination Gateway Genmask Flags Interface
0.0.0.0 128.223.142.1 0.0.0.0 UG eth0
matches every possible destination IP address. This is called the default route. The gateway has to be a router capable of forwarding traffic.

## Slide 28: More complex routing
Consider this route table:
Destination Gateway Genmask Flags Interface
192.168.0.0 0.0.0.0 255.255.255.0 U eth0
192.168.1.0 0.0.0.0 255.255.255.0 U eth1
192.168.2.0 0.0.0.0 255.255.254.0 U eth2
192.168.4.0 0.0.0.0 255.255.252.0 U eth3
0.0.0.0 192.168.1.1 0.0.0.0 UG eth0
This is what a router's routing table might look like. Note that there are multiple interfaces for multiple local networks, and a gateway that can reach other networks.

## Slide 29: Forwarding packets
Any UNIX-like (and other) operating system can function as gateway:
  In Linux in /etc/sysctl.conf set: net.ipv4.ip_forward=1
Without forwarding enabled, the box will not forward packets from one interface to another: it is simply a host with multiple interfaces.