## Slide 1: Layer 2 Network Design
Carlos Vicente
University of Oregon
cvicente@uoregon.edu

## Slide 2: Campus Network Design - Review
A good network design is modular and hierarchical, with a clear separation of functions:
  Core: Resilient, few changes, few features, high bandwidth, CPU power
  Distribution: Aggregation, redundancy
  Access: Port density, affordability, security features, many adds, moves and changes

## Slide 3: Campus Network Design - Simple
ISP1
Access
Core
Network Border
Distribution

## Slide 4: Campus Network Design - Redundant
ISP1
ISP2
Access
Core
Network Border
Distribution

## Slide 5: In-Building and Layer 2
There is usually a correspondence between building separation and subnet separation
  Switching inside a building
  Routing between buildings
This will depend on the size of the network
  Very small networks can get by with doing switching between buildings
  Very large networks might need to do routing inside buildings

## Slide 6: Layer 2 Concepts
Layer 2 protocols basically control access to a shared medium (copper, fiber, electro-magnetic waves)
Ethernet is the de-facto standard today
  Reasons:
    Simple
    Cheap
    Manufacturers keep making it faster

## Slide 7: Ethernet Functions
Source and Destination identification
  MAC addresses
Detect and avoid frame collisions
  Listen and wait for channel to be available
  If collision occurs, wait a random period before retrying
    This is called CASMA-CD: Carrier Sense Multiple Access with Collision Detection

## Slide 8: Ethernet Frame
SFD = Start of Frame Delimiter
DA = Destination Address
SA = Source Address
CRC = Cyclick Redundancy Check

## Slide 9: Evolution of Ethernet Topologies
Bus
  Everybody on the same coaxial cable
Star
  One central device connects every other node
    First with hubs (repeated traffic)
    Later with switches (bridged traffic)
  Structured cabling for star topologies standardized

## Slide 10: Switched Star Topology Benefits
It’s modular:
  Independent wires for each end node
  Independent traffic in each wire
  A second layer of switches can be added to build a hierarchical network that extends the same two benefits above
  ALWAYS DESIGN WITH MODULARITY IN MIND

## Slide 11: Hub
Receives a frame on one port and sends it out every other port, always.
Collision domain is not reduced
Traffic ends up in places where it’s not needed

## Slide 12: Hub
Hub
A frame sent by one node is always sent to every other node.
Hubs are also called “repeaters” because they just “repeat”
what they hear.

## Slide 13: Switch
Learns the location of each node by looking at the source address of each incoming frame, and builds a forwarding table
Forwards each incoming frame to the port where the destination node is
  Reduces the collision domain
  Makes more efficient use of the wire
  Nodes don’t waste time checking frames not destined to them

## Slide 14: Switch
Switch
Address | Port
AAAAAAAAAAAA | 1
BBBBBBBBBBBB | 5
A
B
Forwarding Table

## Slide 15: Switches and Broadcast
A switch broadcasts some frames:
  When the destination address is not found in the table
  When the frame is destined to the broadcast address (FF:FF:FF:FF:FF:FF)
  When the frame is destined to a multicast ethernet address
So, switches do not reduce the broadcast domain!

## Slide 16: Switch vs. Router
Routers more or less do with IP packets what switches do with Ethernet frames
  A router looks at the IP packet destination and checks its routing table to decide where to forward the packet
Some differences:
  IP packets travel inside ethernet frames
  IP networks can be logically segmented into subnets
  Switches do not usually know about IP, they only deal with Ethernet frames

## Slide 17: Switch vs. Router
Routers do not forward Ethernet broadcasts. So:
  Switches reduce the collision domain
  Routers reduce the broadcast domain
This becomes really important when trying to design hierarchical, scalable networks that can grow sustainably

## Slide 18: Traffic Domains
Router
Switch
Hub
Hub
Switch
Hub
Hub
Broadcast Domain
Collision Domain

## Slide 19: Traffic Domains
Try to eliminate collision domains
  Get rid of hubs!
Try to keep your broadcast domain limited to no more than 250 simultaneously connected hosts
  Segment your network using routers

## Slide 20: Layer 2 Network Design Guidelines
Always connect hierarchically
  If there are multiple switches in a building, use an aggregation switch
  Locate the aggregation switch close to the building entry point (e.g. fiber panel)
  Locate edge switches close to users (e.g. one per floor)
    Max length for Cat 5 is 100 meters

## Slide 21: Minimize Path Between Elements
✔
✗

## Slide 22: Build Incrementally
Start small
Switch
Hosts
Fiber link to distribution switch

## Slide 23: Build Incrementally
As you have demand and money, grow like this:
Aggreg.
Hosts
Switch

## Slide 24: Build Incrementally
And keep growing within the same hierarchy:
Aggreg.
Hosts
Switch
Switch

## Slide 25: Build Incrementally
At this point, you can also add a redundant aggregation switch
Aggreg.
Hosts
Switch
Switch
Aggreg.

## Slide 26: Do not daisy-chain
Resist the temptation of doing this:
✗

## Slide 27: Connect buildings hierarchically
✔

## Slide 28: Virtual LANs (VLANs)
Allow us to split switches into separate (virtual) switches
Only members of a VLAN can see that VLAN’s traffic
  Inter-vlan traffic must go through a router

## Slide 29: Local VLANs
2 VLANs or more within a single switch
Edge ports, where end nodes are connected, are configured as members of a VLAN
The switch behaves as several virtual switches, sending traffic only within VLAN members

## Slide 30: Local VLANs
VLAN X
VLAN Y
Switch
VLAN X nodes
VLAN Y nodes
Edge ports

## Slide 31: VLANs across switches
Two switches can exchange traffic from one or more VLANs
Inter-switch links are configured as trunks, carrying frames from all or a subset of a switch’s VLANs
Each frame carries a tag that identifies which VLAN it belongs to

## Slide 32: 802.1Q
The IEEE standard that defines how ethernet frames should be tagged when moving across switch trunks
This means that switches from different vendors are able to exchange VLAN traffic.

## Slide 33: 802.1Q tagged frame

## Slide 34: VLANs across switches
802.1Q Trunk
Tagged Frames
VLAN X
VLAN Y
VLAN X
VLAN Y
Edge Ports
Trunk Port
This is called “VLAN Trunking”

## Slide 35: Tagged vs. Untagged
Edge ports are not tagged, they are just “members” of a VLAN
You only need to tag frames in switch-to-switch links (trunks), when transporting multiple VLANs
A trunk can transport both tagged and untagged VLANs
  As long as the two switches agree on how to handle those

## Slide 36: VLANS increase complexity
You can no longer “just replace” a switch
  Now you have VLAN configuration to maintain
  Field technicians need more skills
You have to make sure that all the switch-to-switch trunks are carrying all the necessary VLANs
  Need to keep in mind when adding/removing VLANs

## Slide 37: Good reasons to use VLANs
You want to segment your network into multiple subnets, but can’t buy enough switches
  Hide sensitive infrastructure like IP phones, building controls, etc.
Separate control traffic from user traffic
  Restrict who can access your switch management address

## Slide 38: Bad reasons to use VLANs
Because you can, and you feel cool 
Because they will completely secure your hosts (or so you think)
Because they allow you to extend the same IP network over multiple separate buildings

## Slide 39: Do not build “VLAN spaghetti”
Extending a VLAN to multiple buildings across trunk ports
Bad idea because:
  Broadcast traffic is carried across all trunks from one end of the network to another
  Broadcast storm can spread across the extent of the VLAN
  Maintenance and troubleshooting nightmare

## Slide 40: Link Aggregation
Also known as port bundling, link bundling
You can use multiple links in parallel as a single, logical link
  For increased capacity
  For redundancy (fault tolerance)
LACP (Link Aggregation Control Protocol) is a standardized method of negotiating these bundled links between switches

## Slide 41: LACP Operation
Two switches connected via multiple links will send LACPDU packets, identifying themselves and the port capabilities
They will then automatically build the logical aggregated links, and then pass traffic.
Switche ports can be configured as active or passive

## Slide 42: LACP Operation
Switch A
Switch B
LACPDUs
Switches A and B are connected to each other using two sets of Fast Ethernet ports
LACP is enabled and the ports are turned on
Switches start sending LACPDUs, then negotiate how to set up the aggregation
100 Mbps
100 Mbps

## Slide 43: LACP Operation
200 Mbps logical link
The result is an aggregated 200 Mbps logical link
The link is also fault tolerant: If one of the member links fail, LACP will automatically take that link off the bundle, and keep sending traffic over the remaining link
Switch A
Switch B
100 Mbps
100 Mbps

## Slide 44: Distributing Traffic in Bundled Links
Bundled links distribute frames using a hashing algorithm, based on:
  Source and/or Destination MAC address
  Source and/or Destination IP address
  Source and/or Destination Port numbers
This can lead to unbalanced use of the links, depending on the nature of the traffic
Always choose the load-balancing method that provides the most distribution

## Slide 45: Switching Loop
Switch A
Switch B
Swtich C
When there is more than one path between two switches
What are the potential problems?

## Slide 46: Switching Loop
If there is more than one path between two switches:
  Forwarding tables become unstable
    Source MAC addresses are repeatedly seen coming from different ports
  Switches will broadcast each other’s broadcasts
    All available bandwidth is utilized
    Switch processors cannot handle the load

## Slide 47: Switching Loop
Switch A
Switch B
Swtich C
Node1 sends a broadcast frame (e.g. an ARP request)
Node 1

## Slide 48: Switching Loop
Switch A
Switch B
Swtich C
Switches A, B and C broadcast node 1’s frame out every port
Node 1

## Slide 49: Switching Loop
Switch A
Switch B
Swtich C
But they receive each other’s broadcasts, which they need to forward again out every port!
The broadcasts are amplified, creating a broadcast storm
Node 1

## Slide 50: Good Switching Loops
But you can take advantage of loops!
  Redundant paths improve resilience when:
    A switch fails
    Wiring breaks
How to achieve redundancy without creating dangerous traffic loops?

## Slide 51: What is a Spanning Tree
“Given a connected, undirected graph, a spanning tree of that graph is a subgraph which is a tree and connects all the vertices together”.
A single graph can have many different spanning trees.

## Slide 52: Spanning Tree Protocol
The purpose of the protocol is to have bridges dynamically discover a subset of the topology that is loop-free (a tree) and yet has just enough connectivity so that where physically possible, there is a path between every switch

## Slide 53: Spanning Tree Protocol
Several flavors:
  Traditional Spanning Tree (802.1d)
  Rapid Spanning Tree or RSTP (802.1w)
  Multiple Spanning Tree or MSTP (802.1s)

## Slide 54: Traditional Spanning Tree (802.1d)
Switches exchange messages that allow them to compute the Spanning Tree
  These messages are called BPDUs (Bridge Protocol Data Units)
  Two types of BPDUs:
    Configuration
    Topology Change Notification (TCN)

## Slide 55: Traditional Spanning Tree (802.1d)
First Step:
  Decide on a point of reference: the Root Bridge
  The election process is based on the Bridge ID, which is composed of:
    The Bridge Priority: A two-byte value that is configurable
    The MAC address: A unique, hardcoded address that cannot be changed.

## Slide 56: Root Bridge Selection (802.1d)
Each switch starts by sending out BPDUs with a Root Bridge ID equal to its own Bridge ID
  I am the root!
Received BPDUs are analyzed to see if a lower Root Bridge ID is being announced
  If so, each switch replaces the value of the advertised Root Bridge ID with this new lower ID
Eventually, they all agree on who the Root Bridge is

## Slide 57: Root Bridge Selection (802.1d)
Switch B
Switch C
Swtich A
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC
All switches have the same priority.
Who is the elected root bridge?

## Slide 58: Root Port Selection (802.1d)
Now each switch needs to figure out where it is in relation to the Root Bridge
  Each switch needs to determine its Root Port
  The key is to find the port with the lowest Root Path Cost
    The cumulative cost of all the links leading to the Root Bridge

## Slide 59: Root Port Selection (802.1d)
Each link on a switch has a Path Cost
  Inversely proportional to the link speed
    e.g. The faster the link, the lower the cost
Link Speed | STP Cost
10 Mbps | 100
100 Mbps | 19
1 Gbps | 4
10 Gbps | 2

## Slide 60: Root Port Selection (802.1d)
Root Path Cost is the accumulation of a link’s Path Cost and the Path Costs learned from neighboring Switches.
  It answers the question: How much does it cost to reach the Root Bridge through this port?

## Slide 61: Root Port Selection (802.1d)
Root Bridge sends out BPDUs with a Root Path Cost value of 0
Neighbor receives BPDU and adds port’s Path Cost to Root Path Cost received
Neighbor sends out BPDUs with new cumulative value as Root Path Cost
Other neighbor’s down the line keep adding in the same fashion

## Slide 62: Root Port Selection (802.1d)
On each switch, the port where the lowest Root Path Cost was received becomes the Root Port
  This is the port with the best path to the Root Bridge

## Slide 63: Root Port Selection (802.1d)
Switch B
Switch C
Swtich A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC
What is the Path Cost on each Port?
What is the Root Port on each switch?

## Slide 64: Root Port Selection (802.1d)
Switch B
Switch C
Swtich A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC
Root Port
Root Port

## Slide 65: Electing Designated Ports (802.1d)
OK, we now have selected root ports but we haven’t solved the loop problem yet, have we
  The links are still active!
Each network segment needs to have only one switch forwarding traffic to and from that segment
Switches then need to identify one Designated Port per link
  The one with the lowest cumulative Root Path Cost to the Root Bridge

## Slide 66: Electing Designated Ports(802.1d)
Which port should be the Designated Port on each segment?
Switch B
Switch C
Swtich A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC

## Slide 67: Electing Designated Ports (802.1d)
Two or more ports in a segment having identical Root Path Costs is possible, which results in a tie condition
All STP decisions are based on the following sequence of conditions:
  Lowest Root Bridge ID
  Lowest Root Path Cost to Root Bridge
  Lowest Sender Bridge ID
  Lowest Sender Port ID

## Slide 68: Electing Designated Ports(802.1d)
Switch B
Switch C
Swtich A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC
Designated Port
Designated Port
Designated Port
In the B-C link, Switch B has the lowest Bridge ID, so port 2 in Switch B is the Designated Port

## Slide 69: Blocking a port
Any port that is not elected as either a Root Port, nor a Designated Port is put into the Blocking State.
This step effectively breaks the loop and completes the Spanning Tree.

## Slide 70: Designated Ports on each segment (802.1d)
Switch B
Switch C
Swtich A
1
2
1
1
2
2
Cost=19
Cost=19
Cost=19
32678.0000000000AA
32678.0000000000BB
32678.0000000000CC
Port 2 in Switch C is then put into the Blocking State because it is neither a Root Port nor a Designated Port
✕

## Slide 71: Spanning Tree Protocol States
Disabled
  Port is shut down
Blocking
  Not forwarding frames
  Receiving BPDUs
Listening
  Not forwarding frames
  Sending and receiving BPDUs

## Slide 72: Spanning Tree Protocol States
Learning
  Not forwarding frames
  Sending and receiving BPDUs
  Learning new MAC addresses
Forwarding
  Forwarding frames
  Sending and receiving BPDUs
  Learning new MAC addresses

## Slide 73: STP Topology Changes
Switches will recalculate if:
  A new switch is introduced
    It could be the new Root Bridge!
  A switch fails
  A link fails

## Slide 74: Root Bridge Placement
Using default STP parameters might result in an undesired situation
  Traffic will flow in non-optimal ways
  An unstable or slow switch might become the root
You need to plan your assignment of bridge priorities carefully

## Slide 75: Bad Root Bridge Placement
Switch B
Switch C
Swtich D
32678.0000000000DD
32678.0000000000BB
32678.0000000000CC
Switch A
32678.0000000000AA
Root Bridge
Out to router

## Slide 76: Good Root Bridge Placement
Switch B
Switch C
Swtich D
1.0000000000DD
0.0000000000BB
32678.0000000000CC
Switch A
32678.0000000000AA
Alernative Root Bridge
Out to active router
Root Bridge
Out to standby router

## Slide 77: Protecting the STP Topology
Some vendors have included features that protect the STP topology:
  Root Guard
  BPDU Guard
  Loop Guard
  UDLD
  Etc.

## Slide 78: STP Design Guidelines
Enable spanning tree even if you don’t have redundant paths
Always plan and set bridge priorities
  Make the root choice deterministic
  Include an alternative root bridge
If possible, do not accept BPDUs on end user ports
  Apply BPDU Guard or similar where available

## Slide 79: 8021.d Convergence Speeds
Moving from the Blocking state to the Forwarding State takes at least 2 x Forward Delay time units (~ 30 secs.)
  This can be annoying when connecting end user stations
Some vendors have added enhancements such as PortFast, which will reduce this time to a minimum for edge ports
  Never use PortFast or similar in switch-to-switch links
Topology changes tipically take 30 seconds too
  This can be unacceptable in a production network

## Slide 80: Rapid Spanning Tree (802.1w)
Convergence is much faster
  Communication between switches is more interactive
Edge ports don’t participate
  Edge ports transition to forwarding state immediately
  If BPDUs are received on an edge port, it becomes a non-edge port to prevent loops

## Slide 81: Rapid Spanning Tree (802.1w)
Defines these port roles:
  Root Port (same as with 802.1d)
  Alternate Port
    A port with an alternate path to the root
  Designated Port (same as with 802.1d)
  Backup Port
    A backup/redundant path to a segment where another bridge port already connects.

## Slide 82: Rapid Spanning Tree (802.1w)
Synchronization process uses a handshake method
  After a root is elected, the topology is built in cascade, where each switch proposes to be the designated bridge for each point-to-point link
  While this happens, all the downstream switch links are blocking

## Slide 83: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP

## Slide 84: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP

## Slide 85: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP
DP
RP

## Slide 86: Rapid Spanning Tree (802.1w)
Root
Switch
Proposal
Switch
Agreement
Switch
Switch
DP
RP
DP
RP
DP
RP
DP
RP

## Slide 87: Rapid Spanning Tree (802.1w)
Prefer RSTP over STP if you want faster convergence
Always define which ports are edge ports

## Slide 88: Multiple Spanning Tree (802.1s)
Allows separate spanning trees per VLAN group
  Different topologies allow for load balancing between links
  Each group of VLANs are assigned to an “instance” of MST
Compatible with STP and RSTP

## Slide 89: Multiple Spanning Tree (802.1s)
Vlan A
Vlan B
Root VLAN A
Root VLAN B
✕
✕

## Slide 90: Multiple Spanning Tree (802.1s)
MST Region
  Switches are members of a region if they have the same set of attributes:
    MST configuration name
    MST configuration revision
    Instance-to-VLAN mapping
  A digest of these attributes is sent inside the BPDUs for fast comparison by the switches
  One region is usually sufficient

## Slide 91: Multiple Spanning Tree (802.1s)
CST = Common Spanning Tree
  In order to interoperate with other versions of Spanning Tree, MST needs a common tree that contains all the other islands, including other MST regions

## Slide 92: Multiple Spanning Tree (802.1s)
IST = Internal Spanning Tree
  Internal to the Region, that is
  Presents the entire region as a single virtual bridge to the CST outside

## Slide 93: Multiple Spanning Tree (802.1s)
MST Instances
  Groups of VLANs are mapped to particular Spanning Tree instances
  These instances will represent the alternative topologies, or forwarding paths
  You specify a root and alternate root for each instance

## Slide 94: Multiple Spanning Tree (802.1s)
CST
MST Region
IST
MST Region
IST
802.1D switch

## Slide 95: Multiple Spanning Tree (802.1s)
Design Guidelines
  Determine relevant forwarding paths, and distribute your VLANs equally into instances matching these topologies
  Assign different root and alternate root switches to each instance
  Make sure all switches match region attributes
  Do not assign VLANs to instance 0, as this is used by the IST

## Slide 96: Selecting Switches
Minimum features:
  Standards compliance
  Encrypted management (SSH/HTTPS)
  VLAN trunking
  Spanning Tree (RSTP at least)
  SNMP
    At least v2 (v3 has better security)
    Traps

## Slide 97: Selecting Switches
Other recommended features:
  DHCP Snooping
    Prevent end-users from running a rogue DHCP server
      Happens a lot with little wireless routers (Netgear, Linksys, etc) plugged in backwards
    Uplink ports towards the legitimate DHCP server are defined as “trusted”. If DHCPOFFERs are seen coming from any untrusted port, they are dropped.

## Slide 98: Selecting Switches
Other recommended features:
  Dynamic ARP inspection
    A malicious host can perform a man-in-the-middle attack by sending gratuitous ARP responses, or responding to requests with bogus information
    Switches can look inside ARP packets and discard gratuitous and invalid ARP packets.

## Slide 99: Selecting Switches
Other recommended features:
  IGMP Snooping:
    Switches normally flood multicast frames out every port
    Snooping on IGMP traffic, the switch can learn which stations are members of a multicast group, thus forwarding multicast frames only out necessary ports
    Very important when users run Norton Ghost, for example.

## Slide 100: Network Management
Enable SNMP traps and/or syslog
  Collect and process in centralized log server
    Spanning Tree Changes
    Duplex mismatches
    Wiring problems
Monitor configurations
  Use RANCID to report any changes in the switch configuration

## Slide 101: Network Management
Collect forwarding tables with SNMP
  Allows you to find a MAC address in your network quickly
  You can use simple text files + grep, or a web tool with DB backend
Enable LLDP (or CDP or similar)
  Shows how switches are connected to each other and to other network devices

## Slide 102: Documentation
Document where your switches are located
  Name switch after building name
    E.g. building1-sw1
  Keep files with physical location
    Floor, closet number, etc.
Document your edge port connections
  Room number, jack number, server name

## Slide 103: Questions?
Thank you.