## Slide 1: Network Performance Definitions & Analysis
Unix/IP Preparation Course
July 19, 2009
Eugene, Oregon, USA
hervey@nsrc.org

## Slide 2
Network Performance Metrics
Planning performance management
Metrics
  Network
  Systems
  Services
Definitions
Notes: <number>

## Slide 3
Planning
What's the intention?
  Baselining, Troubleshooting, Planning growth
  Defend yourself from accusations -”it's the network!”
Who is the information for?
  Administration, NOC, customers
  How to structure and present the information
Reach: Can I measure everything?
    Impact on devices (measurements and measuring)
    Balance between amount of information and time to get it
Notes: <number>

## Slide 4
Metrics
Network performance metrics
    Channel capacity, nominal & effective
    Channel utilization
    Delay and jitter
    Packet loss and errors
Notes: <number>

## Slide 5
Metrics
What we are not discussing:
System performance metrics
      Availability
      Memory, CPU Utilization, load, I/O wait, etc.
Service performance metrics
Available here and in class outline: http://nsrc.org/workshops/2009/summer/ref/performance-metrics.pdf
Notes: <number>

## Slide 6
Common network performance measurements
Relative to traffic:
  Bits per second
  Packets per second
  Unicast vs. non-unicast packets
  Errors
  Dropped packets
  Flows per second
  Round trip time (RTT)
  Jitter (variation between packet RTT)
Notes: <number>

## Slide 7
Nominal channel capacity
The maximum number of bits that can be transmitted for a unit of time (eg: bits per second)
Depends on:
  Bandwidth of the physical medium
    Cable
    Electromagnetic waves
  Processing capacity for each transmission element
  Efficiency of algorithms in use to access medium
  Channel encoding and compression
Notes: <number>

## Slide 8
Effective channel capacity
Always a fraction of the nominal channel capacity
Dependent on:
  Additional overhead of protocols in each layer
  Device limitations on both ends
    Flow control algorithm efficiency, etc.
      For example: TCP
Notes: <number>

## Slide 9
What fraction of the nominal channel capacity is actually in use
Important!
  Future planning
    What utilization growth rate am I seeing?
    For when should I plan on buying additional capacity?
    Where should I invest for my updates?
  Problem resolution
    Where are my bottlenecks, etc.
Channel utilization
Notes: <number>

## Slide 10
95th Percentile
The smallest value that is larger than 95% of the values in a given sample
This means that 95% of the time the channel utilization is equal to or less than this value
  Or rather, the peaks are discarded from consideration
Why is this important in networks?
  Gives you an idea of the standard, sustained channel utilization.
  ISPs use this measure to bill customers with “larger” connections.
Notes: <number>

## Slide 11
95th Percentile
Notes: <number>

## Slide 12
Bits per second vs Packets p.s.
Notes: <number>

## Slide 13
End-to-end delay
The time required to transmit a packet along its entire path
  Created by an application, handed over to the OS, passed to a network card (NIC), encoded, transmitted over a physical medium (copper, fibre, air), received by an intermediate device (switch, router), analyzed, retransmitted over another medium, etc.
  The most common measurement uses ping for total round-trip-time (RTT).
Notes: <number>

## Slide 14
Historical measurement of delay
Notes: <number>

## Slide 15
Types of Delay
Causes of end-to-end delay
    Processor delays
    Buffer delays
    Transmission delays
    Propagation delays
Notes: <number>

## Slide 16
Processing delay
Required time to analyze a packet header and decide where to send the packet (eg. a routing decision)
  Inside a router this depends on the number of entries in the routing table, the implementation of data structures, hardware in use, etc.
This can include error verification / checksumming (i.e. IPv4, IPv6 header checksum)
Notes: <number>

## Slide 17
Queuing Delay
The time a packet is enqueued until it is transmitted
The number of packets waiting in the queue will depend on traffic intensity and of the type of traffic
Router queue algorithms try to adapt delays to specific preferences, or impose equal delay on all traffic.
Notes: <number>

## Slide 18
Transmission Delay
The time required to push all the bits in a packet on the transmission medium in use
For N=Number of bits, S=Size of packet, d=delay
d = S/N
For example, to transmit 1024 bits using Fast Ethernet (100Mbps) d = 1024/1x10e8 = 10.24 micro seconds
Notes: <number>

## Slide 19
Once a bit is 'pushed' on to the transmission medium, the time required for the bit to propagate to the end of its physical trajectory
The velocity of propagation of the circuit depends mainly on the actual distance of the physical circuit
  In the majority of cases this is close to the speed of light.
For d = distance, s = propagation velocity
PD = d/s
Propagation Delay
Notes: <number>

## Slide 20
Transmission vs. Propagation
Can be confusing at first
Consider this example:
  Two 100 Mbps circuits
    1 km of optic fiber
    Via satellite with a distance of 30 km between the base and the satellite
  For two packets of the same size which will have the larger transmission delay? Propagation delay?
Notes: <number>

## Slide 21
Occur due to the fact that buffers are not infinite in size
  When a packet arrives to a buffer that is full the packet is discarded.
  Packet loss, if it must be corrected, is resolved at higher levels in the network stack (transport or application layers)
  Loss correction using retransmission of packets can cause yet more congestion if some type of (flow) control is not used (to inform the source that it's pointless to keep sending more packets at the present time)
Packet Loss
Notes: <number>

## Slide 22
Jitter
Notes: <number>

## Slide 23
Flow Control and Congestion
Limits the transmission amount (rate) because the receiver cannot process packets at the same rate that packets are arriving.
Limit the amount sent (transmission rate) because of loss or delays in the circuit.
Notes: <number>

## Slide 24
Controls in TCP
IP (Internet Protocol) implements service that not connection oriented.
  There is no mechanism in IP to deal with packet loss.
TCP (Transmission Control Protocol) implements flow and congestion control.
  Only on the ends as the intermediate nodes at the network level do not talk TCP
Notes: <number>

## Slide 25
Congestion vs. Flow in TCP
Flow: controlled by window size (RcvWindow), which is sent by the receiving end.
Congestion: controlled by the value of the congestion window (Congwin)
  Maintained independently by the sender
  This varies based on the detection of packets lost
    Timeout or receiving three ACKs repeated
  Behaviors:
    Additive Increments / Multiplicative Decrements (AIMD)
    Slow Start
    React to timeout events
Notes: <number>

## Slide 26
Different TCP Congestion Control Algorithms
Notes: <number>

## Slide 27: ?

## Slide 28: Local analysis
As we know... Before we blame the network, let's verify whether the problem is ours.
What can go wrong locally?
  Hardware problems
  Excessive load (CPU, memory, I/O)‏
What's considered 'normal'?
  Use analysis tools frequently
    Become familiar with the normal state and values for your machine.
  It is essential to maintain history
    SNMP agents and databases

## Slide 29: Performance analysis in Unix
Three main categories:
  Processes
    Processes that are executing (running)‏
    Processes that are waiting (sleeping)‏
      waiting their turn
      blocked
  Memory
    Real
    Virtual
  I/O (Input/Output)‏
    Storage
    Network

## Slide 30: Key indicators
Insufficent CPU
  Number of processes waiting to execute is always high
  High CPU utilization (load avg.)
Insufficient memory
  Very little free memory
  Lots of swap activity (swap in, swap out)‏
Slow I/O
  Lots of blocked processes
  High number of block transfers

## Slide 31: Local analysis
Luckily, in Unix there are dozens of useful tools that give us lots of useful information about our machine
Some of the more well-known include:
  vmstat - tcpdump
  top - wireshark (ethereal)‏
  lsof - iptraf
  netstat - iperf

## Slide 32: vmstat
Show periodic summary information about processes, memory, pagin, I/O, CPU state, etc
vmstat <-options> <delay> <count>
# vmstat 2
procs -----------memory---------- ---swap-- -----io---- --system-- ----cpu----
r b swpd free buff cache si so bi bo in cs us sy id wa
2 0 209648 25552 571332 2804876 0 0 3 4 3 3 15 11 73 0
2 0 209648 24680 571332 2804900 0 0 0 444 273 79356 16 16 68 0
1 0 209648 25216 571336 2804904 0 0 6 1234 439 46735 16 10 74 0
1 0 209648 25212 571336 2804904 0 0 0 22 159 100282 17 21 62 0
2 0 209648 25196 571348 2804912 0 0 0 500 270 82455 14 18 68 0
1 0 209648 25192 571348 2804912 0 0 0 272 243 77480 16 15 69 0
2 0 209648 25880 571360 2804916 0 0 0 444 255 83619 16 14 69 0
2 0 209648 25872 571360 2804920 0 0 0 178 220 90521 16 18 66 0

## Slide 33: top
Basic performance tool for Unix/Linux environments
Periodically show a list of system performance statistics:
  CPU use
  RAM and SWAP memory usage
  Load average (cpu utilization)
  Information by process

## Slide 34: Load Average
Average number of active processes in the last 1, 5 and 15 minutes
  A simple yet useful measurement
  Depending on the machine the acceptable range considered to be normal can vary:
    Multi-processor machines can handle more active processes per unit of time (than single processor machines)

## Slide 35: top
Information by process (most relevant columns shown):
  PID: Process ID
  USER: user running (owner) of the process
  %CPU: Percentage of CPU utilization by the process since the last sample
  %MEM: Percentage of physical memory (RAM) used by the process
  TIME: Total CPU time used by the process since it was started

## Slide 36: top
Some useful interactive commands
  f : Add or remove columns
  F : Specify which column to order by
  < , > : Move the column on which we order
  u : Specify a specific user
  k : Specify a process to kill (stop)
  d , s : Change the display update interval

## Slide 37: netstat
Show us information about:
  Network connections
  Routing tables
  Interface (NIC) statistics
  Multicast group members

## Slide 38: netstat
Some useful options
-n: Show addresses, ports and userids in numeric form
-r: Routing table
-s: Statistics by protocol
-i: Status of interfaces
-l: Listening sockets
--tcp, --udp: Specify the protocol
-A: Address family [inet | inet6 | unix | etc.]
-p: Show the name of each process for each port
-c: Show output/results continuously

## Slide 39: netstat
Examples:
# netstat -n --tcp -c
Active Internet connections (w/o servers)‏
Proto Recv-Q Send-Q Local Address Foreign Address State
tcp 0 272 ::ffff:192.188.51.40:22 ::ffff:128.223.60.27:60968 ESTABLISHED
tcp 0 0 ::ffff:192.188.51.40:22 ::ffff:128.223.60.27:53219 ESTABLISHED
# netstat -lnp --tcp
Active Internet connections (only servers)‏
Proto Recv-Q Send-Q Local Address Foreign Address State PID/Program name
tcp 0 0 0.0.0.0:199 0.0.0.0:* LISTEN 11645/snmpd
tcp 0 0 0.0.0.0:3306 0.0.0.0:* LISTEN 1997/mysqld
# netstat -ic
Kernel Interface table
Iface MTU Met RX-OK RX-ERR RX-DRP RX-OVR TX-OK TX-ERR TX-DRP TX-OVR Flg
eth0 1500 0 2155901 0 0 0 339116 0 0 0 BMRU
lo 16436 0 18200 0 0 0 18200 0 0 0 LRU
eth0 1500 0 2155905 0 0 0 339117 0 0 0 BMRU
lo 16436 0 18200 0 0 0 18200 0 0 0 LRU
eth0 1500 0 2155907 0 0 0 339120 0 0 0 BMRU
lo 16436 0 18200 0 0 0 18200 0 0 0 LRU
eth0 1500 0 2155910 0 0 0 339122 0 0 0 BMRU
lo 16436 0 18200 0 0 0 18200 0 0 0 LRU
eth0 1500 0 2155913 0 0 0 339124 0 0 0 BMRU

## Slide 40: netstat
Examples:
# netstat –tcp –listening --program
Active Internet connections (only servers)‏
Proto Recv-Q Send-Q Local Address Foreign Address State PID/Program name
tcp 0 0 *:5001 *:* LISTEN 13598/iperf
tcp 0 0 localhost:mysql *:* LISTEN 5586/mysqld
tcp 0 0 *:www *:* LISTEN 7246/apache2
tcp 0 0 t60-2.local:domain *:* LISTEN 5378/named
tcp 0 0 t60-2.local:domain *:* LISTEN 5378/named
tcp 0 0 t60-2.local:domain *:* LISTEN 5378/named
tcp 0 0 localhost:domain *:* LISTEN 5378/named
tcp 0 0 localhost:ipp *:* LISTEN 5522/cupsd
tcp 0 0 localhost:smtp *:* LISTEN 6772/exim4
tcp 0 0 localhost:953 *:* LISTEN 5378/named
tcp 0 0 *:https *:* LISTEN 7246/apache2
tcp6 0 0 [::]:ftp [::]:* LISTEN 7185/proftpd
tcp6 0 0 [::]:domain [::]:* LISTEN 5378/named
tcp6 0 0 [::]:ssh [::]:* LISTEN 5427/sshd
tcp6 0 0 [::]:3000 [::]:* LISTEN 17644/ntop
tcp6 0 0 ip6-localhost:953 [::]:* LISTEN 5378/named
tcp6 0 0 [::]:3005 [::]:* LISTEN 17644/ntop

## Slide 41: netstat
Examples:
$ sudo netstat -atup
Active Internet connections (servers and established) (if run as root PID/Program name is included)
Proto Recv-Q Send-Q Local Address Foreign Address State PID/Program name
tcp 0 0 *:35586 *:* LISTEN 2540/ekpd
tcp 0 0 localhost:mysql *:* LISTEN 2776/mysqld
tcp 0 0 *:www *:* LISTEN 14743/apache2
tcp 0 0 d229-231.uoregon:domain *:* LISTEN 2616/named
tcp 0 0 *:ftp *:* LISTEN 3408/vsftpd
tcp 0 0 localhost:domain *:* LISTEN 2616/named
tcp 0 0 *:ssh *:* LISTEN 2675/sshd
tcp 0 0 localhost:ipp *:* LISTEN 3853/cupsd
tcp 0 0 localhost:smtp *:* LISTEN 3225/exim4
tcp 0 0 localhost:953 *:* LISTEN 2616/named
tcp 0 0 *:https *:* LISTEN 14743/apache2
tcp6 0 0 [::]:domain [::]:* LISTEN 2616/named
tcp6 0 0 [::]:ssh [::]:* LISTEN 2675/sshd
tcp6 0 0 ip6-localhost:953 [::]:* LISTEN 2616/named
udp 0 0 *:50842 *:* 3828/avahi-daemon:
udp 0 0 localhost:snmp *:* 3368/snmpd
udp 0 0 d229-231.uoregon:domain *:* 2616/named
udp 0 0 localhost:domain *:* 2616/named
udp 0 0 *:bootpc *:* 13237/dhclient
udp 0 0 *:mdns *:* 3828/avahi-daemon:
udp 0 0 d229-231.uoregon.ed:ntp *:* 3555/ntpd
udp 0 0 localhost:ntp *:* 3555/ntpd
udp 0 0 *:ntp *:* 3555/ntpd
udp6 0 0 [::]:domain [::]:* 2616/named
udp6 0 0 fe80::213:2ff:fe1f::ntp [::]:* 3555/ntpd
udp6 0 0 ip6-localhost:ntp [::]:* 3555/ntpd
udp6 0 0 [::]:ntp [::]:* 3555/ntpd

## Slide 42: lsof (List Open Files)‏
lsof is particularly useful because in Unix everything is a file: unix sockets, ip sockets, directories, etc.
Allows you to associate open files by:
-p: PID (Process ID)
-i : A network address (protocol:port)
-u: A user

## Slide 43: lsof
Example:
  First, using netstat -ln –tcp determine that port 6010 is open and waiting for a connection (LISTEN)
# netstat -ln --tcp
Active Internet connections (only servers)‏
Proto Recv-Q Send-Q Local Address Foreign Address State
tcp 0 0 127.0.0.1:6010 0.0.0.0:* LISTEN
tcp 0 0 127.0.0.1:6011 0.0.0.0:* LISTEN

## Slide 44: lsof
Determine what process has the port (6010) open and what other resources are being used:
# lsof -i tcp:6010
COMMAND PID USER FD TYPE DEVICE SIZE NODE NAME
sshd 10301 root 6u IPv4 53603 TCP localhost.localdomain:x11-ssh-offset (LISTEN)‏
sshd 10301 root 7u IPv6 53604 TCP [::1]:x11-ssh-offset (LISTEN)‏
# lsof -p 10301
COMMAND PID USER FD TYPE DEVICE SIZE NODE NAME
sshd 10301 root cwd DIR 8,2 4096 2 /
sshd 10301 root rtd DIR 8,2 4096 2 /
sshd 10301 root txt REG 8,2 379720 1422643 /usr/sbin/sshd
sshd 10301 root mem REG 8,2 32724 1437533 /usr/lib/libwrap.so.0.7.6
sshd 10301 root mem REG 8,2 15088 3080329 /lib/libutil-2.4.so
sshd 10301 root mem REG 8,2 75632 1414093 /usr/lib/libz.so.1.2.3
sshd 10301 root mem REG 8,2 96040 3080209 /lib/libnsl-2.4.so
sshd 10301 root mem REG 8,2 100208 1414578 /usr/lib/libgssapi_krb5.so.2.2
sshd 10301 root mem REG 8,2 11684 1414405 /usr/lib/libkrb5support.so.0.0
sshd 10301 root mem REG 8,2 10368 3080358 /lib/libsetrans.so.0
sshd 10301 root mem REG 8,2 7972 3080231 /lib/libcom_err.so.2.1
sshd 10301 root mem REG 8,2 30140 1420233 /usr/lib/libcrack.so.2.8.0
sshd 10301 root mem REG 8,2 11168 3080399 /lib/security/pam_succeed_if.so
...

## Slide 45: lsof
What network services am I running?
# lsof -i
COMMAND PID USER FD TYPE DEVICE SIZE NODE NAME
firefox 4429 hervey 50u IPv4 1875852 TCP 192.168.179.139:56890->128.223.60.21:www (ESTABLISHED)‏
named 5378 bind 20u IPv6 13264 TCP *:domain (LISTEN)‏
named 5378 bind 21u IPv4 13267 TCP localhost:domain (LISTEN)‏
sshd 5427 root 3u IPv6 13302 TCP *:ssh (LISTEN)‏
cupsd 5522 root 3u IPv4 1983466 TCP localhost:ipp (LISTEN)‏
mysqld 5586 mysql 10u IPv4 13548 TCP localhost:mysql (LISTEN)‏
snmpd 6477 snmp 8u IPv4 14633 UDP localhost:snmp
exim4 6772 Debian-exim 3u IPv4 14675 TCP localhost:smtp (LISTEN)‏
ntpd 6859 ntp 16u IPv4 14743 UDP *:ntp
ntpd 6859 ntp 17u IPv6 14744 UDP *:ntp
ntpd 6859 ntp 18u IPv6 14746 UDP [fe80::250:56ff:fec0:8]:ntp
ntpd 6859 ntp 19u IPv6 14747 UDP ip6-localhost:ntp
proftpd 7185 proftpd 1u IPv6 15718 TCP *:ftp (LISTEN)‏
apache2 7246 www-data 3u IPv4 15915 TCP *:www (LISTEN)‏
apache2 7246 www-data 4u IPv4 15917 TCP *:https (LISTEN)‏
...
iperf 13598 root 3u IPv4 1996053 TCP *:5001 (LISTEN)‏
apache2 27088 www-data 3u IPv4 15915 TCP *:www (LISTEN)‏
apache2 27088 www-data 4u IPv4 15917 TCP *:https (LISTEN)‏

## Slide 46: tcpdump
Show received packet headers by a given interface. Optionally filter using boolean expressions.
Allows you to write information to a file for later analysis.
Requires administrator (root) privileges to use since you must configure network interfaces (NICs) to be in “promiscuous” mode.
  Note: promiscuous mode is not very useful when you are connected by a switch.

## Slide 47: tcpdump
Some useful options:
  -i : Specify the interface (ex: -i eth0)‏
  -l : Make stdout line buffered (view as you capture)
  -v, -vv, -vvv: Display more information
  -n : Don't convert addresses to names (avoid DNS)
  -nn : Don't translate port numbers
  -w : Write raw packets to a file
  -r : Read packets from a file created by '-w'

## Slide 48: tcpdump
Boolean expressions
  Using the 'AND', 'OR', 'NOT' operators
  Expressions consist of one, or more, primtives, which consist of a qualifier and an ID (name or number)
    Expression ::= [NOT] <primitive> [ AND | OR | NOT <primitive> ...]
    <primitive> ::= <qualifier> <name|number>
    <qualifier> ::= <type> | <address> | <protocol>
    <type> ::= host | net | port | port range
    <address> ::= src | dst
    <protocol> ::= ether | fddi | tr | wlan | ip | ip6 | arp | rarp | decnet | tcp | udp

## Slide 49: tcpdump
Examples:
  Show all HTTP traffic that originates from 192.168.1.1
        Show all traffic originating from 192.168.1.1 except SSH
# tcpdump -lnXvvv port 80 and src host 192.168.1.1
# tcpdump -lnXvvv src host 192.168.1.1 and not port 22

## Slide 50: wireshark
Wireshark is a graphical packet analyser based on libpcap, the same library that tcpdump utilizes for capturing and storing packets
The graphical interface has some advantages, including:
  Hierarchical visualization by protocol (drill-down)
  Follow a TCP “conversation” (Follow TCP Stream)‏
  Colors to distinguish traffic types
  Lots of statistics, graphs, etc.

## Slide 51: wireshark
Wireshark is what came after Ethereal.
The combination of tcpdump and wireshark can be quite powerful. For example:
  # tcpdump -i eth1 -A -s1500 -2 dump.log port 21
  $ sudo wireshark -r dump.log

## Slide 52: wireshark

## Slide 53: iptraf
Many measurable statistics and functions
  By protocol/port
  By packet size
  Generates logs
  Utilizes DNS to translate addresses
Advantages
  Simplicity
  Menu-based (uses “curses”)
  Flexible configuration

## Slide 54: iptraf
You can run it periodically in the background (-B)
  It allows you, for example, to run as a cron job to periodically analyze logs.
    Generate alarms
    Save in a data base
    Has a great name... “Interactive Colorful IP LAN Monitor”
    etc...
Example: iptraf -i eth1

## Slide 55: iperf
To measure network throughput between two points
iperf has two modes, server and client
Easy to use
Great to help determine optimal TCP parameters
  TCP window size for optimal throughput

## Slide 56: iperf
Using UDP you can generate packet loss and jitter reports
You can run multiple parallel sessions using threads
Supports IPv6

## Slide 57: Iperf parameters
Usage: iperf [-s|-c host] [options]
iperf [-h|--help] [-v|--version]
Client/Server:
-f, --format [kmKM] format to report: Kbits, Mbits, KBytes, MBytes
-i, --interval # seconds between periodic bandwidth reports
-l, --len #[KM] length of buffer to read or write (default 8 KB)‏
-m, --print_mss print TCP maximum segment size (MTU - TCP/IP header)‏
-p, --port # server port to listen on/connect to
-u, --udp use UDP rather than TCP
-w, --window #[KM] TCP window size (socket buffer size)‏
-B, --bind <host> bind to <host>, an interface or multicast address
-C, --compatibility for use with older versions does not sent extra msgs
-M, --mss # set TCP maximum segment size (MTU - 40 bytes)‏
-N, --nodelay set TCP no delay, disabling Nagle's Algorithm
-V, --IPv6Version Set the domain to IPv6
Server specific:
-s, --server run in server mode
-U, --single_udp run in single threaded UDP mode
-D, --daemon run the server as a daemon
Client specific:
-b, --bandwidth #[KM] for UDP, bandwidth to send at in bits/sec
(default 1 Mbit/sec, implies -u)‏
-c, --client <host> run in client mode, connecting to <host>
-d, --dualtest Do a bidirectional test simultaneously
-n, --num #[KM] number of bytes to transmit (instead of -t)‏
-r, --tradeoff Do a bidirectional test individually
-t, --time # time in seconds to transmit for (default 10 secs)‏
-F, --fileinput <name> input the data to be transmitted from a file
-I, --stdin input the data to be transmitted from stdin
-L, --listenport # port to recieve bidirectional tests back on
-P, --parallel # number of parallel client threads to run
-T, --ttl # time-to-live, for multicast (default 1)‏

## Slide 58: iperf - TCP
$ iperf -s
------------------------------------------------------------
Server listening on TCP port 5001
TCP window size: 85.3 KByte (default)‏
------------------------------------------------------------
[ 4] local 128.223.157.19 port 5001 connected with 201.249.107.39 port 39601
[ 4] 0.0-11.9 sec 608 KBytes 419 Kbits/sec
------------------------------------------------------------
# iperf -c nsrc.org
------------------------------------------------------------
Client connecting to nsrc.org, TCP port 5001
TCP window size: 16.0 KByte (default)‏
------------------------------------------------------------
[ 3] local 192.168.1.170 port 39601 connected with 128.223.157.19 port 5001
[ 3] 0.0-10.3 sec 608 KBytes 485 Kbits/sec

## Slide 59: Iperf - UDP
# iperf -c host1 -u -b100M
------------------------------------------------------------
Client connecting to nsdb, UDP port 5001
Sending 1470 byte datagrams
UDP buffer size: 106 KByte (default)‏
------------------------------------------------------------
[ 3] local 128.223.60.27 port 39606 connected with 128.223.250.135 port 5001
[ 3] 0.0-10.0 sec 114 MBytes 95.7 Mbits/sec
[ 3] Sent 81377 datagrams
[ 3] Server Report:
[ 3] 0.0-10.0 sec 114 MBytes 95.7 Mbits/sec 0.184 ms 1/81378 (0.0012%)‏
$ iperf -s -u -i 1
------------------------------------------------------------
Server listening on UDP port 5001
Receiving 1470 byte datagrams
UDP buffer size: 108 KByte (default)‏
------------------------------------------------------------
[ 3] local 128.223.250.135 port 5001 connected with 128.223.60.27 port 39606
[ 3] 0.0- 1.0 sec 11.4 MBytes 95.4 Mbits/sec 0.184 ms 0/ 8112 (0%)‏
[ 3] 1.0- 2.0 sec 11.4 MBytes 95.7 Mbits/sec 0.177 ms 0/ 8141 (0%)‏
[ 3] 2.0- 3.0 sec 11.4 MBytes 95.6 Mbits/sec 0.182 ms 0/ 8133 (0%)‏
...‏
[ 3] 8.0- 9.0 sec 11.4 MBytes 95.7 Mbits/sec 0.177 ms 0/ 8139 (0%)‏
[ 3] 9.0-10.0 sec 11.4 MBytes 95.7 Mbits/sec 0.180 ms 0/ 8137 (0%)‏
[ 3] 0.0-10.0 sec 114 MBytes 95.7 Mbits/sec 0.184 ms 1/81378 (0.0012%)‏

## Slide 60: Bibliography
Monitoring Virtual Memory with vmstat http://www.linuxjournal.com/article/8178
How to use TCPDump http://www.erg.abdn.ac.uk/users/alastair/tcpdump.html
linux command tcpdump example http://smartproteam.com/linux-tutorials/linux-command-tcpdump/
simple usage of tcpdump http://linux.byexamples.com/archives/283/simple-usage-of-tcpdump/
TCPDUMP Command man page with examples http://www.cyberciti.biz/howto/question/man/tcpdump-man-page-with-examples.php
TCPDump Tutorial http://inst.eecs.berkeley.edu/~ee122/fa06/projects/tcpdump-6up.pdf