## Slide 1: Terminal and Console Access
Unix/IP Preparation Course
July 19, 2009
Eugene, Oregon, USA
hervey@nsrc.org

## Slide 2: Contents
Virtual terminals
Mouse daemon buffer (if available)
Copy/paste between terminals
OOB and serial console access
Server/Switch console access (minicom)

## Slide 3: (Virtual) Consoles
Usually you have 6:
  tty[1-6]
tty7 takes you back to X
Access them using ALT-CTRL-F[1-7]
Virtual terminals are very useful. If you run without a GUI, then they are your friend.
Some Unix/Linux versions have optional mouse daemons in text mode (FreeBSD).

## Slide 4: (Virtual) Consoles
Depending on Unix/Linux version these are defined in:
  /etc/default/console-setup (Upstart)
  /etc/inittab
  /etc/ttys
  /boot/grub/menu.1st (OOB trick)
  /etc/init.d/console-setup
  /etc/init.d/console-screen.sh

## Slide 5: Copy/Paste Between Consoles
If you boot without a GUI (no gnome, KDE, etc.) and you have a mouse-daemon, the for example you can:
  Highlight text in tty1
  Press ALT-CTRL-2 to access tty2
  Place mouse in another file
  Press middle-mouse button to paste text from tty1

## Slide 6: OOB and Serial Console Access
OOB or “Out Of Band” access:
Critical for remote management of servers.
How do you access a machine's BIOS remotely?
How do you access RAID BIOS remotely?
In Linux tell the boot loader to pass options to the kernel. The kernel can send output to ttyS0.
Why is this useful?...

## Slide 7: OOB and Serial Console Access
Use serial to ethernet converter.
With an OOB solution connect to separate IP to view your machine's console.
During boot you can see your machine's console using terminal software connecting to a separate IP (user and password almost always required as well).
Set Kernel load options (for instance) in /boot/grup/menu.1st

## Slide 8: OOB and Serial Console Access
Sample /boot/grub/menu.1st file entry: title Ubuntu 8.04.2, kernel 2.6.24-23-server root (hd0,0) kernel /vmlinuz-2.6.24-23-server root=UUID=96e73009-3bf7-421e -a4bc-6de1d21eaa97 ro console=ttyS0,38400n8 console=tty0 quiet splash initrd /initrd.img-2.6.24-23-server quiet
What does this mean?
Key option for OOB serial console access is:
console=ttyS0,38400n8 console=tty0
We'll look at an example now...

## Slide 9: Server/Switch Console Access
Connect serial cable from your machine to serial/aux port on switch or router.
Default settings in most cases are:
  9600 bps, 8 bits, no parity, 1 stop bit
  Or, 9600 8n1
  Be sure that Hardware Flow Control is off (No). Your data cable probably does not have the lines for hardware flow control.
  Your serial port is probably ttyS0.

## Slide 10: Console Access using Minicom
To configure 9600bps, 8-n-1, no hardware flow control and use ttyS0 in Minicom do:
  sudo minicom
  CTRL-a, z. Choose “cOnfigure Minicom”
  Choose “Serial port setup”
    Set Serial Device to /dev/ttyS0
    Set Hardware Flow Control to “No”
  Exit, then press CTRL-a, z. Choose “comm Parameters”
    Set Speed to 9600
  Exit. Exit Minicom (CTRL-a, x) and restart.

## Slide 11: Console Access using Minicom
When you start your device, if you need to send a BREAK do:
CTRL-a, f
Note, to ensure access to your serial port(s) you must run Minicom using sudo or as root.