## Slide 1: Cisco Configuration
These materials are licensed under the Creative Commons Attribution-NonCommercial 4.0 International license
(http://creativecommons.org/licenses/by-nc/4.0/)
Network Startup Resource Center
www.ws.nsrc.org

## Slide 2: Topics
CLI modes
Accessing the configuration
Basic configuration (hostname and DNS)
Authentication and authorization (AAA)
Log collection
Time Synchronization (date/timezone)
SNMP configuration
Cisco Discovery Protocol (CDP)
NetFlow flows (version 5 and 9)
Notes: For the presenter – PLEASE DO NOT GO THROUGH EVERY EXAMPLE!. That is, the class is going to do all of this during the week. You do not need to read each command and explain, rather please give more of an overview and explain that the class will be doing each of these exercises with more in-depth explanation during the week.

## Slide 3: CLI Modes
User EXEC
  Limited access to the router
  Can show some information but cannot view nor change configuration
  bdr1.campusY>
Privileged EXEC
  Full view of the router’s status, troubleshooting, manipulate config, etc.
  bdr1.campusY> enable
  bdr1.campusY#

## Slide 4: Accessing the router (first time)
Before setting up SSH
  telnet to a Cisco network device
  login “cisco” and “cisco” (user and password) (We use different <USER> and <PASS> in class)
Privileged user can go to privileged mode:
  bdr1.campusY> enable (enter <PASS> default is
  “cisco”)
  bdr1.campusY# configure terminal
  bdr1.campusY(config)#
Notes: You might note the prompt name and tie it in to the classroom architecture.

## Slide 5: Accessing the router (first time)
Now that you are in “config” mode you can adjust router settings. When done:
Exit and save the new configuration
  bdr1.campusY(config)# end
  bdr1.campusY# write memory
If you don’t “wr mem” (write memory) changes are lost if router reboots.
We have added a space between “#” and commands for clarity. On the router there is no space.

## Slide 6: Accessing the configuration
There are two configurations:
  Running config is the actual configuration that is active on the router and stored in RAM (will be gone if router is rebooted):
    rtr# configure terminal (conf t)
    rtr(config)# end
    rtr# show running-config (show run)
  Startup config
    Stored in NVRAM (Non-Volatile RAM):
    rtr# copy running-config startup-config (or)
    rtr# write memory (wr mem)
    rtr# show startup-config (sh start)
*For simplicity we use “rtr” for the remainder of this presentation vs. “bdr1.campus”
Notes: Note, to simplify our command line for this presentation we are using “rtr” vs the example of “bdr1.campusY” on the previous slide

## Slide 7: Basic configuration (hostname and DNS)
  Assign a name
    rtr(config)# hostname bdr1.campusY
    or (for example) rtr(config)# hostname core1.campusY
  Assign a domain
    rtr(config)# ip domain-name ws.nsrc.org
  Assign a DNS server
    rtr(config)# ip name-server 100.68.100.254
  Or, disable DNS resolution
    rtr(config)# no ip domain-lookup if no dns this is very useful to avoid long waits

## Slide 8: Authentication & authorization
Configuring passwords:
  Passwords stored as a hash
    Example:
    rtr# enable secret 0 cisco
    rtr# user admin secret 0 cisco
In class we use different user names and passwords.

## Slide 9: Authentication & authorization
Configuring SSH with a 2048 bit key (at least 768 for OpenSSH clients)
  rtr(config)# aaa new-model
  rtr(config)# crypto key generate rsa (key size prompt)
Verify key creation:
  rtr# show crypto key mypubkey rsa
Optionally register events. Restrict to only use SSH version 2 :
  rtr(config)# ip ssh logging events
  rtr(config)# ip ssh version 2
Use SSH, disable telnet (only use telnet if no other option):
rtr(config)# line vty 0 4
rtr(config)# transport input ssh
Notes: Heads up! If you do # sh ip ssh Cisco felt the need to make their versions not match what we’d expect. show ip ssh will return:
1.5 for version 1 only
2.0 for version 2 only
1.99 for both version 1 and 2.
Thank you Patrick Okui.

## Slide 10: Log collection (syslog*)
Send logs to the syslog server:
  rtr(config)# logging 100.68.Y.130. (example)
Identify what channel will be used (local0 to local7):
rtr(config)# logging facility local5
Up to what priority level do you wish to record?
rtr(config)# logging trap <logging_level>
<0-7> Logging severity level
emergencies System is unusable (severity=0)
alerts Immediate action needed (severity=1)
critical Critical conditions (severity=2)
errors Error conditions (severity=3)
warnings Warning conditions (severity=4)
notifications Normal but significant conditions (severity=5)
informational Informational messages (severity=6)
debugging Debugging messages (severity=7)
*syslog, syslog-ng, rsyslog

## Slide 11: Time synchronization
It is essential that all devices in our network are time-synchronized
In config mode:
rtr(config)# ntp server pool.ntp.org rtr(config)# clock timezone <timezone>
To use UTC time:
rtr(config)# no clock timezone
If your site observes daylight savings time you can do:
rtr(config)# clock summer-time recurring last Sun Mar 2:00 last Sun Oct 3:00
Verify:
rtr# show clock
22:30:27.598 UTC Tue Feb 15 2011
rtr# show ntp status
        Clock is synchronized, stratum 3, reference is 4.79.132.217
        nominal freq is 250.0000 Hz, actual freq is 249.9999 Hz, precision is 2**18
        reference time is D002CE85.D35E87B9 (11:21:09.825 CMT Tue Aug 3 2010)
        clock offset is 2.5939 msec, root delay is 109.73 msec…

## Slide 12: SNMP configuration
Start with SNMP version 2
  It’s easier to configure and understand
  Example:
rtr(config)# snmp-server community NetManage ro 99
rtr(config)# access-list 99 permit 100.68.Y.128 0.0.0.15
rtr(config)# access-list 99 permit 100.68.100.0 0.0.0.255
Note the Cisco subnet mask inversion:
0.0.0.255 == 255.255.255.0 == /24 (254 hosts)
0.0.0.15 == 255.255.255.240 == /28 (14 hosts)

## Slide 13: SNMP configuration
From a Linux machine (once snmp utils are installed), you might try:
snmpwalk –v2c –c NetManage bdrX.campusY.ws.nsrc.org sysDescr

## Slide 14: Cisco Discovery Protocol (CDP)
Enabled by default in most modern routers
If it’s not enabled:
  rtr(config)# cdp run
  rtr(config-if)# cdp enable (per-interface)
To see existing neighbors:
  rtr# show cdp neighbors
Tools to visualize/view CDP announcements:
  tcpdump
  cdpr
  wireshark
  tshark

## Slide 15: Enabling NetFlow flows version 5
Configure version 5 NetFlow flows on FastEthernet interface 0/0 and export them to 100.68.Y.130 on port 9996:
  rtr# configure terminal
  rtr(config)# interface FastEthernet 0/0
  rtr(config-if)# ip flow ingress
  rtr(config-if)# ip flow egress
  rtr(config-if)# exit
  rtr(config-if)# ip flow-export destination 100.68.Y.130 9996
  rtr(config-if)# ip flow-export version 5
  rtr(config-if)# ip flow-cache timeout active 5
This breaks up long-lived flows into 5-minute fragments. You can choose any number of minutes between 1 and 60. If you leave it at the default of 30 minutes your traffic reports will have spikes.
Note: Newer version of Cisco IOS have changed this syntax.

## Slide 16: Enabling top-talkers NetFlow (version 5)
  rtr(config)# snmp-server ifindex persist
Ensures that the ifIndex values are retained over router reboots or if you add/remove interface modules.
Now configure how you want the ip flow top-talkers to work:
rtr(config)# ip flow-top-talkers
rtr(config-flow-top-talkers)# top 20
rtr(config-flow-top-talkers)# sort-by bytes
rtr(config-flow-top-talkers)# end
Verify what we've done
rtr# show ip flow export
rtr# show ip cache flow
See your "top talkers" across your router interfaces:
rtr# show ip flow top-talkers

## Slide 17: Enabling NetFlow IPv4 flows (version 9)
Configure version 9 NetFlow flows for IPv4 on FastEthernet interface 0/0 and export them to 100.68.Y.130 on port 9996:
  rtr# configure terminal
  rtr(config)# flow exporter EXPORTER-1
  rtr(config-flow-exporter)# description Export to DB Server CampusY
  rtr(config-flow-exporter)# destination 100.68.Y.130
  rtr(config-flow-exporter)# transport udp 9996
  rtr(config-flow-exporter)# template data timeout 300
  rtr(config-flow-exporter)# flow monitor FLOW-MONITOR-V4
  rtr(config-flow-monitor)# exporter EXPORTER-1
  rtr(config-flow-monitor)# record netflow ipv4 original-input
  rtr(config-flow-monitor)# cache timeout active 300
  rtr(config)# snmp-server ifindex persist
  rtr(config)# interface FastEthernet 0/0
  rtr(config-if)# ip flow monitor FLOW-MONITOR-V4 input
  rtr(config-if)# ip flow monitor FLOW-MONITOR-V4 output
  rtr(config-if)# exit
  rtr# write memory

## Slide 18: Enabling NetFlow IPv6 flows (version 9)
Configure version 9 NetFlow flows for IPv6:
To monitor IPv6 flows you would have to create a new flow monitor for IPv6 and attach it to the interface and the existing exporters.
  rtr(config-flow-exporter)# flow monitor FLOW-MONITOR-V6
  rtr(config-flow-monitor)# exporter EXPORTER-1
  rtr(config-flow-monitor)# record netflow ipv6 original-input
  rtr(config-flow-monitor)# cache timeout active 300
  rtr(config)# interface FastEthernet 0/0
  rtr(config-if)# ipv6 flow monitor FLOW-MONITOR-V6 input
  rtr(config-if)# ipv6 flow monitor FLOW-MONITOR-V6 output
  rtr(config-if)# exit
  rtr# write memory

## Slide 19: Viewing NetFlow flows (version 9)
These are not configuration directives, just a few samples of viewing flow information directly on your router.
To view your current configuration:
  rtr# show flow exporter EXPORTER-1
  rtr# show flow monitor FLOW-MONITOR-V4
It’s possible to see active individual flows on the device:
  rtr# show flow monitor FLOW-MONITOR-V4 cache
Will display too many flows. Press ‘q’ to exit display. Group flows so you can see your “Top Talkers” by traffic destinations and sources. This is one long command:
  rtr# show flow monitor FLOW-MONITOR-V4 cache aggregate ipv4 \
  source address ipv4 destination address sort counter \
  bytes top 20

## Slide 20: Questions?
?
For more information, check out
http://www.cisco.com/en/US/docs/ios/12_2/configfun/configuration/guide/ffun_c.html