## Slide 1: Network Documentation
Network Monitoring and Management

## Slide 2: Documentation
Maybe you’ve asked, “How do you keep track of it all?”...
Document, document, document…

## Slide 3: Updated Documentation is essential
So that you can remember what you did 6 months ago
So that others in your team can troubleshoot problems quickly
Think about these questions:
  What would happen to the network if the main engineer moves to another job?
  How would your team deal with problems if you were sick? Or on vacation?

## Slide 4: Documenting is hard
It’s tedious
  “I’m so busy, I don’t have time right now”
It’s difficult to keep organized
  You need to have an established methodology that everyone can follow
  Otherwise it becomes crazy with time
It becomes outdated very quickly
  Old information is useless and can be even dangerous!

## Slide 5: Guidelines
Create a documentation policy
  What’s the responsibility of each person?
  What is the process? Order of tasks?
  How to verify completeness/quality?
  Methodologies
    Consistent naming schemes
      For devices, cabling, etc.

## Slide 6: Guidelines
Label EVERYTHING
  Devices: routers, switches, servers, access points, etc.
  Cabling
  Network jacks
  Racks

## Slide 7: Documentation
Basics, such as documenting your switches...
  What is each port connected to?
  Can be simple text file with one line for every port in a switch:
    health-switch1, port 1, Room 29 – Director’s office
    health-switch1, port 2, Room 43 – Receptionist
    health-switch1, port 3, Room 100 – Classroom
    health-switch1, port 4, Room 105 – Professors Office
    …..
    health-switch1, port 25, uplink to health-backbone
  This information might be available to your network staff, help desk staff, via a wiki, software interface, etc.
  Remember to label your ports!

## Slide 8: Documentation: Labeling
Nice…

## Slide 9: Network Documentation
More automation might be needed. An automated network documentation system is something to consider.
  You can write local scripts to do this.
  You can consider some automated documentation systems.
  You’ll probably end up doing both.

## Slide 10: NOCs: Network Operation Centers
Where documentation, monitoring and management can all come together:
  Links to monitoring tools
  Ticketing systems
  Documentation systems
    Diagrams
    Databases
    Wikis

## Slide 11: The Network Operations Center
NOC = Network Operations Center
  Come in many forms and depend on the size of your organization and your goals.
  “One or more locations from which control is exercised over your network.”
  NOCs can be:
    Virtual
    Located at the core of your network
    With your help desk
    Built in pieces
    Etc.

## Slide 12: A BIG NOC
There are even bigger NOCs out there…

## Slide 13: A small NOC
In the same room there is a desk with a phone, another computer and a monitor. This acted as the group’s Help Desk.
Many network problems could be detected and solved on the spot!

## Slide 14: Automated Documentation Systems
There are quite a few automated network documentation systems. Each tends to do something different:
  Netdot: https://github.com/cvicente/Netdot/
  NetBox: https://netbox.readthedocs.io/ https://github.com/digitalocean/netbox
  Netdisco: http://netdisco.org/
  Rack Tables: http://www.racktables.org/

## Slide 15: NetBox
From the web page:
IP address management (IPAM) - IP networks and addresses, VRFs, and VLANs
Equipment racks - Organized by group and site
Devices - Types of devices and where they are installed
Connections - Network, console, and power connections among devices
Virtualization - Virtual machines and clusters
Data circuits - Long-haul communications circuits and providers
Secrets - Encrypted storage of sensitive credentials

## Slide 16: Netdisco
  Netdisco 2
  Locate a machine on the network by MAC or IP and show the switch port it lives at.
  Turn off a switch port, or change the VLAN or PoE status of a port. Leave on audit trail. Log why a port was shut down.
  Inventory your network hardware by model, vendor, switch-card, firmware, operating system, software, etc.
  Report IP address & switch port usage: historical & current.
  Pretty pictures of your network.

## Slide 17: Netdisco
Demo available at https://netdisco2-demo.herokuapp.com/

## Slide 18: 1
Web site: http://racktables.org/
“Racktables is a nifty and robust solution for datacenter and server room asset management. It helps document hardware assets, network addresses, space in racks, networks configuration and much much more!”
Demo available at:
http://demo.racktables.org/

## Slide 20
It’s a very comprehensive tool:
  Device discovery via SNMP
  Layer2 topology discovery and graphing, using:
    CDP/LLDP
    Spanning Tree Protocol
    Switch forwarding tables
    Router point-to-point subnets
  IPv4 and IPv6 address space management (IPAM)
    Address space visualization
    DNS/DHCP config management
    IP and MAC address tracking
Continued 

## Slide 21: Netdot:
Functionality continued:
  Cable plant (sites, fiber, copper, closets, circuits...)
  Contacts (departments, providers, vendors, etc.)
  Export scripts for various tools (Nagios, Sysmon, RANCID, Cacti, etc)
    I.E., how we could automate node creation in Cacti!
  Multi-level user access: Admin, Operator, User
  It draws pretty pictures of your network

## Slide 22: Netdot: NETwork DOcumentation Tool

## Slide 23: Netdot Topology example
Netdot can draw the
topology of a network or
a segment of a network
dynamically.

## Slide 24: Documentation: Diagrams

## Slide 25: Diagramming Software
WINDOWS
    Visio: http://office.microsoft.com/en-us/visio/
    Edraw: http://www.edrawsoft.com/
MACINTOSH
    Omnigraffle: https://www.omnigroup.com/omnigraffle
    EazyDraw: https://www.eazydraw.com/
OPEN SOURCE
    LibreOffice Draw
    Pencil: http://pencil.evolus.vn/
    Dia: http://live.gnome.org/Dia

## Slide 26: Diagramming Software
WEB BASED
    Lucidchart: https://www.lucidchart.com/
    Google: Google Docs drawings
    Gliffy: https://www.gliffy.com/
ICONS
  Cisco icons: https://www.cisco.com/c/en/us/about/brand-center/network-topology-icons.html
  For LibreOffice: http://www.vrt.com.au/downloads/vrt-network-equipment
  Nagios Exchange: http://www.nagiosexchange.org/

## Slide 27: Netdot Demo
Assuming there is time we will now give a short demonstration of Netdot
Netdot can be found at: https://github.com/cvicente/Netdot/

## Slide 28: Questions
?