## Slide 1: All in one network graphing and monitoring
This document is a result of work by the Network Startup Resource Center (NSRC at http://www.nsrc.org). This document may be freely copied, modified, and otherwise re-used on the condition that any re-use acknowledge the NSRC as the original source.

## Slide 2: LibreNMS
SNMP-based auto-discover network monitoring
Derived from another project (Observium)
Written in PHP as a web application
Includes support for a wide range of hardware:
  Cisco, Linux, FreeBSD, Juniper, Brocade, Foundry, HP and many more
    See http://docs.librenms.org/Support/Features/
  Over 100 supported!
  Routers, Switches, Access Points, Security gateways, Hosts, Printers, …

## Slide 3: Available metrics
CPU, memory and storage statistics
Interface traffic, packet and detailed error statistics (L2 and L3)
Temperature, fan speed, voltage, amperage, power humidity and frequency sensors
Users, processes, load average and uptime statistics

## Slide 4: Available metrics cont.
Linux distribution detection
Real-time interface traffic graphing
Device inventory collection (useful!)
Detailed IPv4, IPv6, TCP and UDP stack statistics
BGP and OSPF information
MAC <-> IP address lookup
  Find which port an IP/MAC was last seen on

## Slide 5: Features
Dashboard
Status Map
Many extensions, including:
  Host monitoring well supported using check_mk and support scripts
  Billing module
Integration with other tools:
  Smokeping, collectd, syslog (receive logs from devices)/graylog, Rancid/Oxidized (config management)

## Slide 6: Philosophy
LibreNMS’ approach is that the network monitoring shouldn’t take long to set up
  You’ve already worked hard to build your network and configure it
  LibreNMS is easier to understand if you understand its philosophy

## Slide 7: Philosophy (2)
Configure equipment correctly…
  community
  xDP (CDP or LLDP)
  sysName
  sysLocation (geo mapping)
... and LibreNMS will do the rest
  Auto discovery of devices and resources
  Optional use of sysServices to map which services (ports) are running on a device

## Slide 8: Philosophy (3)
Concept of enabled vs. ignored
  By default, LibreNMS will monitor (collect data) all ports/interfaces it finds.
  If a port is configured to be up, but it’s operationnally up, LibreNMS will complain about
  You can tell LibreNMS to ignore these ports – or better, shut them down if they’re not used
  When they’re used, bring them up

## Slide 9: SNMP or nothing
Be aware that for LibreNMS to function, SNMP must be enabled
LibreNMS makes use of CDP/LLDP/OSPF information to detect neighbors and automatically scan for neighboring devices and add them to the monitoring
  … but this information is fetched using SNMP!
  If SNMP isn’t enabled or available (or wrongly configured), LibreNMS won’t function.

## Slide 10: Availability
LibreNMS
Fork of Observium. Open Source, Free and GPL
https://github.com/librenms/librenms History
https://github.com/librenms/librenms/blob/master/doc/General/Welcome-to-Observium-users.md Documentation
http://docs.librenms.org/

## Slide 11: Screenshots
These are from LibreNMS. This is the version we will use in class and in our labs.

## Slide 17: Online LibreNMS demo
Is available at:
  https://demo.librenms.org/
  Log on as demo / demo
Workshop installation at:
  http://librenms.ws.nsrc.org/
  Log on as admin / <CLASS PASSWORD>

## Slide 18: Questions/Discussion?
This document is a result of work by the Network Startup Resource Center (NSRC at http://www.nsrc.org). This document may be freely copied, modified, and otherwise re-used on the condition that any re-use acknowledge the NSRC as the original source.