## Slide 1: Network Monitoring and Management Log Management
These materials are licensed under the Creative Commons Attribution-NonCommercial 4.0 International license
(http://creativecommons.org/licenses/by-nc/4.0/)
Network Startup Resource Center
www.ws.nsrc.org

## Slide 2: Log Management & Monitoring
Keep your logs in a secure place
Where they can be easily inspected
Watch your log file
They contain important information
  Many things happen
  Someone needs to review them
  It’s not practical to do this manually

## Slide 3: Log Management & Monitoring
On your routers and switches
And, on your servers

## Slide 4: Log Management
Centralize and consolidate log files
Send all log messages from your routers, switches and servers to a single node – a log server.
All network hardware and UNIX/Linux servers can be monitored using some version of syslog (we use either syslog-ng or rsyslog for this workshop).
Windows can, also, use syslog with extra tools.
Save a copy of the logs locally, but, also, save them to a central log server.
Notes: 10/28/10
4
04/26/10
4

## Slide 5: Syslog Basics
Uses UDP protocol, port 514
Syslog messages have two attributes (in addition to the message itself):
Facility Level Auth Security | Emergency (0) Authpriv User | Alert (1) Console Syslog | Critical (2) Cron UUCP | Error (3) Daemon Mail | Warning (4) Ftp Ntp | Notice (5) Kern News | Info (6) Lpr | Debug (7) Local0 ...Local7 |
In addition there is a concept of ”Priority” which is a result of the combination of the facility and the level. See http://en.wikipedia.org/wiki/Syslog#Priority.
Notes: 10/28/10
5
04/26/10
5

## Slide 6: Centralized Logging

## Slide 7: Configuring Centralized Logging
  Cisco hardware
    At a minimum:
    logging ip.of.logging.host
  Unix and Linux nodes
    In syslogd.conf, or in rsyslog.conf, add:
  *.* @ip.of.log.host
    Restart syslogd, rsyslog or syslog-ng
  Other equipment have similar options
    Options to control facility and level

## Slide 8: Receiving Messages – syslog-ng
Identify the facility that the equipment is going to use to send its messages.
Reconfigure syslog-ng to listen to the network*
  In Ubuntu update /etc/syslog-ng/syslog-ng.conf
Create the following file* /etc/syslog-ng/conf.d/10-network.conf
Create a new directory for logs:
# mkdir -p /var/log/network
Restart the syslog-ng service: # systemctl restart syslog-ng *See logging exercises for details
Notes: 10/28/10
8
04/26/10
8

## Slide 9: If Using rsyslog
rsyslog is included by default in Ubuntu (but we prefer syslog-ng). It’s a slightly different configuration – we have labs for this as well:
Update /etc/rsyslog
Create the following file
    /etc/rsyslog.d/30-routerlogs.conf
Create a new directory for logs and update permissions on the directory
    # mkdir /var/log/network
    # chown syslog:adm /var/log/network
Restart the rsyslog service
    # systemctl restart rsyslog
Notes: 10/28/10
9
04/26/10
9

## Slide 10: Grouping Logs
Using facility and level you can group by category in distinct files.
With software such as rsyslog you can group by machine, date, etc. automatically in different directories.
You can use grep to review logs.
You can use typical UNIX tools to group and eliminate items that you wish to filter:
  egrep -v '(list 100 denied|logging rate-limited)' mylogfile
Is there a way to do this automatically?
Notes: 10/28/10
10
04/26/10
10

## Slide 11: Tenshi
Simple and flexible log monitoring tool https://inversepath.com/tenshi.html
Messages are classified into queues, using regular expressions
Each queue can be configured to send a summary e-mail within a time period
  E.G. You can tell Tenshi to send you a summary of all matching messages every 5 minutes to avoid cluttering your mailbox
Notes: 10/28/10
11
04/26/10
11

## Slide 12: Sample Tenshi Configruation
set uid tenshi
set gid tenshi
set logfile /log/dhcp
set sleep 5
set limit 800
set pager_limit 2
set mailserver localhost
set subject tenshi report
set hidepid on
set queue dhcpd tenshi@localhost sysadm@hostX.campusY.ws.nsrc.org [*/10 * * * *]
group ^dhcpd:
dhcpd ^dhcpd: .+no free leases
dhcpd ^dhcpd: .+wrong network
group_end
Notes: 10/28/10
12
04/26/10
12

## Slide 13: To Learn More About Syslog
RFC 3164: BSD Syslog Protocol http://tools.ietf.org/html/rfc3164
RFC 5426: Transmission of Syslog Messages over UDP http://tools.ietf.org/html/rfc5426
Transmission of syslog messages over UDP draft-ietf-syslog-transport-udp-00 http://tools.ietf.org/html/draft-ietf-syslog-transport-udp-00
Wikipedia Syslog Entry http://tools.ietf.org/html/rfc3164
Cisco Press: An Overview of the Syslog Protocol http://www.ciscopress.com/articles/article.asp?p=426638
Notes: 10/28/10
13
04/26/10
13

## Slide 14: References & links
Rsyslog
http://www.rsyslog.com/
SyslogNG
http://www.balabit.com/network-security/syslog-ng/
Windows Log to Syslog
http://code.google.com/p/eventlog-to-syslog/
http://www.intersectalliance.com/projects/index.html
Tenshi
http://www.inversepath.com/tenshi.html
Other software
http://sourceforge.net/projects/swatch/
http://www.crypt.gen.nz/logsurfer
http://simple-evcorr.sourceforge.net/
Notes: 10/28/10
14

## Slide 15: Questions?
Notes: 10/28/10
15
04/26/10
15