## Slide 1
Network Delay
Network Management &
Monitoring
Notes: 10/25/10
1

## Slide 2
The time required to transmit a packet along its entire path
  Created by an application, handed over to the OS, passed to a network card (NIC), encoded, transmitted over a physical medium (copper, fibre, air), received by an intermediate device (switch, router), analyzed, retransmitted over another medium, etc.
  The most common measurement uses ping for total round-trip-time (RTT).
End-to-end Delay
Notes: 10/25/10
2
2
2

## Slide 3
Historical Measurement of RTT
What is this telling us?
We need to understand the sources of delay
Notes: 10/25/10
3
3
3

## Slide 4
    Processing delays
    Queuing delays
    Transmission delays
    Propagation delays
Causes of Delay
Notes: 10/25/10
4
4
4

## Slide 5
Time required by intermediate routers to decide where to forward the packet, update TTL, perform header checksum calculations
(Note: most modern routers handle packet forwarding in hardware at full line rate)
plus:
Time for the far end to process the ICMP echo request and generate a response
1. Processing Delay
Notes: 10/25/10
5
5
5

## Slide 6
Queuing Delay
The time a packet is enqueued while the link is busy sending other packets
This is a statistical function and depends on the arrival times of other packets
QoS configurations may prioritize some types of traffic over others
(In practice, that means multiple queues, and different packets are assigned to different queues)
2. Queuing Delay
Notes: 10/25/10
6
6
6

## Slide 7
Transmission Delay
The time required to push all the bits in a packet on the transmission medium in use
For N=Number of bits in packet, R=transmission rate (bits per second)
t = N/R
For example, to transmit 1500 bytes (12000 bits) using Fast Ethernet (100Mbps):
t = 12000/1x108 = 0.12 milliseconds
3. Transmission Delay
Notes: 10/25/10
7
7
7

## Slide 8
Once a bit is 'pushed' on to the transmission medium, the time required for the bit to propagate to the other end of its physical path
For a given medium, the velocity of propagation is usually constant (some fraction of the speed of light)
The longer the path, the longer the delay
For x = distance, v = propagation velocity
t = x/v
4. Propagation Delay
Notes: 10/25/10
8
8
8

## Slide 9
Can be confusing at first
Consider this example:
  Two 100 Mbps circuits
  1 km of optic fiber
  Via satellite with a distance of 35,000 km between the base and the satellite
For two packets of the same size which will have the larger transmission delay? Propagation delay?
Transmission vs. Propagation
Notes: 10/25/10
9
9
9

## Slide 10
Jitter
Notes: 10/25/10
10
10
10

## Slide 11
Queuing Delay
We've seen four causes of delay. Which are constant for a given path and packet size, and which are variable?
What applications are particularly sensitive to jitter?
Those applications may apply extra buffering to smooth out jitter – why is that additional delay a problem?
Questions about Jitter
Notes: 10/25/10
11
11
11

## Slide 12
Questions?
?
Notes: 10/25/10
12
12

## Slide 13
Causes of packet loss:
    Transmission errors
    Queue overflow (congestion)
Packet Loss
Notes: 10/25/10
13
13
13

## Slide 14
"1" received as "0", or vice versa
  e.g. due to excess noise, poor connections, ...
Can be measured in terms of "bit error rate" (BER)
If one or more bits in a packet is corrupted, the whole packet is discarded
Retransmission of lost packets is the responsibility of higher layers (transport or application)
1. Transmission errors
Notes: 10/25/10
14
14
14

## Slide 15
Queues do not have infinite size
If a packet arrives when queue already full, it is dropped
Ultimately caused by insufficient capacity
However, packet loss starts to occur before the link is 100% utilized, because of random distribution of arrival times
Retransmissions cause further demand and could lead to network collapse!
2. Queue overflow
Notes: 10/25/10
15
15
15

## Slide 16
Flow Control and Congestion
TCP limits sending rate by means of a "congestion window"
The congestion window starts small, and increases gradually while there is no packet loss
Any detected packet loss causes the congestion window to shrink rapidly, so the sender sends more slowly
TCP and Congestion Control
Notes: 10/25/10
16
16
16

## Slide 17
Different TCP Congestion Control Algorithms
Notes: 10/25/10
17
17
17

## Slide 18
Flow Control and Congestion
Network collapse is prevented
"Fair sharing"
  When there are multiple TCP streams, each one uses an approximately equal share of available bandwidth
TCP detects congestion by observing packet loss
  Newer TCP stacks also respond to "Explicit Congestion Notification" signals from routers: packets are marked when queues nearly full
Effects of TCP congestion control
Notes: 10/25/10
18
18
18

## Slide 19
Flow Control and Congestion
TCP cannot tell the difference between transmission errors and queue overflows!
Hence transmission errors cause TCP to slow down too
Formula for maximum throughput of TCP in the presence of packet loss:
TCP and transmission errors
MSS
RTT . √ploss
Notes: 10/25/10
19
19
19

## Slide 20
Flow Control and Congestion
MSS = 1460 bytes
RTT = 1ms = 0.001 seconds
Packet loss = 2% = 0.02
1460 / (0.001 * √0.02) ≈ 10.3MB/sec = 82 Mbps
Short RTT means packet loss does not have a huge impact on local transfers
Example calculation: LAN
Notes: 10/25/10
20
20
20

## Slide 21
Flow Control and Congestion
MSS = 1460 bytes
RTT = 150ms = 0.15 seconds
Packet loss = 0.02% = 0.0002
1460 / (0.15 * √0.0002) ≈ 690KB/sec = 5.5 Mbps
Loss of just 1 packet in 5,000 causes severe reduction of throughput when transferring across the Internet!
Example calculation: WAN
Notes: 10/25/10
21
21
21

## Slide 22
Flow Control and Congestion
Smokeping gives a coarse measurement (20 packets every 5 minutes => 5% loss detectable, but bursts may be missed)
For more accurate measurement you need a tool like perfsonar / owamp
  Standard configuration sends 10 packets per second continuously
  Can detect packet loss of 0.17% over one minute, or 0.0028% over one hour
  Separate measurements in each direction
Measurement of packet loss
Notes: 10/25/10
22
22
22

## Slide 23
Questions?
?
Notes: 10/25/10
23
23