## Slide 1
Network Management & Monitoring Introduction to SNMP
Network Startup Resource Center
www.nsrc.org
These materials are licensed under the Creative Commons Attribution-NonCommercial 4.0 International license (http://creativecommons.org/licenses/by-nc/4.0/)

## Slide 2
Overview
What is SNMP?
Polling and querying
OIDs and MIBs
Notifications
SNMPv3

## Slide 3
What is SNMP?
SNMP – Simple Network Management Protocol
  Structured protocol, structured information
  For querying network device state and receiving notifications
  Also can be used to change state
  Industry standard, hundreds of tools exist that use it
  Supported on any decent network equipment
  Transport : UDP ports 161 and 162 (notifications)
Notes: Informs => evil
Why?
Only timestamp is sysUpTime, no notification receiver (management station) tracks sysUpTime to date/time. As informs are retried several times until acknowledged, the date/time shown in the management station logs is arrival time, which could be many seconds or minutes after it was sent. This screws up correlation of events.

## Slide 4
Uses for SNMP
Typical queries
  Bytes In/Out on an interface, errors
  CPU load
  Uptime
  Temperature
  …
For hosts (servers or workstations)
  Disk space
  Installed software
  Running processes
  ...

## Slide 5
SNMP Versions
v1 (1988) Original specification
  Historic
v2 (1996) Failed Standard
  Security + new data types + new operators
  64-bit counters, get-bulk, v2 notifications
  View-based access control model (VACM) introduced
  Historic, no current implementations left
v2c (1996) De facto standard
  v2 data types and operators
  v1 security (community string) (simple security model)
  Historic

## Slide 6
SNMP Versions cont.
v3 (1998) Robust security
  User/view based security (USM/VACM)
  Full Internet Standard
We will use SNMP v2c and v3 in this class

## Slide 7
SNMP roles
Terminology—We will be using Manager and Agent
Manager (the monitoring station)
Sometimes known as the SNMP client
SNMPv3 calls it the Command Generator and Notification Receiver
Agent (running on the equipment/server)
Sometimes known as the SNMP server
SNMPv3 calls it the Command Responder and Notification Originator
Windows and UNIX have SNMP agents

## Slide 8: How SNMP works Query / Response

## Slide 9
How SNMP works Trap / Inform

## Slide 10
How SNMP works
Basic operators:
get (manager -> agent)
  Query for a value
getnext (manager -> agent)
  Get next value (e.g. list of values for a table)
getresponse (agent -> manager)
  Response to get, getnext, or set, includes error returns

## Slide 11
How SNMP works
Basic operators:
set (manager -> agent)
  Set a value, or perform an action
trap (agent -> manager)
  Spontaneous notification from equipment (line down, temperature above threshold, ...)

## Slide 12
How SNMP works
Query/response based
  Monitoring generally uses get, getnext, getbulk
  Changing state uses set
  Response is always a getresponse
  getbulk requires v2c or v3
Notifications are delivered as traps or informs
  traps are unacknowledged
  informs are acknowledged (v2c, v3)
  Use v2c format traps
  No one uses informs

## Slide 13
SNMP TRAPS
A way for an Agent to notify the Manager without getting a Query from the Manager
Agent is configured to send TRAP messages when an event occurs
    coldStart
    warmStart
    ifDown
    authenticationFailure
After the manager receives the TRAP message, it can take further action if necessary

## Slide 14
The SNMP database
The information offered by a device is available in its Management Information Base (MIB)
SNMP uses Object Identifiers (OIDs) to organize this information
OIDs are keys to identifying each piece of data
OIDs are organized into a tree structure that is the MIB
MIB files document parts of the MIB on a device
Notes: Notice distinction between the MIB and MIB files.
The MIB is the information on the device.
MIB files document this information for humans and management stations.

## Slide 15
OIDs
OID: Object Identifier
A unique key to select a particular item of data in the device
The same piece of information is always found at the same OID. That's simple!
An OID is a variable-length string of numbers, e.g.
  .1.3.6.1.2.1.1.3
Allocated hierarchically in a tree to ensure uniqueness (similar to DNS)

## Slide 16
The MIB Tree
Root(.)
ccitt(0)
iso(1)
joint-iso-ccitt(3)
org(3)
dod(6)
internet(1)
directory(1)
mgmt(2)
1.3.6.1
experimental(3)
private(4)
enterprises(1)
cisco(9)
mib-2(1)
system(1)
interfaces(2)
ip(4)
snmp(11)
host(25)
hrStorage
hrSystem
hrDevice

## Slide 17
The MIB Tree
Root(.)
ccitt(0)
iso(1)
joint-iso-ccitt(3)
org(3)
dod(6)
internet(1)
directory(1)
mgmt(2)
1.3.6.1
experimental(3)
private(4)
enterprises(1)
cisco(9)
ciscoMgmt(9)
ciscoEnvMonMIB(13)
ciscoEnvMonObjects(1)
ciscoEnvMonTemperatureStatusTable(3)
ciscoEnvMonTemperatureStatusValue(3)
ciscoEnvMonTemperatureStatusEntry(1)
...
mib-2(1)
system(1)
interfaces(2)
ip(4)
snmp(11)

## Slide 18
If Email Addresses were OIDs
user@nsrc.org
would have been something like:
user@nsrc.enterprises.private.internet.dod.org.iso
user@99999.1.4.1.6.3.1
Except that we reverse the ordering, putting iso(1) first:
.1.3.6.1.4.1.99999.117.115.101.114
Note the portion after 99999—it spells “user” in ascii dotted decimal!
Don't worry about the deeply branched tree. What matters is that OIDs are unique.
Ensures vendors don't have conflicting OIDs
The numeric OID is what gets sent on the wire

## Slide 19
Interesting parts of the MIB tree
The Internet MIB, .1.3.6.1, really only two branches of interest:
Standard MIBs
.1.3.6.1.2.1 = .iso.org.dod.internet.mgmt.mib-2
Vendor-specific (proprietary) MIBs
.1.3.6.1.4.1 = .iso.org.dod.internet.private.enterprises

## Slide 20
Interesting parts of the MIB tree
The IEEE has MIBs of interest in three parts of the tree:
IEEE 802 MIBs, including LLDP
.1.0.8802 = .iso.standard.iso8802
IEEE 802.3 MIBs, including LAG
.1.2.840.10006 = .iso.member-body.us.ieee802dot3
IEEE 802.11 wireless MIBs
.1.2.840.10036 = .iso.member-body.us.ieee802dot11

## Slide 21
OIDs and MIB files
Read from left to right
OID components separated by '.'
  .1.3.6.1.4.1.9. ...
Each OID corresponds to a label
  .1.3.6.1.2.1.1.5 => sysName
The complete path:
  .iso.org.dod.internet.mgmt.mib-2.system.sysName
How do we convert from OIDs to Labels (and vice versa)?
Use the MIBs files!

## Slide 22
MIB Files
MIB files define the objects that can be queried, including:
Object name
Object description
Data type (integer, text, list)
MIB files are structured text
using an ASN.1 subset called the Structure of Management Information (SMI)

## Slide 23
MIB Files
Standard MIB files include:
MIB-II – (RFC1213) – a sub-group of MIBs
HOST-RESOURCES-MIB (RFC2790)

## Slide 24
MIB Sample (1 of 3)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the network management portion of the system was last re-initialized."
::= { system 3 }

## Slide 25
MIB Sample (2 of 3)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the network management portion of the system was last re-initialized."
::= { system 3 }
sysUpTime OBJECT-TYPE
This defines the object called sysUpTime.
SYNTAX TimeTicks
This object is of the type TimeTicks. Object types are specified in the SMI we mentioned a moment ago. ACCESS read-only
This object can only be read via SNMP (i.e., get, getnext); it cannot be changed (i.e., set).

## Slide 26
MIB Sample (2 of 3)
sysUpTime OBJECT-TYPE
SYNTAX TimeTicks
ACCESS read-only
STATUS mandatory
DESCRIPTION
"The time (in hundredths of a second) since the network management portion of the system was last re-initialized."
::= { system 3 }
STATUS mandatory
This object must be implemented in any SNMP agent.
DESCRIPTION
A description of the object
::= { system 3 }
The sysUpTime object is the third branch off of the system object group tree.

## Slide 27
MIB Files
MIB files also make it possible to interpret a returned value from an agent
For example, the status for a fan could be:
  1, 2, 3, 4, 5, or 6
  What does it mean?
Look for the Textual Convention (tc) in the MIB

## Slide 28
MIB Sample
CiscoEnvMonState ::= TEXTUAL-CONVENTION
STATUS current
DESCRIPTION
"Represents the state of a device being monitored.
Valid values are:
normal(1): the environment is good, such as low
temperature.
warning(2): the environment is bad, such as temperature
above normal operation range but not too
high.
critical(3): the environment is very bad, such as
temperature much higher than normal
operation limit.
shutdown(4): the environment is the worst, the system
should be shutdown immediately.
notPresent(5): the environmental monitor is not present,
such as temperature sensors do not exist.
notFunctioning(6): the environmental monitor does not
function properly, such as a temperature
sensor generates a abnormal data like
1000 C.
Notes: Courier New is not behaving correctly as a fixed font in LibreOffice Version: 4.3.5.2
Build ID: 3a87456aaa6a95c63eea1c1b3201acedf0751bd5
So I used Courier instead.

## Slide 29
SNMP and Security
SNMP versions 1 and 2c are insecure
SNMP version 3 was created to fix this
SNMPv3 authentication is based on a “User-based Security Model” (USM):
  Authenticity and integrity
  Keys are used for users, and messages have digital signatures generated with a hash function (MD5 or SHA)
  Privacy
  Messages can be encrypted with secret-key (private) algorithms (DES or AES)
  Temporary validity
  Utilizes a synchronized clock with a 150 second window with sequence checking

## Slide 30
SNMPv3 Security Levels
noAuthNoPriv
  No authentication, no privacy
authNoPriv
  Authentication with no privacy
authPriv
  Authentication with privacy

## Slide 31
Cisco SNMP Agent Configuration R/O
Read-only
# snmp-server community NetManage RO
  Enables SNMPv1 and v2c
# snmp-server group ReadGroup v3 auth
# snmp-server user admin ReadGroup v3 auth sha NetManage
  SNMPv3 authentication, no encryption
Notes: “priv aes 128” does not exist in all IOS images.
APs, for example, did not do AES with SNMP until IOS 15.
Other versions may only do AES 128, so there is no option after the aes keyword.

## Slide 32
Cisco SNMP Agent Configuration R/W
Read-write
# snmp-server group WriteGroup v3 auth write v1default
# snmp-server user admin-rw WriteGroup v3 auth sha NetManage priv aes 128 NetWrite
  Cisco allows authNoPriv and authPriv queries with this user
  You could also define a read-write user without encryption (priv)
  Note that we recommend using SNMP version 3 if you want write access using the set operator
Notes: “priv aes 128” does not exist in all IOS images.
APs, for example, did not do AES with SNMP until IOS 15.
Other versions may only do AES 128, so there is no option after the aes keyword.

## Slide 33
Net-SNMP Agent (snmpd)
Add a community string by editing /etc/snmp/snmpd.conf
and adding:
rocommunity NetManage 100.64.0.0/16
Add the SNMPv3 user
# systemctl stop snmpd
# net-snmp-create-v3-user –X DES -a NetManage admin
# system start snmpd

## Slide 34
Querying an SNMP agent
Using Net-SNMP command line tools...
Some typical commands for querying:
  snmpget
  snmpwalk
  snmpbulkwalk (requires v2c or v3)
  snmpstatus
  snmptable
All commands have same authentication options:
  snmpXXX -v1 -c<community> host [OID]
  snmpXXX -v2c -c<community> host [OID]
  snmpXXX -v3 -lauthNoPriv -u<user> -X DES -a<pass> host [OID]

## Slide 35
Using defaults
Set defaults in config file ~/.snmp/snmp.conf
  defVersion 3
  defCommunity NetManage
  defSecurityName admin
  defSecurityLevel authNoPriv
  defAuthPassphrase NetManage
  defAuthType SHA
After creating this file the commands are much shorter:
  snmpxxx host [OID]
Or, if you want to force the version to v2c:
  snmpxxx -v2c host [OID]

## Slide 36
Querying an SNMP agent
Let's look at some examples
$ snmpstatus 100.64.Y.1
$ snmpget 100.64.Y.1 ifNumber.0
$ snmpwalk -v2c 100.64.Y.1 ifDescr
“Y” == your campus number

## Slide 37
Querying an SNMP agent
Authentication options
  From command line flags or snmp.conf
OID
  A value, for example, .1.3.6.1.2.1.1.5.0
  or its name equivalent: sysName.0
Let's ask for the system's name (using the OID above)
  Why the .0? What do you notice?

## Slide 38
Queries Using snmp.conf
Two walks:
# snmpwalk 100.64.0.251 sysUpTime
DISMAN-EVENT-MIB::sysUpTimeInstance = Timeticks: (1946738) 5:24:27.38
# snmpwalk -v2c 3 100.64.0.251 sysUpTime
DISMAN-EVENT-MIB::sysUpTimeInstance = Timeticks: (1953429) 5:25:34.29
First walk used SNMPv3 as it was the default in snmp.conf, second walk specified SNMPv2c, and used the community string from snmp.conf.

## Slide 39
Failed Query...Why?
Two gets:
# snmpget -v1 100.64.0.251 ifHCInOctets.1
Error in packet
Reason: (noSuchName) There is no such variable name in this MIB.
Failed object: IF-MIB::ifHCInOctets.1
# snmpget 100.64.0.251 ifHCInOctets.1
IF-MIB::ifHCInOctets.1 = Counter64: 475028252
Why? Notice the data type: Counter64. 64-bit counters are only supported in SNMPv2c and v3.
64-bit counters are important because 32-bit interface counters (ifInOctets) can wrap in 34 seconds on Gig interfaces. (How fast can it wrap on 10G?)
snmpstatus: Unsupported security level # SNMPv3 configuration
snmpstatus: Unknown user name # problems

## Slide 40
SNMP failure: no response?
The device might be offline or unreachable
The device might not be running an SNMP agent
The device might be configured with a different community string
The device might be configured to refuse SNMP queries from your IP address
In all of these cases you will get no response

## Slide 41
SNMP Best Practices
Secure your SNMP access and traffic:
  Management VLAN
  Access lists
  Use SNMPv3 with authentication for queries and sets where possible
Use SNMPv2c traps
  Better formatted than v1 traps
  Accurate timestamps
Do no harm
  Only poll as fast as you really need
  Possible to drive CPU load on devices up and affect other protocol processing
  It does no good to poll every 5 seconds if the device updates the counter every 10

## Slide 42
Coming up in our exercises...
Using snmpwalk, snmpget
Config file: ~/.snmp/snmp.conf or /etc/snmp/snmp.conf
Running Linux SNMP agent (daemon) Config file: /etc/snmp/snmpd.conf
Loading MIBs

## Slide 43
References
Essential SNMP (O’Reilly Books) by Douglas Mauro, Kevin Schmidt
http://www.amazon.com/Essential-Second-Edition-Douglas-Mauro/dp/0596008406
Wikipedia
http://en.wikipedia.org/wiki/Simple_Network_Management_Protocol
MIB/OID Browser
http://oid-info.com/
Cisco SNMP on IOS, MIB tools, and MIB/OID browser
http://www.cisco.com/c/en/us/td/docs/ios-xml/ios/snmp/command/nm-snmp-cr-book.html
http://tools.cisco.com/ITDIT/MIBS/servlet/index
http://tools.cisco.com/Support/SNMP/do/BrowseOID.do?local=en&substep=2&translate=Translate&tree=NO

## Slide 44
References
Open Source Java MIB Browser
http://www.dwipal.com/mibbrowser.htm
SNMP Link – collection of SNMP resources
http://www.snmplink.org/
Net-SNMP Open Source SNMP tools
http://net-snmp.sourceforge.net/
Integration with Nagios
https://web.archive.org/web/20100614010336/http://www.cisl.ucar.edu/nets/tools/nagios/SNMP-traps.html

## Slide 45
SNMP Versions
v1 Original specification
RFCs 1155,1157,1213
v2 Security + new data types + new operators
RFCs 1901,1909-1910, 2011, 2576, 2578- 2580, 3416-3418
v2c De facto standard
Documented in RFC 3584
v3 Robust security: USM/VACM
RFCs 3411-3415, 3417- 3418, 3826, 5343, 5345, 5590
RFC 3584 specifies coexistence between versions
Notes: So much more could be added...random order...
SNMPv3 contexts and how it relates to the bridge-MIB, OSPF-MIB, etc...and how to use v1/v2c to get to the same info on xxx (Cisco's indexed community strings, net-snmp proxies)
Cisco's implementation of indexed community strings and switch stacks?
Views and VACM...we never even explain anything about them—we just use v1default on Cisco devices
Counter wraps—how it works, when it'll hurt you, what to do
How/where to get MIBs, how to use, when to use, errors in compilation with net-snmp, etc.
The whole leading . thing in OIDs
getnext...really important...
Leaves...touched on with the what is .0...enough?
…