## Slide 1: Campus Network Design Workshop
Introduction to Network Management & Monitoring
These materials are licensed under the Creative Commons Attribution-NonCommercial 4.0 International license
(http://creativecommons.org/licenses/by-nc/4.0/)
Last updated 18th October 2016

## Slide 2: Objectives
Introduce Core Concepts & Terminology
  Network Monitoring & Management
  What & Why we Monitor
  Uptime Expectations & Calculations
  Baseline Performance & Attack Detection
  What & Why we Manage
  Network Monitoring & Management Tools
  The NOC: Consolidating Systems

## Slide 3: NOC: Consolidating NMM Systems
NOC = Network Operations Center
  Coordination of tasks, handling of network related incidents (ticketing system)
  Status of network and services (monitoring tools)
  Where the tools are accessed
  Store of Documentation (wiki, database, repository ==> network documentation tool(s))
NOC Location
  NOC is an organizational concept
  Does not need to be a place, or even a single server
  Remote / Distributed NOC is valid with OOB Management

## Slide 5: Network Monitoring & Management
Monitoring
  Check the status of a network
Management
  Processes for successfully operating a network

## Slide 6: Monitoring Systems & Services
Systems
  Routers
  Switches
  Servers
Services
  DNS
  HTTP
  SMTP
  SNMP

## Slide 7: Why do we Monitor?
Are Systems and Services Reachable?
Are they Available?
What's their Utilisation?
What's their Performance
  Round-trip times, throughout
  Faults and Outages
Have they been Configured or Changed?
Are they under Attack?

## Slide 8: Why do we Monitor?
Know when there are problems – before our customers!
Track resource utilisation, and bill our customers
To Deliver on Service Level Agreements (SLAs)
  What does management expect?
  What do customers expect?
  What does the rest of the Internet expect?
To prove we're delivering
  Have we achieved Five Nines? 99.999%
To ensure we meet SLAs in the future
  Is our network about to fail? Become congested?

## Slide 9: Uptime Expectations
What does it take to deliver 99.9% uptime?
  Only 44 minutes of downtime a month!
Need to shut down one hour a week?
  That's only 99.4% uptime ((732-4)/732 = .9945355...)
Maintenance might be negotiated in SLAs
What does it mean that the network is up?
  Does it work at every location? Every host?
  Is the network up if it works at the Boss's desk?
  Should the network be reachable from the Internet?

## Slide 10: Establishing a Baseline
Monitoring can be used to Establish a Baseline
Baseline = What's normal for your network?
  Typical latency across paths
  Jitter across paths
  Load on links
  Percent Resource Utilisation
  Typical amounts of noise
    Network scans & random attacks from the Internet
    Dropped packets
    Reported errors or failures
Notes: Graph is just to show what jitter can look like (in SmokePing).

## Slide 11: Detecting Attacks
Deviation from baseline can mean an attack
Are there more flows than usual?
Is the load higher on some servers or services?
Have there been multiple service failures?
These things could mean an attack
Notes: This graph is from the Slammer worm causing UDP floods resulting in Denial of Service attacks.

## Slide 12: What do we Manage?
Asset management: What equipment have we deployed?
  What software is it running
  What's its configuration (hardware & software)
  Where is it installed
  Do we have spares?
Incident management: fault tracking and resolution
Change management: Are we satisfying user requests?
  Installing, moving, adding, or changing things
Staff management

## Slide 13: Why do we Manage?
To ensure we meet business requirements for service level, incident response times etc
To make efficient use of our resources (including staff)
To learn from problems and make improvements to reduce future problems
To plan for upgrades, and make purchasing decisions with sufficient lead time

## Slide 14: Network Monitoring Tools
Availability: Nagios
  for servers, services, routers, switches, environment
Reliability: Smokeping
  connection health, rtt, service response time, jitter
Performance: LibreNMS
  traffic, port utilisation, cpu, RAM, disk, processes
Integration & overlap exists between these programs!

## Slide 15: Network Management Tools
Ticket Systems: RT
  Manage provisioning & support
Configuration Management: RANCID
  Track router configurations
Network Documentation: NetDot
  Inventory, Location, Ownership of Network Assets
Integration & overlap exists between these programs!

## Slide 16: A few Open Source NMM Tools
Performance | Change Management | Net Management
Cricket | Mercurial | Big Brother
flowc | RANCID | Cacti
mrtg | CVS | Hyperic
NetFlow | Subversion | LibreNMS
NfSen | git | Nagios
ntop | Security/NIDS | OpenNMS
perfSONAR | Nessus | Sysmon
pmacct | OSSEC | Zabbix
RRDTool | Prelude | Documentation
SmokePing | Samhain | IPplan
Ticketing | SNORT | Netdisco
RT | Untangle | Netdot
Trac |  | Utilities
Redmine |  | SNMP, Perl, Ping

## Slide 17: NMM Review
Network Monitoring & Management
What & Why we Monitor
Uptime Expectations & Calculations
Baseline Performance & Attack Detection
Network Attack Detection
What & Why we Manage
Network Monitoring & Management Tools
The NOC: Consolidating Systems

## Slide 18: Questions?