## Slide 1: The Domain Name System

## Slide 2: Some DNS topics
What the Internet’s DNS is
Configuring a resolver on a Unix-like system
Configuring a nameserver on a Unix-like system
Exercise: Create and install a simple zone

## Slide 3: What the Internet’s DNS is
A systematic namespace called the domain name space
Different people or organisations are responsible for different parts of the namespace
Information is associated with each name
A set of conventions for using the information
A distributed database system
Protocols that allow retrieval of information, and synchronisation between servers

## Slide 4: A systematic namespace - the domain name space
Several components (called labels)
  written separated by dots
  often written terminated by a dot
Hierarchical structure
  Leftmost label has most local scope
  Rightmost label has global scope
  Terminal dot represents root of the hierarchy
Domain names are case independent

## Slide 5: Why use hierarchical names?
Internet hosts and other resources need globally unique names
Difficult to keep unstructured names unique
  would require a single list of all names in use
Hierarchical names are much easier to make unique
  cat.abc.at. is different from cat.abc.au.

## Slide 6: What are domain names used for?
To identify computers (hosts) on the Internet
    austin.ghana.com
To identify organisations
    afnog.org
To map other information to a form that is usable with the DNS infrastructure
    IP addresses, Telephone numbers, AS numbers

## Slide 7: Examples of domain names
.
COM.
GH.
CO.ZA.
www.afnog.org.
in-addr.arpa.

## Slide 8
Domain Name Hierarchy
.
edu
Root domain
com
gov
mil
net
org
ro
fr
at
. . . . . .
jp
ici
rnc
ase
pub
utt
vsat
roearn ns std
cs
lmn
dsp
ulise paul
ac
co
gv
or . . .
uni-linz
tuwien
. . . . . . .
eunet
cc
univie
mat
exp
itc
. . . . . .
phytia alpha chris
Top-Level-Domains
Second Level Domains

## Slide 9: Different uses of the term “domain”
Sometimes, the term “domain” is used to refer to a single name
  such as www.afnog.org
Sometimes, the term “domain” is used to refer to all the names (subdomains) that are hierarchically below a particular name
  in this usage, the afnog.org domain includes www.afnog.org, ws.afnog.org, t1.ws.afnog.org, etc.

## Slide 10: Other information mapped to domain names
Almost any systematic namespace could be mapped to the domain name space
Need an algorithm agreed to by all people who will use the mapping

## Slide 11: Different people responsible for diff. parts
Administrator responsible for a domain may delegate authority for a subdomain
Each part that is administered independently is called a zone
Domain or zone administrator may choose to put subdomains in same zone as parent domain, or in different zone, depending on policy and convenience

## Slide 12: What is a zone? (1)
Think of the namespace as a tree or graph of nodes joined by arcs
  Each node represents a domain name

## Slide 13: What is a zone? (diagram 1)
.
A
B
X.A
Y.A
Z.A
J.B
K.B
L.B
CAT.K.B
DOG.K.B

## Slide 14: What is a zone? (2)
Think of the namespace as a tree or graph of nodes joined by arcs
  Each node represents a domain name
Now cut some of the arcs
  Each cut represents a delegation of administrative control

## Slide 15: What is a zone? (diagram 2)
.
A
B
X.A
Y.A
Z.A
J.B
K.B
L.B
CAT.K.B
DOG.K.B
Zone cut

## Slide 16: What is a zone? (3)
Each zone consists of a set of nodes that are still joined to each other through paths that do not involve arcs that have been cut
  The name “CAT.K.B” is in the “B” zone
  The name “DOG.K.B” is in the “DOG.K.B” zone
  The “DOG.K.B” zone is a child of the “B” zone

## Slide 17: What is a zone? (diagram 3)
.
A
B
X.A
Y.A
Z.A
J.B
K.B
L.B
CAT.K.B
DOG.K.B
Zone
Zone cut
Root zone
A zone
B zone
DOG.K.B zone

## Slide 18: Information is associated with each domain name
Several types of records (Resource Records, RRs), all with a similar format
Each RR contains some information that is associated with a specific domain name
Each domain name can have several RRs of the same type or of different types

## Slide 19: General format of RRs
Owner name - the domain name that this record belongs to
TTL - how long copies of this RR may be cached (measured in seconds)
Class - almost always IN
Type - there are many types
Data - different RR types have different data formats

## Slide 20: Several types of RRs
IP address for a host
Information needed by the DNS infrastructure itself
Hostname for an IP address
Information about mail routing
Free form text
Alias to canonical name mapping
Many more (but less commonly used)

## Slide 21: IP address for a host
A record
Owner is host name
Data is IP address
; IP address of austin.gh.com
austin.ghana.com. 86400 IN A 196.3.64.1

## Slide 22: Information needed by the DNS infrastructure itself
SOA record
  Each zone has exactly one SOA record
NS records
  Each zone has several nameservers that are listed as having authoritative information about domains in the zone
  One NS record for each such nameserver
Zone cuts are marked by these RRs

## Slide 23: SOA record
Every zone has exactly one SOA record
The domain name at the top of the zone owns the SOA record
Data portion of SOA record contains:
  MNAME - name of master nameserver
  RNAME - email address of zone administrator
  SERIAL - serial number
  REFRESH RETRY EXPIRE MINIMUM - timing parameters

## Slide 24: NS record
Each zone has several listed nameservers
One NS record for each listed nameserver
  master/primary and slaves/secondaries
the data portion of each NS record contains the domain name of a nameserver
Does not contain IP address
  Get that from an A record for the nameserver

## Slide 25: SOA and NS record example
  ; owner TTL class type data
  ghana.com. 86400 IN SOA austin.gh.com. support.gh.com. (
  199710161 ; serial
  21600 ; refresh
  3600 ; retry
  2600000 ; expire
  900 ) ; minimum
  ghana.com. 86400 IN NS ns1.ghana.com.
  ghana.com. 86400 IN NS ns2.ghana.com.
  ghana.com. 86400 IN NS server.elsewhere.example.

## Slide 26: SOA and NS example using some shortcuts
  $ORIGIN ghana.com.
  $TTL 86400
  ; owner TTL class type data
  @ IN SOA austin.gh.com. Support.gh.com. (
  199710161 ; serial
  21600 ; refresh
  3600 ; retry
  2600000 ; expire
  900 ) ; minimum
  NS ns1
  NS ns2
  NS server.elsewhere.example.

## Slide 27: More about RRs above and below zone cuts
RRs in the child zone (below the cut)
  SOA and NS records (authoritative)
RRs in the parent zone (above the cut)
  NS records (should be identical to those in the child zone)
glue records
  the child zone’s nameservers sometimes need A records in the parent zone

## Slide 28: Zone cut example - RRs in the child zone
parent is COM zone; child is GHANA.COM zone
child zone has SOA and NS records, and A records for hosts
  ghana.com. IN SOA xxx xxx xxx xxx xxx xxx xxx
  NS ns1.ghana.com.
  NS another.elsewhere.edu.
  ns1.ghana.com. A 192.0.2.3
  ; the ghana.com zone does not have an A record
  ; for another.elsewhere.edu.

## Slide 29: Zone cut example - RRs in the parent zone
parent is COM zone; child is XYZ.COM zone
parent zone has its own SOA and NS records, plus copies of child zone’s NS records, plus glue records
  COM. IN SOA xxx xxx xxx xxx xxx xxx xxx
  NS xxxxxxx
  NS yyyyyyy
  ghana.com. NS ns1.ghana.com.
  NS another.elsewhere.edu.
  ns1.ghana.com. A 192.0.2.3
  ; the com zone does not have an A record
  ; for another.elsewhere.edu.

## Slide 30: Hostname for an IP address
PTR record
Owner is IP address, mapped into the in-addr.arpa domain
Data is name of host with that IP address
; host name for IP address 196.3.64.1
1.64.3.196.in-addr.arpa. PTR austin.ghana.com.

## Slide 31
Reverse Lookup
When a source host establishes a connection to a destination host, the TCP/IP packets carry out only IP addresses of the source host;
For authentication, access rights or accounting information, the destination host wants to know the name of the source host;
For this purpose, a special domain “in-addr.arpa” is used;
The reverse name is obtained by reversing the IP number and adding the name “in-addr.arpa”;
Example: address: 130.65.240.254
        reverse name: 254.240.65.130.in-addr.arpa
Reverse domains form a hierarchical tree and are treated as any other Internet domain.
Rfc2317 Classless In-ADDR.ARPA delegation

## Slide 32
Reverse Domain Hierarchy
187
188
189
190
191
192
193
194
195
. . . . . .
157
158
159
160
165
166
167
168 . . .
.in-addr
.arpa
162
161
163
164
16
15
14
13
12
17
18
19
20
21
3
1
2
4
5

## Slide 33: Information about mail routing
MX record
Owner is name of email domain
Data contains preference value, and name of host that receives incoming email
; send ghana.com’s email to mailserver or backupserver
ghana.com. MX 0 mail.ghana.com.
ghana.com. MX 10 backupmail.ghana.com.

## Slide 34: Free form text
TXT record
Owner is any domain name
Data is any text associated with the domain name
Very few conventions about how to use it
net.ghana.com. TXT “NETWORKS R US”

## Slide 35: Alias to canonical name mapping
CNAME record
Owner is non-canonical domain name (alias)
Data is canonical domain name
; ftp.xyz.com is an alias
; ftp.ghana.com is the canonical name
ftp.ghana.com. CNAME austin.ghana.com

## Slide 36: A set of conventions for using the information
How to represent the relationship between host names and IP addresses
What records are used to control mail routing, and how the mail system should use those records
How to use the DNS to store IP netmask information
Many other things

## Slide 37: The DNS is a distributed database system
What makes it a distributed database?
How is data partitioned amongst the servers?
What about reliability?

## Slide 38: What makes it a distributed database?
Thousands of servers around the world
Each server has authoritative information about some subset of the namespace
There is no central server that has information about the whole namespace
If a question gets sent to a server that does not know the answer, that is not a problem

## Slide 39
Requirements for a nameserver
A query should be resolved as fast as possible;
It should be available 24 hours a day;
It should be reachable via fast communication lines;
It should be located in the central in the network topology;
It should run robust, without errors and interrupts.

## Slide 40: How is data partitioned amongst the servers?
The namespace is divided into zones
Each zone has two or more authoritative nameservers
  One primary or master
  One or more secondaries or slaves
  Slaves periodically update from master
Each server is authoritative for any number of zones (zero or more)

## Slide 41: What about reliability?
If one server does not reply, clients will ask another server
That’s why there are several servers for each zone
Zone administrators should choose servers that are not all subject to a single point of failure

## Slide 42: DNS Protocols
Client/server question/answer
  What kinds of questions can clients ask?
  The resolver/server model
  What if the server does not know the answer?
Master and slave servers
  Configuration by zone administrator
  Periodic update of slaves from master

## Slide 43: What kinds of questions can clients ask?
All the records of a particular type for a particular domain name
  All the A records, or all the MX records
All records of any type for a particular domain name
A complete zone transfer of all records in a particular zone
  Used to synchronise slave with master server

## Slide 44: The resolver/server model
user software asks resolver a question
resolver asks server
server gives answer, error, or referral to a set of other servers
server may recurse, or expect resolver to recurse
caching
authoritative/non-authoritative answers

## Slide 45: The resolver/server model (diagram)
Authoritative
Nameserver
Recursive Nameserver
CACHE
Resolver
Resolver
First query is forwarded,
and reply is cached
Next query is answered
from cache

## Slide 46: What if the server does not know the answer?
Servers that receive queries for which they have no information can return a referral to another server
Referral may include SOA, NS records and A records
Client can recursively follow the referral
Server may recurse on behalf of client, if client so requests and server is willing

## Slide 47: Master and slave servers
a.k.a. primary and secondary
zone administrator sets up primary/master
asks friends or ISPs to set up slaves/secondaries
slave periodically checks with master to see if data has changed
transfers new zone if necessary
serial number in SOA record in each zone

## Slide 48: Location of servers
one master and at least one slave
on different networks
avoid having a single point of failure
RFC 2182- SELECTION AND OPERATION OF SECONDARY DNS SERVERS
RFC2181- CLARIFICATIONS TO THE DNS SPECIFICATION

## Slide 49: Configuring a resolver on a Unix-like system
Unix-like systems use /etc/resolv.conf file
resolver is part of libc or libresolv, compiled into application programs
resolv.conf says which nameservers should be used by the resolver
resolv.conf also has other functions, see the resolver or resolv.conf man pages

## Slide 50: resolv.conf example
/etc/resolv.conf file contains the following lines
  domain ghana.com
  nameserver 196.3.64.1
  nameserver 192.168.3.57

## Slide 51: Configuring a nameserver on a Unix-like system
BIND is the most common implementation
up to version 4.9.* use /etc/named.boot file
from version 8.* use /etc/named.conf file
cache name
primary/master zone name and file name
secondary/slave zone name, master IP address, backup file name

## Slide 52: named.boot example
/etc/named.boot contains the following lines
  directory /etc/namedb
  ; type zone master file name
  cache . root.cache
  primary t1.ws.afnog.org afnog.org
  secondary gh.com 196.3.64.1 sec/gh.com

## Slide 53: named.conf example
/etc/named.conf contains the following lines
  options { directory "/etc/namedb"; };
  zone "." { type ; file "root.cache"; };
  zone ”t1.ws.afnog.org" { type master; file ”afnog.org"; };
  zone ”gh.com" { type slave; masters { 196.3.64.1; }; file "sec/gh.com"; };

## Slide 54
Checking DNS using nslookup
nslookup commands:
server <nameserver> ; set the server to be queried set type = NS ;queries NS resources set type = SOA ;queries SOA resources set type = A ;queries A resources set type = MX ;queries MX resources set type = CNAME ;queries CNAME resources set type = PTR ;queries PTR resources set type = ANY ;queries ANY resources ls <domain> ;lists the <domain> zone ls <domain> > <file-name> ;gets the zone <domain> into the
file<file-name>

## Slide 55
Checking DNS using dig
Dig
  Tool to manage DNS settings
  Syntax is:
dig [domain] @nameserver [query-type]

## Slide 56
Questions

## Slide 57: Exercise
Each student choose a domain name
  make it a subdomain of t1.ws.afnog.org
Choose two nameservers
Create a zone master file
  SOA, NS and A records
Edit named.conf appropriately
Check that resolv.conf is sensible
Test using nslookup or dig

## Slide 58: Exercise
Each row choose a domain name
  make it a subdomain of t1.ws.afnog.org
  any reasonable name
  must be unique

## Slide 59: Exercise
Choose two nameservers
  One in your cell
  One in another cell
  Get the other cell’s permission
Register with administrator of parent domain
  need to get nameservers working before registration is finished

## Slide 60: Exercise
Create a zone master file
  /etc/namedb/your-file-name
  SOA record
  NS records
  “glue” A records if necessary
  A records for your hosts
  any other records you want

## Slide 61: Exercise
Edit named.conf appropriately
  /etc/named.conf
  Add a section for your master zone
  Add sections for any slave zones, if another cell asks you to be a secondary for them
Start your nameserver
  ndc restart
  or run named by hand

## Slide 62: Exercise
Enable named in freebsd
  edit /etc/rc.conf
  add a section for named
  NAMED_ENABLE= “YES”
  NAMED_PROGRAM=“/USR/SBIN/NAMED”
Start your nameserver
  ndc restart
  or run named by hand/usr/sbin/named

## Slide 63: Exercise
Check that resolv.conf is sensible
  nameserver xxx.xxx.xxx.xxx
This allows applications on your host to do DNS lookups

## Slide 64: Exercise
Test with nslookup or dig
  dig @your.ip.addr.ess yourdomain.t1.ws.afnog.org. SOA
  check for sensible answer with AA flag
  also dig @ your secondary server
  also dig for NS records

## Slide 65
Exercise Checking DNS using dig
dig command: # dig [zone] @nameserver [query-type]
Exercises
  # dig @t1-dns.t1.ws.afnog.org t1.ws.afnog.org A
  # dig @t1-dns.t1.ws.afnog.org t1.ws.afnog.org NS
  # dig @t1-dns.t1.ws.afnog.org t1.ws.afnog.org MX
What information does this give you?
You can check other domains, known to you.