## Slide 1: RADIUS What it is
Remote Authentication Dial-In User Service
     A client/Server security Protocol Created by Livingston Enterprises Inc.
     An Internet draft protocol. RFC 2138 and RFC 2139, draft-ietf-radius-radius-v2-06.txt and draft-ietf-radius-accounting-v2-05.txt.
     Communication between Client and Server uses UDP. Ports 1812 and 1813 are reserved

## Slide 2: RADIUS How it Works
1- User initiates PPP authentication to the NAS.
2- NAS prompts for username and password (if PAP) or challenge (if CHAP).
3- User replies.
4- RADIUS client sends username and encrypted password to the RADIUS server.
5- RADIUS server responds with Accept, Reject, or Challenge.
The RADIUS client acts upon services and services parameters bundled with Accept or Reject.

## Slide 3: RADIUS Authentication-Authorization and accounting
 Support PPP, PAP or CHAP, UNIX login, PAM and other authentication mechanisms.
 Authentication and Authorization are coupled together.
 RADIUS accounting functions allow data to be sent at the start and end of sessions, indicating the amount of resources (such as time, packets, bytes, and so on) used during the session.

## Slide 4: RADIUS Features, Enhancements and distributions
 Security
 Flexibility
 Simplified management
 Extensive auditing capabilities
 Proxy RADIUS ETC….
 Different Radius Server distributions : Livingston, Merit, Cistron …
 Run under Unix and sometimes under Windows NT

## Slide 5: RADIUS current use
 Used to secure many university networks that provide dial-in IP connectivity to students and faculty.
 Used by many Internet service providers to provide security to users accessing their networks from multiple POPs (Points Of Presence).

## Slide 6: RADIUS Installation and Configuration
1. Select a host to use as the RADIUS server.
2. Install the RADIUS server software on the host.
3. Configure client information on the RADIUS server.
4. Configure the NAS as a RADIUS client.

## Slide 7: RADIUS Installation and Configuration
5. Configure user profiles.
6. You can optionally define menus to enable authenticated users to select different login options.
7. You can optionally install and configure RADIUS accounting.
8. You can optionally configure RADIUS proxy service.

## Slide 8: RADIUS Selecting Radius Server Host
 Select Primary and Secondary authentication and accounting servers with following characteristics.
Secure physical location
Root access limited to the security officer or system administrator
Limited number of user accounts--preferably none
Basic memory and disk space
Inaccessibility from outside your local network
Absence of public network services such as email, FTP, HTTP, netnews, Telnet, rlogin , and rcp
 Secondary is queried when Primary is down or not responding.

## Slide 9: RADIUS Radius Server Installation
 Depends on your Platform
 For Radius for Unix (radiusd) :
Get the package
Unpack it
Compile source
Install Binary and configuration files

## Slide 10: RADIUS Adding a Radius Client
1. Modify the clients file /usr/local/etc/raddb/clients to add the NAS and shared secret.
2. Configure the following on the NAS
- Security enabled on all ports
- IP addresses of the primary and optional alternate RADIUS authentication and accounting servers
- RADIUS shared secret

## Slide 11: RADIUS Adding a Radius Client
aaa new-model
aaa authentication login default group radius
aaa authentication ppp pppusers group radius
aaa authorization exec group radius
aaa authorization network group radius
aaa accounting exec start-stop radius
aaa accounting network start-stop radius
radius-server host 137.158.217.40 auth-port 1812 acct-port 1813
radius-server key afnog
Cisco router authentication and accounting configuration example

## Slide 12: RADIUS Configuring User Profile
 Following components of a profile must match the access-request for authentication to occur:
1. username
2. password check item
3. other check items
 Edit the file /usr/local/etc/raddb/users

## Slide 13: RADIUS Configuring User Profile
 The username matches if any of the following conditions are met :
- The username in the profile is identical to the login name in the access-request.
- The username in the profile is DEFAULT or DEFAULT #, where # is any integer

## Slide 14: RADIUS Configuring User Profile
 The password matches if it is identical to that entered by the user.
 All check items specified in a profile also must be present in the access-request packet or satisfied by local system information, for a match to occur

## Slide 15: RADIUS Running and and test
 Start radiusd on your Radius Servers
 Important: You need to restart radiusd or update configuration files (send a HUP SIGNAL) any time you change configuration files.
 Authenticate users

## Slide 16: RADIUS Proxy Service : ROAMING
 A common use for proxy service is roaming.
- Roaming permits two or more Internet service providers (ISPs) to allow each other's users to dial in to either ISP's network for service.
 Proxy service also enables an ISP to share its modem pool with that of neighboring ISPs.
 In some geographic areas, ISPs are establishing consortia to pool modems throughout the region by using remote servers.

## Slide 17: RADIUS Proxy Service : How it works
 The forwarding server sends the request to the remote server specified by the authentication realm .There are two kinds of realms:

## Slide 18: RADIUS Proxy Service : How it works
 A named realm is the part of a user login following the at sign (@).
For example: If aalain@ecowas.net is the user login, ecowas.net is the realm.
 A numbered realm is a Called-Station-Id.
You can forward proxy requests based on the number called.
 Special Realms: DEFAULT, NOREALM and NULL

## Slide 19: RADIUS Proxy Service : How it works
Configuring proxy using clients and proxy files.

## Slide 20: RADIUS Proxy Service : How it works
Roaming between ISPs in Lome and ISPs in Cape Town.

## Slide 21: RADIUS Scaling Radius Server
 Configuring Database Caching of User Profiles
- If your users file contains more than 500 users, use the builddbm utility to convert the users text file to the UNIX DBM format, which increases the speed of user lookups.
 Configure Radiusd to use PAM modules to authenticate users by more efficient security
systems.
- Example of using /etc/pwd.db or /etc/spwd.db on FreeBSD instead of the flat /etc/passwd .

## Slide 22: RADIUS Extra
RADIUS Codes (decimal) are assigned as follows:
1 Access-Request
2 Access-Accept
3 Access-Reject
4 Accounting-Request
5 Accounting-Response
11 Access-Challenge
12 Status-Server (experimental)
13 Status-Client (experimental)
255 Reserved