## Slide 1
Network Management
and
Network Operations
I have a network, now what?
Slides based on work by Abha Ahuja
<ahuja@merit.edu>
some slides based on the netmgt talk in T4-98 by Scott Bradner

## Slide 2: Outline
What is network management?
Fault Management
  Fault detection and tracking
  Performance Monitoring
  Basic Network Operations
  What are typical network problems?
Other parts of network management

## Slide 3: Outline (con)
Network Management Tools
  what do I need?
  what is available?
  Pros and Cons of various tools

## Slide 4: Network Management - What is it?
Making sure the network is up, running and performing well
Parts of Network Management
  fault management
  performance management
  security management
  trouble tracking
  statistics and accounting

## Slide 5: Fault Management
one of the most important parts of network management
detect network problems
  transient/persistent
  failure/overload
    examples: router down, serial link down
detect server problems
isolating problems

## Slide 6: Fault Management (con)
reporting mechanism
  link to help desk
  notify on-call personnel
setup & control alarm procedures
repair/recovery procedures
ticket system

## Slide 7: Fault Management - Fault Detection
Who notices a problem with the network?
  Network Operations Center w/ 24x7 operations staff
    open trouble ticket to track problem
    preliminary troubleshooting
    escalate to engineer or call carrier

## Slide 8: Fault Management - Fault Detection (con)
How can you tell if there is a problem with the network?
  Network Monitoring Tools
    common utilities
      ping
      traceroute
      snmp
  Report state or unreachability
    detect node down
    routing problems

## Slide 9: Fault Management - Fault Detection (con)
  “Alert” shows up for NOC
    rover
    spectrum
    NOCol
    HP Openview
    other
  Other methods
    customer complaint via phone/email
    another ISP notices problem

## Slide 10: Fault Detection Example - Using Rover
Rover = network monitoring system
  http://www.merit.edu/internet.tools/rover/
Keep it Simple
add nodes and tests to hostfile
run Display to see status
NOC notices alert on board for failed node
  opens ticket
  investigates

## Slide 11: The Alert Display Program
Time of Alert that failed
Name as in hostfile
IPAddress as in hostfile
Name of Test that failed
Place for status updates
Command line: ‘Help’ Problem #1

## Slide 12: hostfile

## Slide 13: InetRover
Pingd
Other tests
  dixie-X.500()
  SMTP(),FTP()
  NAMED(),TROUBLE()
  WWWTest

## Slide 14: InetRover (cont’d)
Extensibility
  Generic tests
  InetRoverd
  file existence
Any # of Displays
telnet/web display
Simple, right?
pingd
Generic test script
Generic test script

## Slide 15: Fault Management - Ticket System (Why all the fuss?)
Very Important!
Need mechanism to track:
  failures
  current status of outage
  carrier ticket #s

## Slide 16: Fault Management - Ticket Systems (Why all the fuss?)
system provides for:
  short term memory & communication
  scheduling and work assignment
  referrals and dispatching
  oversight
  statistical analysis
  long term accountability

## Slide 17: Fault Management - Ticket Systems (Why all the fuss?)
Goal: make your NOC the communication and coordination center!
Central repository for all information
  current status
  troubleshooting information
Engineers can coordinate their work through the NOC

## Slide 18: Fault Management - Ticket Usage
create a ticket on ALL calls
create a ticket on ALL problems
create a ticket for ALL scheduled events
copy of ticket mailed to reporter and mailing list(s)
all milestones in resolution of problem create a new ticket entry with reference to original
ticket stays "open" until problem resolved according to problem reporter

## Slide 19: Fault Management - Ticket Example
sample opening ticket
TT0000033975 has been OPENED. Here is the trouble ticket contents:
Create-date : 06/09/99 12:46:42
Ticket ID : TT0000033975
Node + : rs2.mae-west.rsng.net
Equipment Type : host
NOC Customer : RA
Trouble Reported : Unreachable
Next Action : Investigate
Next Action Date : 06/09/99 12:46:42
Outage type : unscheduled
Source of Report : Noc/roverStatus : Assigned
Assigned-to : Noc
Contact Name : rsng
Group Member :
Contact pager#/email address :
Contact Phone : .
Carrier Ticket History :
Carrier :
Carrier Phone :
Ticket information log :
06/09/99 12:46:42 noc-op
toppingb@facesofdeath.ns.itd.umich.edu said ...
11 Wed12:23 rs2MW_O/C 198.32.136.2 PING

## Slide 20: Fault Management - Ticket Example
sample progress ticket
TT0000033975 has been MODIFIED. Here are the fields that have been changed:
CopyOfTime : 5
TTC Temp : 0
Ticket information log : toppingb@facesofdeath.ns.itd.umich.edu said ...
While I was investigating this, Debbie from UUNet called (via Merit main
number) to tell us they were seeing it down. She can be reached at
xxx-xxxx. The UUNet ticket is xxxxx..

## Slide 21: Fault Management - Ticket Example
sample closing ticket
  includes previous ticket contents plus resolution
T0000033975 has been CLOSED. Here is the trouble ticket contents:
01/15/99 12:50:06 noc-op
mgf@wonka.ns.itd.umich.edu said ...
Email response from Abha suggesting contacting peers directly -- see
internal log.
01/15/99 14:25:22 noc-op
aubinc@augustus2.ns.itd.umich.edu said ...
The alerts cleared shortly before 14:00. I called MCI/Worldcom for an
update, and found out their ticket was closed. According to them the
outage was due solely to a power problem.
Closing.
Last-modified-by : noc-op
Modified-date : 01/15/99 14:25:22
Submitter : btracy

## Slide 22: Fault Management - typical failures
Node unpingable
  no ip connectivity to router
  possible reasons:
    serial link down
      call telco
    router down/hardware problem
      call engineer
    routing problem
      troubleshoot with traceroute
      routeviews machine

## Slide 23: Performance Management
evaluate the behavior of network elements
information used in planning
    interface stats
    throughput
    error rates
    software stats
    usage
    queues
    system load
    disk space
    percent availability

## Slide 24: Security Management
tends to be host-based
protect your stats, data and NOC info
protect other services
security required to operate network and protect managed objects
security services
  Kerberos
  PGP key server
  secure time

## Slide 25: Security Management (con)
security tools
  cops - host configuration checker (www.cert.org)
  swatch - email reports of activity on machine
  tcpwrappers
  ssh/skey
  tripwire
distribute security information
  bug reports
    CERT advisories
  bug fixes
  intruder alerts

## Slide 26: Security Management (con)
reporting procedure for security events
  e.g. break-ins
  abuse email address for customers to report complaints (abuse@your-isp.net)
control internal and external gateways
  control firewalls (external and internal)
security logs
privacy issues a conflict

## Slide 27: Security Management
Network based security
  Types of attacks
    DOS - Denial of Service
      ping floods
      smurf
      attacks that make your network unusable
    Spoofing
      packets with “spoofed” source address

## Slide 28: What types of problems?
Blocking and tracing denial of service attacks
Tracing incoming forged packets back to their source
Blocking outgoing forged packets
Most other security problems are not specific to backbone operators
Deal with complaints

## Slide 29: smurf
attacker sends many ping request packets:
  from forged (victim) source address
  to broadcast address on “amplifier” network
many ping responses from systems on amplifier network
attacker on dialup modem can saturate victim’s T1 using a T3-connected amplifier
http://users.quadrunner.com/chuegen/smurf/

## Slide 30: Protection against smurf
configure “no directed-broadcast” on all interfaces
  so you can’t be used as an amplifier
trace forged packets back, hop by hop
block outgoing forged packets from your customers
limit the bandwidth that can be used by ICMP traffic

## Slide 31: Smurf Attack
victim
attacker
amplifier
215.23.16.0/24
src IP=132.34.65.1
dst IP= 215.23.16.255
5*100 byte packets
132.34.65.1
24.3.2.1
253*5*100

## Slide 32: SYN flooding
attacker sends many TCP SYN packet from forged source address
victim sends SYN+ACK packets to invalid address
  gets no response
  connection hangs in half open state
  wastes OS resources, possibly crashing system

## Slide 33: Protection against SYN flooding
Make operating system more robust
  not a backbone problem, except on routers
Trace and block forged packets
Limit bandwidth that can be used by TCP SYN traffic

## Slide 34: Syn attack
attacker
victim
24.13.51.2
132.16.12.5
src IP=230.55.65.1
dst IP=132.16.12.5
connection request packets
( syn packets)
230.55.65.1
Replies go to spoofed IP

## Slide 35: Notice a pattern?
Forged packets
Need a way of preventing customers from sending forged packets
Need a way of tracing where forged packets really come from

## Slide 36: Tracing forged packets
Start on router near victim
Find how packets get to that router
Repeat on next router
Continue until edge of your AS
Ask next AS to trace further
Need cooperation
IMPORTANT - Should have a 24hour security contact!

## Slide 37: Security Management
Protecting your network
  traffic shapers
    use CAR to limit ICMP traffic
  anti-spoofing filters
    RFC 2267 (Network Ingress Filtering)
    for singly-homed customers
      IF packet's source address from within your network
      THEN forward as appropriate
      IF packet's source address is anything else
      THEN deny packet
    Filter on the outbound

## Slide 38: Preventing forged packets from customers
packet filters!
you know what IP addresses are used (at least for dialup and statically routed customers)
make a filter for each customer that denies other source addresses
very recent cisco code has “ip verify source-address”

## Slide 39: Preventing forged packets from you to outside world
you might know all the IP addresses that are used in your AS
  if your connections to the outside world and your transit arrangements are not too complicated
make a filter that denies other source addresses
apply that filter to all links from you to other Ases

## Slide 40: Configuration and Name Management
track network vitals
  ip addresses, interfaces, console phone numbers, etc
NOC needs valid contact info for nodes
network state information
  network topology
  operation status of network elements
    including resources
  network element configuration

## Slide 41: Configuration and Name Management
inventory management
  database of network elements
  history of changes & problems
directory maintenance
  all hosts & applications
  nameserver database
host and service naming coordination
  "Information is not information if you can't find it"

## Slide 42: Config. Mgmt. - Network State Info.
e.g. SNMP driven display
nnhvd
husc6
harvard
geo
oitgw1
mghgw
sphgw1
wjhgw1
wjh12
generali
talcott
harvisr
huelings
pitirium
nngw
lmagw1
dfch
tch
tch

## Slide 43: Network Management Tools
many use SNMP
ping
traceroute
References:
  MON - http://www.kernel.org/software/mon/
  NOCol - ftp://ftp.navya.com/pub/vikas/nocol.tar.gz
  Sysmon - ftp://puck.nether.net/pub/jared
  Rover - http://www.merit.edu/~rover
  Concord - http://www.concord.com

## Slide 44: What is SNMP? (the quick version...)
Simple Network Management Protocol
query - response system
  can obtain status from a device
  standard queries
  enterprise specific
uses database defined in MIB
  management information base

## Slide 45: What do we use SNMP for?
query routers for:
  in and out bytes per second
  CPU load
  uptime
  BGP peer session status
query hosts for:
  network status

## Slide 46: SNMP Network Management Tools
mrtg (http//:www.ee.ethz.ch/~oetiker/webtools/mrtg
  why we like it
    simple to use and configure
    quickly determine spikes/drops in traffic
      ping floods
  in/out bps
  uptime
  supplement to monitoring tools

## Slide 47: MRTG

## Slide 48: Netscarf/Scion
free
snmp collector and analyzer package
  collects snmp data
  display on web pages
http://www.merit.net/~netscarf

## Slide 49: Other Network Tools
netflow
  cflowd (http://www.caida.org/Tools/Cflowd)
  collects flow information from cisco routers
  AS to AS information
  src and destination ip and port information
  useful for accounting and statistics
  how much of my traffic is port 80?
  how much of my traffic goes to AS237?

## Slide 50: Netflow examples
Top ten lists (or top five)
##### Top 5 AS's based on number of bytes #######
srcAS dstAS pkts bytes
6461 237 4473872 3808572766
237 237 22977795 3180337999
3549 237 6457673 2816009078
2548 237 5215912 2457515319
##### Top 5 Nets based on number of bytes ######
Net Matrix
----------
number of net entries: 931777
SRCNET/MASK DSTNET/MASK PKTS BYTES
165.123.0.0/16 35.8.0.0/13 745858 1036296098
207.126.96.0/19 198.108.98.0/24 708205 907577874
206.183.224.0/19 198.108.16.0/22 740218 861538792
35.8.0.0/13 128.32.0.0/16 671980 467274801
##### Top 10 Ports #######
input output
port packets bytes packets bytes
119 10863322 2808194019 5712783 427304556
80 36073210 862839291 17312202 1387817094
20 1079075 1100961902 614910 62754268
7648 1146864 419882753 1147081 414663212
25 1532439 97294492 2158042 722584770

## Slide 51: More Tools!
http://www.caida.org/Tools/
  OC3Mon/Coral
http://www.merit.edu/~ipma
  RouteTracker
  IRRj
  ASExplorer
http://www.geektools.com/
http://www.merit.edu/ipma/tools/other.html

## Slide 52: ASexplorer

## Slide 53: Route Flap Stats

## Slide 54: Looking Glass Tools
route-views.oregon-ix.net>show ip bgp 35.0.0.0
BGP routing table entry for 35.0.0.0/8, version 56135569
Paths: (17 available, best #12)
11537 237
198.32.8.252 from 198.32.8.252
Origin incomplete, localpref 100, valid, external
Community: 11537:900 11537:950
2914 5696 237
129.250.0.3 (inaccessible) from 129.250.0.3
Origin IGP, metric 0, localpref 100, valid, external
Community: 2914:420
2914 5696 237
129.250.0.1 (inaccessible) from 129.250.0.1
Origin IGP, metric 0, localpref 100, valid, external
Community: 2914:420
3561 237 237 237
204.70.4.89 from 204.70.4.89
Origin IGP, localpref 100, valid, external
267 1225 237
204.42.253.253 from 204.42.253.253
Origin IGP, localpref 100, valid, external
Community: 267:1225 1225:237
http://www.merit.edu/~ipma/tools/lookingglass.html

## Slide 55: More Looking Glass Tools
Traceroute servers
http://www.merit.edu/ipma/tools/trace.html
Query: trace
Addr: www.isoc.org
Translating "www.isoc.org"...domain server (206.205.242.132) [OK]
Type escape sequence to abort.
Tracing the route to info.isoc.org (198.6.250.9)
1 iad1-core2-fa5-0-0.atlas.digex.net (165.117.129.2) 0 msec 0 msec 4 msec
2 dca5-core2-s5-0-0.atlas.digex.net (165.117.53.41) 0 msec 4 msec 0 msec
3 dca5-core1-fa5-1-0.atlas.digex.net (165.117.56.117) 4 msec 0 msec 4 msec
4 Hssi3-1-0.BR1.DCA1.ALTER.NET (209.116.159.98) 0 msec 0 msec 4 msec
5 101.ATM2-0.XR1.DCA1.ALTER.NET (146.188.160.226) [AS 701] 4 msec 0 msec 4 msec
6 195.ATM7-0.XR1.TCO1.ALTER.NET (146.188.160.102) [AS 701] 4 msec 0 msec 0 msec
7 193.ATM8-0-0.GW1.TCO1.ALTER.NET (146.188.160.33) [AS 701] 4 msec 4 msec 4 msec
8 charlie.isoc.org (198.6.250.1) [AS 701] 8 msec 8 msec 8 msec
9 info.isoc.org (198.6.250.9) [AS 701] 8 msec * 12 msec

## Slide 56: Accounting Management
what do you account for?
if you count packets sent
  it can inhibit anonymous ftp & web sites
  QoS differences in the future
want to charge "user" of service
  application dependent determination of "user"
if count hosts
  is a PC equal to a mainframe?
  cost?
usage-based billing may become common as telcos take over Internet service providers

## Slide 57: getoctets
simple traffic stats collector
cron-driven shell procedure
  get-octets router1 router2 router3
  figures out interface list for each router
then gets
  ifInOctets, ifOutOctets, ifInUcastPkts, ifOutUcastPkts
  ifInNUcastPkts, ifOutNUcastPkts, system.sysUpTime
ftp://ndtl.harvard.edu/pub/SNMPoll/octets.tar
  needs cmu snmp package

## Slide 58: getoctets, contd.
makes separate stats file for each interface
  example filename: 128.103.1.2.WJHgw1
example data
1997,06,23,160,09,1,00,02,37,EDT,1764089502,1045789221,99138769,92200835,10,628226,758006814
1997,06,23,160,09,1,00,22,37,EDT,1766362487,1047093977,99151676,92213338,10,628281,758126831
1997,06,23,160,09,1,00,42,36,EDT,1768439726,1048266407,99163118,92224546,10,628342,758246748
processing a bit hard
  must deal with counter wrap & router reboots
  sample period must be < 59 min for an Ethernet
link utilization calculation complex
  must include link encapsulation etc

## Slide 59: getoctets, processing
UpDate routine
  bug in 32 bit versions of perl (gives bad results)
example output
week millions of bits per second millions of octets
ending peak in peak out 95% in 95% out in out total
1997.06.01 5.0976 0.9330 1.3389 0.4104 18782 13752 32534

## Slide 60: Accounting, Cont.
could do settlements based in routing information
  try to minimize size of routing tables
Telco model
  everyone shares in revenue
  call an 800 number from a pay phone
    800 destinations pays pay phone owner
  receive a long distance call to your own switch
    you get free for local delivery

## Slide 61: Importance of Network Statistics
Accounting
Troubleshooting
Long-term trend analysis
Capacity Planning
Management Tools have statistical functionality

## Slide 62: Management for Real
Which tools should I use? What do I really need?
  Keep it simple!
  Need to consider engineers working remotely
  Don’t want to spend too much time maintaining the tool (it should be helping you!)
  Different tools for NOC and engineers
  Different tools for statistics
  RELIABILITY!

## Slide 63: Monitoring
simple monitoring tools do 95% of task
  e.g. ftp://ndtl.harvard.edu/pub/SNMPoll
  e.g. http://www.merit.edu/internet.tools/rover/
monitor should be both poll & trap based for best reliability
  but just polling will do better than just traps
  and will work fine other than response latency
simple, terse, messages on problems

## Slide 64: A Day in the Life of Merit’s NOC
running rover
  prefer because easy to tell when change occurs
  quickly can determine type of problem
  no sifting through GUIs
  quick screen display
alert appears on screen
27 Wed02:07 MCH_MSU:S6/1/7.6-->STOCKBRIDG 198.109.177.41 PING
28 Tue16:00 MCH_STOCKBRIDGE:S0.2-->JACKSO 198.109.177.46 PING
29 Tue16:00 MCH_STOCKBRIDGE:E0-GW 207.74.125.129 PING
30 Tue16:00 MCH_STOCKBRIDGE:S0.1-->MSU 198.109.177.42 PING

## Slide 65: A Day in the Life of Merit’s NOC
open ticket
investigate
  the two most important questions:
    can you ping it?
    can you trace to it?
  get to the the node from somewhere else in the network?
  dial-in to the router?
  serial line problem? call telco
If necessary, escalate to engineer

## Slide 66: Another example - Sluggishness
customer calls NOC - reports sluggishness
open ticket
investigate
  check mrtg
    more traffic now than normal?
  use netflow to determine what type of traffic
    possible denial of service attack
  circuit problem?
    call telco to test
always call customer back to get okay to close

## Slide 67: Another example - DOS
Customer reports possible Denial of Service
Open ticket
Investigate
  notice a large amount of packets from one destination?
    log onto router
    ip accounting
    sho ip route cache flow
  install packet filter
  report to offending ISP

## Slide 68: Tracing packets on cisco - interface access-group
cisco access list
  permit everything, but log packets from 10.2.3.4 to 195.176.0.0/16
    access-list 199 permit ip 10.2.3.4 0.0.0.0 195.176.0.0 0.0.255.255 log-input
    access-list 199 permit ip 0.0.0.0 255.255.255.255 0.0.0.0 255.255.255.255
apply access-list to interface
    interface serial3
    ip access-group 199 out

## Slide 69: Tracing packets on cisco - debug ip packet
cisco access list
  permit packets from 10.2.3.4 to 195.176.0.0/16, deny others
    access-list 199 permit ip 10.2.3.4 0.0.0.0 195.176.0.0 0.0.255.255 log-input
    access-list 199 deny ip 0.0.0.0 255.255.255.255 0.0.0.0 255.255.255.255
use access-list with “debug ip packet”
    debug ip packet 199

## Slide 70: Problems
we are early in the internet management game
  there is still a lot to learn
prices still high for functionality
  many new NMSs will be on the market soon, will help lower price and expand capabilities
data networks are not "plug and play" with large scale

## Slide 71: More Problems
not so good at provoking simple, easy to understand, warning to non-gurus
should have database & logic about when to cry wolf
  critical vs, noncritical device, access restrictions, who to call when
needs to be usable by "normal" people
needs to say when users will complain

## Slide 72: Even more Problems
training your Network Operations Staff
keeping your database up-to-date
  router configs
  contact information
communication with the telco

## Slide 73: More things you can do!
secure your router
  tacacs
  radius
  restrict login and snmp access
enable syslog logging
  security
  debugging

## Slide 74: More things you can do!
educate your NOC
  provide adequate documentation
  escalation procedures
register your routers in DNS
  traceroutes easier to follow
coolbeans% traceroute www.above.net
traceroute to www.above.net (207.126.96.163), 30 hops max, 40 byte packets
1 eth0-2.michnet1.mich.net (198.108.61.1) 1.074 ms 0.888 ms 0.696 ms
2 hssi1-0-0.msu.mich.net (198.108.22.102) 77.602 ms 75.356 ms 12.437 ms
3 aads.above.net (198.32.130.71) 9.981 ms 15.098 ms 11.342 ms
4 chicago-core1.ord.above.net (209.249.0.129) 9.634 ms 9.834 ms 9.590 ms
5 sjc-chicago-oc3.above.net (209.249.0.125) 71.261 ms 71.232 ms 71.305 ms
6 main2-core1-oc3-3.sjc.above.net (209.133.31.97) 123.499 ms 71.512 ms 71.8
7 www.above.net (207.126.96.163) 72.861 ms 72.624 ms 74.529 ms

## Slide 75: More things you can do!
Prevent excessive route-flapping
  enable route-flap dampening
  use CIDR
  use filters

## Slide 76: References
http://www.merit.edu/ipma/docs/isp.html
http://www.nanog.org
http://www.caida.org
http://www.nlanr.net
http://www.cisco.com
http://www.amazing.com/internet/
http://www.isp-resource.com/
http://www.merit.edu/ipma
http://www.ripe.net