## Slide 1: Welcome! APNIC DNS Workshop
15-18 January 2004, Bangalore, India
In conjunction with the SANOG III and the South Asian IPv6 Summit
Notes: Information about APNIC Training courses can be found at:
http://www.apnic.net/training/

## Slide 2: Introduction
Presenters
  Champika Wijayatunga <champika@apnic.net>
    Senior Training Specialist
  Arth Paulite <arth@apnic.net>
    Internet Resource Analyst
  Srinivas Chendi <sunny@apnic.net>
    Internet Resource Analyst
  <training@apnic.net>

## Slide 3: Acknowledgements
Bill Manning
Olaf M. Kolkman
Ed Lewis
Joe Abley

## Slide 4: Overview
15 Jan
  9.30am - Start
    DNS concepts I
  TEA BREAK (10.30am - 11.00am)
    DNS concepts II
    BIND installation
  LUNCH (12:30pm – 2:00pm)
    Lab 1 – BIND Installation
    Recursive Server
  TEA BREAK (3:00pm – 3:30pm)
    Lab 2 – Recursive Server

## Slide 5: Overview
16 Jan
  9.30am - Start
    Lab 3 – Configuring Domains
  TEA BREAK (10.30am - 11.00am)
    DNS Registries
  LUNCH (12:30pm – 2:00pm)
    Troubleshooting I (dig, traceroutes, nslookup, ethereal)
    Reverse DNS
  TEA BREAK (3:00pm – 3:30pm)
    Configuring the Reverse domain
    Lab 4 – Reverse DNS
    IPv6 reverse DNS

## Slide 6: Overview
17 Jan
  9.30am - start
    RNDC & TSIG
  TEA BREAK (10.30am - 11.00am)
    Lab 5 - RNDC & TSIG
  LUNCH (12:30pm – 2:00pm)
    DNSSEC Presentation
  TEA BREAK (3:00pm – 3:30pm)
    Lab 6 - Troubleshooting

## Slide 7: Overview
18 Jan
  9.30am - start
    Secured Dynamic Updates
  TEA BREAK (10.30am - 11.00am)
    Lab 7 – Secured Dynamic Updates
  LUNCH (12:30pm – 2:00pm)
    Creating the whole DNS hierarchy
  TEA BREAK (3:00pm – 3:30pm)
    Lab 8 - Creating the whole DNS hierarchy

## Slide 8: Introduction to DNS

## Slide 9: Purpose of naming
Addresses are used to locate objects
Names are easier to remember than numbers
You would like to get to the address or other objects using a name
DNS provides a mapping from names to resources of several types

## Slide 10: Names and addresses in general
An address is how you get to an endpoint
  Typically, hierarchical (for scaling):
    950 Charter Street, Redwood City CA, 94063
    204.152.187.11, +1-650-381-6003
A “name” is how an endpoint is referenced
  Typically, no structurally significant hierarchy
    “David”, “Tokyo”, “itu.int”

## Slide 11: Naming History
1970’s ARPANET
  Host.txt maintained by the SRI-NIC
  pulled from a single machine
  Problems
    traffic and load
    Name collisions
    Consistency
DNS created in 1983 by Paul Mockapetris (RFCs 1034 and 1035), modified, updated, and enhanced by a myriad of subsequent RFCs

## Slide 12: DNS
A lookup mechanism for translating objects into other objects
A globally distributed, loosely coherent, scalable, reliable, dynamic database
Comprised of three components
  A “name space”
  Servers making that name space available
  Resolvers (clients) which query the servers about the name space

## Slide 13: DNS Features: Global Distribution
Data is maintained locally, but retrievable globally
  No single computer has all DNS data
DNS lookups can be performed by any device
Remote DNS data is locally cachable to improve performance

## Slide 14: DNS Features: Loose Coherency
The database is always internally consistent
  Each version of a subset of the database (a zone) has a serial number
    The serial number is incremented on each database change
Changes to the master copy of the database are replicated according to timing set by the zone administrator
Cached data expires according to timeout set by zone administrator

## Slide 15: DNS Features: Scalability
No limit to the size of the database
  One server has over 20,000,000 names
    Not a particularly good idea
No limit to the number of queries
  24,000 queries per second handled easily
Queries distributed among masters, slaves, and caches

## Slide 16: DNS Features: Reliability
Data is replicated
  Data from master is copied to multiple slaves
Clients can query
  Master server
  Any of the copies at slave servers
Clients will typically query local caches

## Slide 17: DNS Features: Dynamicity
Database can be updated dynamically
  Add/delete/modify of any record
Modification of the master database triggers replication
  Only master can be dynamically updated
    Creates a single point of failure

## Slide 18: Concept: DNS Names
The namespace needs to be made hierarchical to be able to scale.
The idea is to name objects based on
  location (within country, set of organizations, set of companies, etc)
  unit within that location (company within set of company, etc)
  object within unit (name of person in company)

## Slide 19: Concept: DNS Names contd.
How names appear in the DNS
  Fully Qualified Domain Name (FQDN)
    WWW.APNIC.NET.
  labels separated by dots
DNS provides a mapping from FQDNs to resources of several types
Names are used as a key when fetching data in the DNS

## Slide 20: Concept: DNS Names contd.
Domain names can be mapped to a tree
New branches at the ‘dots’
whois
Root DNS
net
com
whois
apnic
ftp
www
isi
edu
dots

## Slide 21: Concept: Resource Records
The DNS maps names into data using Resource Records.
More detail later
www.apnic.net. … A 10.10.10.2
Address Resource
Resource Record

## Slide 22: Concept: Domains
Domains are “namespaces”
Everything below .com is in the com domain
Everything below apnic.net is in the apnic.net domain and in the net domain

## Slide 23: Concept: Domains
net
domain
com domain
apnic.net
domain
net
com
apnic
www
www
edu
isi
tislabs
•
whois
ws1
ws2
•
•
•
•
•
ftp
sun
moon
google
•

## Slide 24: Delegation
Administrators can create subdomains to group hosts
  According to geography, organizational affiliation or any other criterion
An administrator of a domain can delegate responsibility for managing a subdomain to someone else
  But this isn’t required
The parent domain retains links to the delegated subdomain
  The parent domain “remembers” who it delegated the subdomain to

## Slide 25: Concept: Zones and Delegations
Zones are “administrative spaces”
Zone administrators are responsible for portion of a domain’s name space
Authority is delegated from a parent and to a child

## Slide 26: Concept: Zones and Delegations
net
domain
apnic.net
zone
net zone
whois.apnic.net
zone
net
com
apnic
www
www
edu
isi
tislabs
•
whois
ws1
ws2
•
•
•
•
•
•
ftp
sun
moon
google

## Slide 27: Concept: Name Servers
Name servers answer ‘DNS’ questions
Several types of name servers
  Authoritative servers
    master (primary)
    slave (secondary)
  (Caching) recursive servers
    also caching forwarders
  Mixture of functionality

## Slide 28: Concept: Name Servers contd.
Authoritative name server
  Give authoritative answers for one or more zones
  The master server normally loads the data from a zone file
  A slave server normally replicates the data from the master via a zone transfer

## Slide 29: Concept: Name Servers contd.
master
slave
slave
Authoritative name server

## Slide 30: Concept: Name Servers contd.
Recursive server
  Do the actual lookups; ask questions to the DNS on behalf of the clients
  Answers are obtained from authoritative servers but the answers forwarded to the clients are marked as not authoritative
  Answers are stored for future reference in the cache

## Slide 31: Concept: Resolvers
Resolvers ask the questions to the DNS system on behalf of the application
Normally implemented in a system library (e.g, libc)

## Slide 32: Concept: Resolving process & Cache
Resolver
Question: www.apnic.net A
www.apnic.net A ?
Caching
forwarder
(recursive)
root-server
www.apnic.net A ?
Ask net server @ X.gtld-servers.net (+ glue)
gtld-server
www.apnic.net A ?
Ask apnic server @ ns.apnic.net (+ glue)
apnic-server
www.apnic.net A ?
192.168.5.10
192.168.5.10
Add to cache

## Slide 33: Concept: Resource Records
Resource records consist of it’s name, it’s TTL, it’s class, it’s type and it’s RDATA
TTL is a timing parameter
IN class is widest used
There are multiple types of RR records
Everything behind the type identifier is called rdata
Label
ttl
class
type
rdata
www.apnic.net. 3600 IN A 10.10.10.2

## Slide 34: Example: RRs in a zone file
apnic.net. 7200 IN SOA ns.apnic.net. admin.apnic.net. (
2001061501 ; Serial
43200 ; Refresh 12 hours
14400 ; Retry 4 hours
345600 ; Expire 4 days
7200 ; Negative cache 2 hours )
apnic.net. 7200 IN NS ns.apnic.net.
apnic.net. 7200 IN NS ns.eu.net.
whois.apnic.net. 3600 IN A 193.0.1.162
Label
ttl
class
type
rdata
host25.apnic.net. 2600 IN A 193.0.3.25

## Slide 35: Resource Record: SOA and NS
The SOA and NS records are used to provide information about the DNS itself
The NS indicates where information about a given zone can be found
The SOA record provides information about the start of authority, i.e. the top of the zone, also called the APEX

## Slide 36: Resource Record: SOA
Timing parameter
Master server
Contact address
Version number
net. 3600 IN SOA A.GTLD-SERVERS.net. nstld.verisign-grs.com. (
2002021301 ; serial
30M ; refresh
15M ; retry
1W ; expiry
1D ) ; neg.answ.ttl

## Slide 37: Concept: TTL and other Timers
TTL is a timer used in caches
  An indication for how long the data may be reused
  Data that is expected to be ‘stable’ can have high TTLs
SOA timers are used for maintaining consistency between primary and secondary servers

## Slide 38: Places where DNS data lives
Changes do not propagate instantly
Registry DB
Master
Slave server
Slave
Cache server
Not going to net if TTL>0
Might take up to refresh
to get data from master
Upload of zone data is local policy

## Slide 39: To remember...
Multiple authoritative servers to distribute load and risk:
  Put your name servers apart from each other
Caches to reduce load to authoritative servers and reduce response times
SOA timers and TTL need to be tuned to needs of zone. Stable data: higher numbers

## Slide 40: What have we learned so far
We learned about the architectures of
  resolvers,
  caching forwarders,
  authoritative servers,
  timing parameters
We continue writing a zone file

## Slide 41: Writing a zone file
Zone file is written by the zone administrator
Zone file is read by the master server and it’s content is replicated to slave servers
What is in the zone file will end up in the database
Because of timing issues it might take some time before the data is actually visible at the client side

## Slide 42: First attempt
The ‘header’ of the zone file
  Start with a SOA record
  Include authoritative name servers and, if needed, glue
  Add other information
Add other RRs
Delegate to other zones

## Slide 43: The SOA record
apnic.net. 3600 IN SOA ns.apnic.net. admin\.email.apnic.net. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. ttl
admin.email@apnic.net  admin\.email.apnic.net
Serial number: 32bit circular arithmetic
  People often use date format
  To be increased after editing
The timers above qualify as reasonable
Comments

## Slide 44: Authoritative NS records and related A records
NS record for all the authoritative servers
  They need to carry the zone at the moment you publish
A records only for “in-zone” name servers
  Delegating NS records might have glue associated
sanog.org. 3600 IN NS NS1.sanog.org.
sanog.org. 3600 IN NS NS2.sanog.org.
NS1.sanog.org. 3600 IN A 203.0.0.4
NS2.sanog.org. 3600 IN A 193.0.0.202

## Slide 45: Other data in the zone
Add all the other data to your zone file
Some notes on notation
  Note the fully qualified domain name including trailing dot
  Note TTL and CLASS
localhost.sanog.org. 3600 IN A 127.0.0.1
NS1.sanog.org. 4500 IN A 203.0.0.4
www.sanog.org. 3600 IN CNAME IN.sanog.org.
sanog.org. 3600 IN MX 50 mail.sanog.org.

## Slide 46: Zone file format short cuts nice formatting
sanog.org. 3600 IN SOA NS1.sanog.org. admin\.email.sanog.org. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. Ttl
sanog.org. 3600 IN NS NS1.sanog.org.
sanog.org. 3600 IN NS NS2.sanog.org.
sanog.org. 3600 IN MX 50 mail.sanog.org.
sanog.org. 3600 IN MX 150 mailhost2.sanog.org.
sanog.org. 3600 IN TXT “Demonstration and test zone”
NS1.sanog.org. 4500 IN A 203.0.0.4
NS2.sanog.org. 3600 IN A 193.0.0.202
localhost.sanog.org. 3600 IN A 127.0.0.1
NS1.sanog.org. 3600 IN A 193.0.0.4
www.sanog.org. 3600 IN CNAME IN.sanog.org.

## Slide 47: Zone file short cuts: repeating last name
sanog.org. 3600 IN SOA NS1.sanog.org. admin\.email.sanog.org. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. Ttl
3600 IN NS NS1.sanog.org.
3600 IN NS NS2.sanog.org.
3600 IN MX 50 mail.sanog.org.
3600 IN MX 150 mailhost2.sanog.org.
3600 IN TXT “Demonstration and test zone”
NS1.sanog.org. 3600 IN A 203.0.0.4
NS2.sanog.org. 3600 IN A 193.0.0.202
localhost.sanog.org. 4500 IN A 127.0.0.1
NS1.sanog.org. 3600 IN A 203.0.0.4
www.sanog.org. 3600 IN CNAME IN.sanog.org.

## Slide 48: Zone file short cuts: default TTL
$TTL 3600 ; Default TTL directive
sanog.org. IN SOA NS1.sanog.org. admin\.email.sanog.org. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. Ttl
IN NS NS1.sanog.org.
IN NS NS2.sanog.org.
IN MX 50 mail.sanog.org.
IN MX 150 mailhost2.sanog.org.
IN TXT “Demonstration and test zone”
NS1.sanog.org. IN A 203.0.0.4
NS2.sanog.org. IN A 193.0.0.202
localhost.sanog.org. 4500 IN A 127.0.0.1
NS1.sanog.org. IN A 203.0.0.4
www.sanog.org. IN CNAME NS1.sanog.org.

## Slide 49: Zone file short cuts: ORIGIN
$TTL 3600 ; Default TTL directive
$ORIGIN sanog.org.
@ IN SOA NS1 admin\.email.sanog.org. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. Ttl
IN NS NS1
IN NS NS2
IN MX 50 mailhost
IN MX 150 mailhost2
IN TXT “Demonstration and test zone”
NS1 IN A 203.0.0.4
NS2 IN A 193.0.0.202
localhost 4500 IN A 127.0.0.1
NS1 IN A 203.0.0.4
www IN CNAME NS1

## Slide 50: Zone file short cuts: Eliminate IN
$TTL 3600 ; Default TTL directive
$ORIGIN sanog.org.
@ SOA NS1 admin\.email.sanog.org. (
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. Ttl
NS NS1
NS NS2
MX 50 mailhost
MX 150 mailhost2
TXT “Demonstration and test zone”
NS1 A 203.0.0.4
NS2 A 193.0.0.202
localhost 4500 A 127.0.0.1
NS1 A 203.0.0.4
www CNAME NS1

## Slide 51: Delegating a zone (becoming a parent)
Delegate authority for a sub domain to another party (splitting of whois.apnic.net from apnic.net)
apnic.net
zone
whois.apnic.net
zone
net
com
apnic
www
www
edu
isi
tislabs
•
whois
ns1
ns2
•
•
•
•
•
•
ftp
sun
moon
google

## Slide 52: Concept: Glue
Delegation is done by adding NS records:
  whois.apnic.net. NS ns1.whois.apnic.net.
  whois.apnic.net. NS ns2.whois.apnic.net.
How to get to ns1 and ns2… We need the addresses
Add glue records to so that resolvers can reach ns1 and ns2
  ns1.whois.apnic.net. A 10.0.0.1
  ns2.whois.apnic.net. A 10.0.0.2

## Slide 53: Concept: Glue contd.
Glue is ‘non-authoritative’ data
Don’t include glue for servers that are not in sub zones
Only this record needs glue
  whois.apnic.net. NS ns1.whois.apnic.net.
  whois.apnic.net. NS ns2.apnic.net.
  whois.apnic.net. NS ns1.apnic.net.
  ns1.whois.apnic.net. A 10.0.0.1

## Slide 54: Delegating whois.apnic.net. from apnic.net.
whois.apnic.net
Setup minimum two servers
Create zone file with NS records
Add all whois.apnic.net data
apnic.net
Add NS records and glue
Make sure there is no other data from the whois.apnic.net. zone in the zone file