## Slide 1: Reverse DNS

## Slide 2: Overview
Principles
Creating reverse zones
Setting up nameservers
Reverse delegation procedures
IPv6 reverse delegations
Current status
Notes: In this section we will talk about the reverse dns concepts in details. Initially we will recap some of the fundamentals we covered in IRM1 and then we will go through how to create reverse zones and setting up name servers. We will also explain you the APNIC procedures wrt to creating reverse delegations. IPv6 reverse delegations are also covered in this section before we conclude with the current status.

## Slide 3: What is ‘Reverse DNS’?
‘Forward DNS’ maps names to numbers
  svc00.apnic.net -> 202.12.28.131
‘Reverse DNS’ maps numbers to names
  202.12.28.131 -> svc00.apnic.net
Notes: Overview
The aim of this section is to provide the reader with a sufficient knowledge of the procedures involved in making reverse address mapping possible for a /24 and longer prefixes , for assignments of size of multiple /24, and /16 allocations. Details about changing and deleting an existing delegation are provided and common errors are described
.
What is Forward and Reverse Delegation?
Applications such as ftp, e-mail, and telnet allow users to specify an Internet destination host as a domain name, such as www.sparkynet.my, as names are easier to remember than numbers. However, before an application can send IP packets, the IP address of the destination host must be determined. The Domain Name System (DNS) was thus devised to obtain the IP address for a given domain name. The inverse procedure, which produces the domain name from the IP address, is called reverse address mapping, and is the focus of this section.

## Slide 4: Reverse DNS - why bother?
Service denial
    That only allow access when fully reverse delegated eg. anonymous ftp
Diagnostics
    Assisting in trace routes etc
Registration
    Responsibility as a member and Local IR
Notes: Why is Reverse Delegation Necessary?
In this example FTP is used to illustrate the need for reverse delegation. Many FTP sites want to know which domain is requesting access. If reverse delegation is correctly set up by the domain sending the packet, the accessed domain may successfully trace back the packet to its origins. (Name-based virtual hosts are an exception). Hosts from address space which have not been reverse delegated may have problems accessing some FTP sites.
Not setting reverse address mapping correctly may have the following consequences:
(a) users are blocked from various services (ftp, mail);
(b) troubleshooting becomes more difficult since lookups cannot find the name of a particular machine and the users cannot be identified;
(c) more network traffic is generated as a result of failing lookup responses.
It is the responsibility of the APNIC members to make sure that all their address space is reverse delegated.

## Slide 5: In-addr.arpa
Hierarchy of IP addresses
  Uses ‘in-addr.arpa’ domain
    INverse ADDRess
IP addresses:
  Less specific to More specific
    210.56.14.1
Domain names:
  More specific to Less specific
    delhi.vsnl.net.in
  Reversed in in-addr.arpa hierarchy
    14.56.210.in-addr.arpa

## Slide 6: Principles
Delegate maintenance of the reverse DNS to the custodian of the address block
Address allocation is hierarchical
  LIRs/ISPs -> Customers -> End users

## Slide 7: Principles – DNS tree
whois
Root DNS
net
edu
com
au
whois
apnic
arpa
22
.64
.in-addr
.202
.arpa
- Mapping numbers to names - ‘reverse DNS’
202 203 210 211..
202
RIR
64
64
ISP
22
22
Customer
in-addr
Notes: IN-ADDR.ARPA Domain Tree
Similar to the UNIX file system, the full name of an IP host is determined in a hierarchical fashion. For example, the administration of the top level domain my is performed by ccTLD administrative person. The subdomain sparkynet was delegated by them to the ‘Sparkynet’', which uses the name www to refer to one of the hosts in our network. After the name www has been properly specified in the name server for sparkynet.my, the domain name www.sparkynet.my can be used to find its corresponding
Internet host.
The IN-ADDR.ARPA Domain tree is described in more detail in Chapters 1 and 2 of O'Reilly's DNS and BIND, 4th Edition.
Reverse Delegation is still very classful. It exclusively takes place on octet (/8, /16 and /24) boundaries. The same mechanism is used in reverse and forward delegation, but the authority of delegation is somewhat different. In order to use the same mechanism as forward DNS, a special domain "inaddr.arpa" is created. IP address has to be 'reversed' (written in reversed order) and suffixed by inaddr.arpa.
E.g. in order to reverse map 202.64.22.1 , it must become 1.22.64.202.in-addr.arpa .

## Slide 8: Creating reverse zones
Same as creating a forward zone file
  SOA and initial NS records are the same as normal zone
  Main difference
    need to create additional PTR records
Can use BIND or other DNS software to create and manage reverse zones
  Details can be different

## Slide 9: Creating reverse zones - contd
Files involved
  Zone files
    Forward zone file
      e.g. db.domain.net
    Reverse zone file
      e.g. db.192.168.254
  Config files
    <named.conf>
  Other
    Hints files etc.
      Root.hints

## Slide 10: Start of Authority (SOA) record
<domain.name.> CLASS SOA <hostname.domain.name.> <mailbox.domain.name> ( <serial-number> <refresh> <retry> <expire> <negative-caching> )
253.253.192.in-addr.arpa.

## Slide 11: Pointer (PTR) records
Create pointer (PTR) records for each IP address
or
131.28.12.202.in-addr.arpa. IN PTR svc00.apnic.net.
131 IN PTR svc00.apnic.net.

## Slide 12: A reverse zone example
Note trailing dots
$ORIGIN 1.168.192.in-addr.arpa.
@ 3600 IN SOA test.company.org. (
sys\.admin.company.org.
2002021301 ; serial
1h ; refresh
30M ; retry
1W ; expiry
3600 ) ; neg. answ. ttl
NS ns.company.org.
NS ns2.company.org.
1 PTR gw.company.org.
router.company.org.
2 PTR ns.company.org.
;auto generate: 65 PTR host65.company.org
$GENERATE 65-127 $ PTR host$.company.org.

## Slide 13: What we covered so far
Why Reverse DNS ?
The DNS tree ?
Files involved
Essential Resource Records
How to create reverse zones

## Slide 14: Setting up the primary nameserver
Add an entry specifying the primary server to the named.conf file
<domain-name>
  Ex: 28.12.202.in-addr.arpa.
<type master>
  Define the name server as the primary
<path-name>
  location of the file that contains the zone records
zone "<domain-name>" in {
type master;
file "<path-name>"; };
Notes: IN is optional.

## Slide 15: Setting up the secondary nameserver
Add an entry specifying the primary server to the named.conf file
<type slave> defines the name server as the secondary
<ip address> is the IP address of the primary name server
<domain-name> is same as before
<path-name> is where the back-up file is
zone "<domain-name>" in {
type slave;
file "<path-name>";
Masters { <IP address> ; }; };
Notes: “file” statement is optional. It is just a back-up copy. And the back-up copy is being loaded first before it updates from the primary.

## Slide 16: Reverse delegation requirements
/24 Delegations
    Address blocks should be assigned/allocated
    At least two name servers
/16 Delegations
    Same as /24 delegations
    APNIC delegates entire zone to member
    Recommend APNIC secondary zone
< /24 Delegations
    Read “classless in-addr.arpa delegation”
RFC
2317
Notes: RFC 2317:
This document describes a way to do IN-ADDR.ARPA delegation on non- octet boundaries for address spaces covering fewer than 256 addresses. The proposed method should thus remove one of the objections to subnet on non-octet boundaries but perhaps more significantly, make it possible to assign IP address space in smaller chunks than 24-bit prefixes, without losing the ability to delegate authority for the corresponding IN-ADDR.ARPA mappings.

## Slide 17: APNIC & ISPs responsibilities
APNIC
  Manage reverse delegations of address block distributed by APNIC
  Process members requests for reverse delegations of network allocations
ISPs
  Be familiar with APNIC procedures
  Ensure that addresses are reverse-mapped
  Maintain nameservers for allocations
    Minimise pollution of DNS

## Slide 18: Subdomains of in-addr.arpa domain
Subnetting on an Octet Boundary
  Similar to delegating subdomains of forward-mapping domains
Mapping problems
  In IPv4 the mapping is done on 8 bit boundaries (class full), address allocation is classless
  Zone administration does not always overlap address administration

## Slide 19: Subdomains of in-addr.arpa domain
Example: an organisation given a /16
  192.168.0.0/16 (one zone file and further delegations to downstreams)
  168.192.in-addr.arpa zone file should have:
  0.168.192.in-addr.arpa. NS ns1.organisation0.com.
  0.168.192.in-addr.arpa. NS ns2.organisation0.com.
  1.168.192.in-addr.arpa. NS ns1.organisation1.com.
  1.168.192.in-addr.arpa. NS ns2.organisation1.com.
  2.168.192.in-addr.arpa. NS ns1.organisation2.com.
  2.168.192.in-addr.arpa. NS ns2.organisation2.com.
  :
  :

## Slide 20: Subdomains of in-addr.arpa domain
Example: an organisation given a /20
  192.168.0.0/20 (a lot of zone files!) – have to do it per /24)
  Zone files
  0.168.192.in-addr.arpa.
  1.168.192.in-addr.arpa.
  2.168.192.in-addr.arpa.
  :
  :
  15.168.192.in-addr.arpa.

## Slide 21: Subdomains of in-addr.arpa domain
Example: case of a /24 subnetted with the mask 255.255.255.192
  In-addr zone – 254.253.192.in-addr.arpa
  Subnets
    192.253.254.0/26
    192.253.254.64/26
    192.253.254.128/26
    192.253.254.192/26
  If different organisations has to manage the reverse-mapping for each subnet
    Solution to follow…

## Slide 22: Classless in-addr for 192.253.254/24
CNAME records for each of the domain names in the zone
  Pointing to domain names in the new subdomains
1.254.253.192.in-addr.arpa. IN CNAME 1.0-63.254.253.192.in-addr.arpa.
2.254.253.192.in-addr.arpa. IN CNAME 2.0-63.254.253.192.in-addr.arpa.
:
0-63.254.253.192.in-addr.arpa. IN NS ns1.organisation1.com.
0-63.254.253.192.in-addr.arpa. IN NS ns2.organisation1.com.
65.254.253.192.in-addr.arpa. IN CNAME 65.64-127.254.253.192.in-addr.arpa.
66.254.253.192.in-addr.arpa. IN CNAME 66.64-127.254.253.192.in-addr.arpa.
:
64-127.254.253.192.in-addr.arpa. IN NS ns1.organisation2.com.
64-127.254.253.192.in-addr.arpa. IN NS ns2.organisation2.com.
:
:
:

## Slide 23: Classless in-addr for 192.253.254/24
Using $GENERATE (db.192.253.254 file)
$GENERATE 1-63 $ IN CNAME $.0-63.254.253.192.in-addr.arpa.
0-63.254.253.192.in-addr.arpa. IN NS ns1.organisation1.com.
0-63.254.253.192.in-addr.arpa. IN NS ns2.organisation1.com.
$GENERATE 65-127 $ IN CNAME $.64-127.254.253.192.in-addr.arpa.
64-127.254.253.192.in-addr.arpa. IN NS ns1.organisation2.com.
64-127.254.253.192.in-addr.arpa. IN NS ns2.organisation2.com.
:
:

## Slide 24: Classless in-addr for 192.253.254.0/26
Now, the zone data file for 0-63.254.253.192.in-addr.arpa can contain just PTR records for IP addresses 192.253.254.1 through 192.253.154.63
$TTL 1d
@ IN SOA ns1.organisation1.com. Root.ns1.organisation1.com. (
1 ; Serial
3h ; Refresh
1h ; Retry
1w ; Expire
1h ) ; Negative caching TTL
IN NS ns1.organisation1.com.
IN NS ns2.organisation1.com.
1 IN PTR org1-name1.organisation1.com.
2 IN PTR org1-name2.organisation1.com.
3 IN PTR org1-name3.organisation1.com.

## Slide 25: APNIC reverse delegation procedures
Upon allocation, member is asked if they want /24 place holder domain objects with member maintainer
  Gives member direct control
Standard APNIC database object,
  can be updated through online form or via email.
Nameserver/domain set up verified before being submitted to the database.
Protection by maintainer object
  (current auths: CRYPT-PW, PGP).
Zone file updated 2-hourly

## Slide 26: APNIC reverse delegation procedures
Complete the documentation
    http://www.apnic.net/db/domain.html
On-line form interface
  Real time feedback
  Gives errors, warnings in zone configuration
    serial number of zone consistent across nameservers
    nameservers listed in zone consistent
  Uses database ‘domain’ object

## Slide 27: Whois domain object
domain: 28.12.202.in-addr.arpa
descr: in-addr.arpa zone for 28.12.202.in-addr.arpa
admin-c: DNS3-AP
tech-c: DNS3-AP
zone-c: DNS3-AP
nserver: ns.telstra.net
nserver: rs.arin.net
nserver: ns.myapnic.net
nserver: svc00.apnic.net
nserver: ns.apnic.net
mnt-by: MAINT-APNIC-AP
mnt-lower: MAINT-DNS-AP
changed: inaddr@apnic.net 19990810
source: APNIC
Reverse Zone
Contacts
Name Servers
Maintainers (protection)

## Slide 28: What we covered so far
Why Reverse DNS ?
The DNS tree
Files involved
Essential Resource Records
How to create reverse zones
Setting up nameservers – config files
APNIC reverse delegation requirements
Classless in-addr.arpa
APNIC reverse delegation procedures

## Slide 29: Questions

## Slide 30: IPv6 Reverse delegations

## Slide 31: IPv6 representation in the DNS
Forward lookup support: Multiple RR records for name to number
  AAAA (Similar to A RR for IPv4 )
  A6 without chaining (prefix length set to 0 )
Reverse lookup support:
  Reverse nibble format for zone ip6.int
  Reverse nibble format for zone ip6.arpa

## Slide 32: IPv6 forward and reverse mappings
Existing A record will not accommodate IPv6’s 128 bit addresses
BIND expects an A record’s record-specific data to be a 32-bit address (in dotted-octet format)
An address record
  AAAA (RFC 1886)
A reverse-mapping domain
  Ip6.int (now replaced by ip6.arpa)

## Slide 33: The reverse DNS tree – with IPv6
whois
Root DNS
net
edu
com
int
whois
apnic
arpa
202 203 210
202
22
22
in-addr
64
64
RIR
ISP
Customer
IP6
IPv6 Addresses
Notes: IN-ADDR.ARPA Domain Tree
Similar to the UNIX file system, the full name of an IP host is determined in a hierarchical fashion. For example, the administration of the top level domain my is performed by ccTLD administrative person. The subdomain sparkynet was delegated by them to the ‘Sparkynet’', which uses the name www to refer to one of the hosts in our network. After the name www has been properly specified in the name server for sparkynet.my, the domain name www.sparkynet.my can be used to find its corresponding
Internet host.
The IN-ADDR.ARPA Domain tree is described in more detail in Chapters 1 and 2 of O'Reilly's DNS and BIND, 4th Edition.
Reverse Delegation is still very classful. It exclusively takes place on octet (/8, /16 and /24) boundaries. The same mechanism is used in reverse and forward delegation, but the authority of delegation is somewhat different. In order to use the same mechanism as forward DNS, a special domain "inaddr.arpa" is created. IP address has to be 'reversed' (written in reversed order) and suffixed by inaddr.arpa.
E.g. in order to reverse map 202.64.22.1 , it must become 1.22.64.202.in-addr.arpa .

## Slide 34
64
H1
H10
H8
H12
H32
ISP
/32
Downstream
ISP
/40
Customer
/48
Devices
/128
int
arpa
IP6
Root DNS
b.a.9.8.7.6.5.0.4.0.0.0.3.0.0.0.2.0.0.0.1.0.0.0.0.0.0.0.1.2.3.4.ip6.arpa.

## Slide 35: IPv6 forward lookups
Multiple addresses possible for any given name
  Ex: in a multi-homed situation
Can assign A records and AAAA records to a given name/domain
Can also assign separate domains for IPv6 and IPv4

## Slide 36: Sample forward lookup file
;; domain.edu
$TTL 86400
@ IN SOA ns1.domain.edu. root.domain.edu. (
2002093000 ; serial - YYYYMMDDXX
21600 ; refresh - 6 hours
1200 ; retry - 20 minutes
3600000 ; expire - long time
86400) ; minimum TTL - 24 hours
;; Nameservers
IN NS ns1.domain.edu.
IN NS ns2.domain.edu.
;; Hosts with just A records
host1 IN A 1.0.0.1
;; Hosts with both A and AAAA records
host2 IN A 1.0.0.2
IN AAAA 2001:468:100::2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: IPv6 reverse lookups
IETF decided to restandardize IPv6 PTR RRs
  They will be found in the IP6.ARPA namespace rather than under the IP6.INT namespace
The ip6.int domains has been deprecated, but some hosts still use them
  Supported for backwards compatiblity
Now using ip6.arpa for reverse
Notes: <number>
<footer>
<header>
<date/time>
Add that NATs make something break

## Slide 38: IPv6 reverse lookups - AAAA and ip6.arpa
Address record four times longer than A
  Quad A ( AAAA )
AAAA record is a parallel to the IPv4 A record
It specifies the entire address in a single record

## Slide 39: IPv6 reverse lookups - AAAA and ip6.arpa
Example
  Each level of subdomain
    Represents 4 bits
4.3.2.1.0.0.0.0.0.0.0.1.0.0.0.2.0.0.0.3.0.0.0.4.0.5.6.7.8.9.a.b
b.a.9.8.7.6.5.0.4.0.0.0.3.0.0.0.2.0.0.0.1.0.0.0.0.0.0.0.1.2.3.4.ip6.arpa.
Ipv6-host IN AAAA 4321:0:1:2:3:4:567:89ab

## Slide 40: IPv6 reverse lookups - PTR records
Similar to the in-addr.arpa
Example: reverse name lookup for a host with address 3ffe:8050:201:1860:42::1
b.a.9.8.7.6.5.0.4.0.0.0.3.0.0.0.2.0.0.0.1.0.0.0.0.0.0.0.1.2.3.4.ip6.arpa.
IN PTR test.ip6.example.com.
$ORIGIN 0.6.8.1.1.0.2.0.0.5.0.8.e.f.f.3.ip6.arpa.
1.0.0.0.0.0.0.0.0.0.0.0.2.4.0.0 14400 IN PTR host.example.com.

## Slide 41: Sample reverse lookup file
;; 0.0.0.0.0.0.1.0.8.6.4.0.1.0.0.2.rev ;; These are reverses for 2001:468:100::/64)
;; File can be used for both ip6.arpa and ip6.int.
$TTL 86400
@ IN SOA ns1.domain.edu. root.domain.edu. (
2002093000 ; serial - YYYYMMDDXX
21600 ; refresh - 6 hours
1200 ; retry - 20 minutes
3600000 ; expire - long time
86400) ; minimum TTL - 24 hours
;; Nameservers
IN NS ns1.domain.edu.
IN NS ns2.domain.edu.
1.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0 IN PTR host1.ip6.domain.edu
2.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0 IN PTR host2.domain.edu
;;
;; Can delegate to other nameservers in the usual way
;;
Notes: <number>
<footer>
<header>
<date/time>

## Slide 42: Sample configuration file
// named.conf
zone “domain.edu” {
type master;
file “master/domain.edu”;
}
zone “0.0.0.0.0.0.1.0.8.6.4.0.1.0.0.2.ip6.int" {
type master;
file "master/0.0.0.0.0.0.1.0.8.6.4.0.1.0.0.2.rev";
};
zone “0.0.0.0.0.0.1.0.8.6.4.0.1.0.0.2.ip6.arpa" {
type master;
file "master/0.0.0.0.0.0.1.0.8.6.4.0.1.0.0.2.rev";
};
Notes: <number>
<footer>
<header>
<date/time>

## Slide 43: Current Status – IPv6 in DNS
A6 and Bit label specifications has been made experimental
  RFC3363
IETF standardized 2 different formats
  AAAA and A6
  Confusions on which format to deploy
  More than one choice will lead to delays in the deployment of IPv6

## Slide 44: What we covered so far in IPv6 reverse DNS
IPv6 representation in the DNS
IPv6 forward and reverse mappings
AAAA and A6 records
Current status

## Slide 45: Questions ?

## Slide 46
References

## Slide 47
DNS and BIND by Paul Albitz & Cricket Liu
  O’Reilly
Request Forms
    http://www.apnic.net/db/revdel.html
    http://www.apnic.net/db/domain.html
Classless Delegations
    http://ftp.apnic.net/ietf/rfc/rfc2000/rfc2317.txt
Common DNS configuration errors
    http://ftp.apnic.net/ietf/rfc/rfc1000/rfc1537.txt

## Slide 48
Domain name structure and delegation
    http://ftp.apnic.net/ietf/rfc/rfc1000/rfc1591.txt
Domain administrators operations guide
    http://ftp.apnic.net/ietf/rfc/rfc1000/rfc1033.txt
Taking care of your domain
    ftp://ftp.ripe.net/ripe/docs/ripe-114.txt
Tools for DNS debugging
    http://ftp.apnic.net/ietf/rfc/rfc2000/rfc2317.txt