## Slide 1: Secured Dynamic Updates

## Slide 2: Caution
Portions of this slide set present features that do not appear in BIND until BIND 9.3
  Snapshot code is available for this
BIND 9.2 can perform most of the dynamic update features

## Slide 3: Outline
Dynamic Update Basics
Setting Up A Dynamic Zone
Tools
Securing It
Authorization Configuration
Playing with Update Commands
Interactions with DHCP

## Slide 4: Getting Data Into DNS
Network Database
Primary NS
$origin z.
@ soa ns ro
ns ns1.
ns a 1.1.1.1
Zone File
Secondary NS
AXFR
Dynamic Update

## Slide 5: Advantages of Dynamic Updates
Change DNS data quickly
Make changes from anywhere
No need to reload whole zone
Data becomes more current

## Slide 6: Uses of Dynamic Update
Adding a new delegation to a large zone
  Cut down on reload times
Conference attendees
  Laptops can use same name, new IP

## Slide 7: Risks of Dynamic Update
Authoritative servers listen to the network for data
Authorization checks needed before accepting a request
Server risks being tied up with updates
Dynamic zones are hard to edit via "the old ways"

## Slide 8: Other Considerations
Once a zone goes dynamic, it is hard to edit
Mixing dynamic data and critical static data is a bad idea, even neglecting security concerns
This isn't meant to scare you from dynamic update, but to alert you

## Slide 9: "Secure" Dynamic Update
Secure refers to the safety of the update requests
  Only the right clients will be able to get data into the zone
Limitations on the term "secure"
  Won't stop anyone issuing bad requests
  Doesn't address DNSSEC, adding digital signatures to the zone

## Slide 10: Tools
In order to do any of this, we need tools (software)
All are part of a BIND 9 distribution
  named - the server, concentrating on conf file
  dig - a query/response tool
  nsupdate - issues dynamic update messages
  rndc - remote name server daemon control
  dnssec-keygen - makes the keys needed

## Slide 11: A static zone
zone "myzone.example." {
type master;
file "myzone.example.";
allow-transfer { any; };
};

## Slide 12: Adding a dynamic zone
zone "myzone.example." {
type master;
file "myzone.example.";
allow-transfer { any; };
};
zone "dynamic.myzone.example." {
type master;
file "dynamic.myzone.example.";
allow-transfer { any; };
allow-update { any; };
};
//note: on-line slide is different

## Slide 13: dynamic.myzone.example
> cat db.dynamic.myzone.example
$ORIGIN dynamic.myzone.example.
$TTL 1d ; 1 day
@ IN SOA ns1 root (
1 ; serial
30m ; refresh (30 minutes)
15m ;retry (15 minutes)
19h ;expire (19h12m)
18min ;minimum (18min)
)
NS ns1.myzone.example

## Slide 14: Journal Files
Once a dynamic zone begins running
  A journal file (<zonefile>.jnl) is created when the first dynamic update has been made
  This binary, non-text file maintains all updates in recent times
  Updates aren't immediately reflected in the original <zonefile>, but they are eventually
  Journal entries are written to the zone file at server shutdown (and on demand)

## Slide 15: dig
Basic debugging aid
dig @server domain.name type
Used to verify that change has been made
Used to verify that SOA number increments

## Slide 16: dig examples
> dig @127.0.0.1 version.bind chaos txt
> dig @127.0.0.1 myzone.example. soa +multiline
> dig @127.0.0.1 dynamic.myzone.example. soa

## Slide 17: nsupdate
Generates updates based upon user input
Used to make requested updates

## Slide 18: nsupdate example
% nsupdate
> server 127.0.0.1
> zone dynamic.myzone.example.
> update add alu.dynamic.myzone.example. 600 A192.168.160.1
> update add dynamic.myzone.example. 600 MX 10 alu
> send
> quit
Just to check our work...
% dig @127.0.0.1 alu.dynamic.myzone.example. A
% dig @127.0.0.1 dynamic.myzone.example. MX

## Slide 19: rndc
"Remote" management of server, usually across 127.0.0.1
Used to stop, reload server
Used to freeze and unfreeze dynamic zone { available in BIND 9.3 }

## Slide 20: rndc examples
% rndc -c rndc.conf status
% rndc -c rndc.conf reload
% rndc -c rndc.conf freeze dynamic.myzone.example
% rndc -c rndc.conf unfreeze dynamic.myzone.example
% rndc -c rndc.conf stop
NOTE: "freeze" and "unfreeze" are introduced in BIND 9.3

## Slide 21: dnssec-keygen
Simple tool to generate keys
Used for DNSSEC too
Used here to generate TSIG keys
Used also to generate SIG(0) keys - in version 9.3

## Slide 22: dnssec-keygen tsig example
% dnssec-keygen -a HMAC-MD5 -b 128 -n host sample.tsig.key
Ksample.tsig.key.+157+02308
% ls Ksample*
Ksample.tsig.key.+157+02308.key Ksample.tsig.key.+157+02308.private

## Slide 23: dnssec-keygen sig(0) example
% dnssec-keygen -a RSA -b 512 -n host sample.tsig.key
Ksample.tsig.key.+001+18681
% ls Ksam*
Ksample.tsig.key.+001+18681.key Ksample.tsig.key.+157+02308.key
Ksample.tsig.key.+001+18681.private Ksample.tsig.key.+157+02308.private

## Slide 24: "Secured" Dynamic Update
Limited to the security of the requests
Dynamic Updates to a DNSSEC zone is a work in progress
Two steps
  Identify and authenticate the updater
  Determine if updater is authorized

## Slide 25: Steps
Create a separate zone for dynamic updates
  (Done)
Configure keys
Configure policy

## Slide 26: Configuring Keys
Two styles
  TSIG - shared secret
  SIG (0) - public key
TSIG
  works in 9.2, secret needed in named.conf (or “include”) and in client
SIG(0)
  needs 9.3, public key listed in the zone file (not in named.conf) and private key in client

## Slide 27: TSIG keys
Issue: Naming the key
  Name is arbitrary, but must be consistent between the named.conf and client
  There is an advantage to making it the same as a domain in the zone
To test the keys, turn on key-based authorization of AXFR - just for testing

## Slide 28: Making TSIG keys
dnssec-keygen -a HMAC-MD5 -b 128 -n host \ slave1.dynamic.myzone.example.
dnssec-keygen -a HMAC-MD5 -b 128 -n host \ slave2.dynamic.myzone.example.
ls:
Kslave1.dynamic.myzone.example.+157+42488.key
Kslave1.dynamic.myzone.example.+157+42488.private
Kslave2.dynamic.myzone.example.+157+57806.key
Kslave2.dynamic.myzone.example.+157+57806.private

## Slide 29: Adding TSIG to named.conf
key “slave1.dynamic.myzone.example." {
algorithm HMAC-MD5;
secret "sd7qi6tiw+N5fK3mGNDNJU9TwIju+1ye7r2shgfkxIg=";
};
key “slave2.dynamic.myzone.example." {
algorithm HMAC-MD5;
secret "KXMoZHZIIxVsxKp4aUp6YTy3EswUN9CeDEpneJDOgVM=";
};

## Slide 30: Configuring TSIG AXFR
Just so we can see that the keys work
zone "dynamic.myzone.example." {
type master;
file "dynamic.myzone.example.";
allow-transfer {
key slave1.dynamic.myzone.example.;
key slave2.dynamic.myzone.example.;
};
allow-update { 127.0.0.1; };
};

## Slide 31: Testing with dig
Fails:
% dig @127.0.0.1 dynamic.myzone.example. axfr
Succeeds:
% dig @127.0.0.1 dynamic.myzone.example. axfr -y slave1.dynamic.myzone.example.:KXMoZHZIIxVsxKp4aUp6YTy3EswUN9CeDEpneJDOgVM=
This shows that the TSIG key is properly configured in named.conf

## Slide 32: Key based dynamic updates (TSIG)
zone "dynamic.myzone.example." {
type master;
file "dynamic.myzone.example.";
allow-transfer {
key slave1.dynamic.myzone.example.;
key slave2.dynamic.myzone.example.;
};
allow-update {
key user1.dynamic.myzone.example.;
key user2.dynamic.myzone.example.;
};
};

## Slide 33: "Keying" nsupdate
The next three slides show different ways to add key information to nsupdate
  first hides key from "ps -aux" by entering it interactively
  second hides it by referencing the file it is in
  last puts the secret on the command line

## Slide 34: Keyed nsupdate #1
% nsupdate
> zone dynamic.myzone.example.
> server 127.0.0.1
> key user1.dynamic.myzone.example. sd7qi6tiw+N5fK3mGNDNJU9TwIju+1ye7r2shgfkxIg=
> update add puri.dynamic.myzone.example. 600 A 192.168.50.1
> send
% dig @127.0.0.1 puri.dynamic.myzone.example A

## Slide 35: Keyed nsupdate #2
% nsupdate -k Kuser1.dynamic.myzone.example.+157+57806.
> zone dynamic.myzone.example.
> server 127.0.0.1
> update add alu.dynamic.myzone.example. 900 A 192.168.50.2
> Send
% dig @127.0.0.1 alu.dynamic.myzone.example A

## Slide 36: Keyed nsupdate #3
% nsupdate -y Kuser1.dynamic.myzone.example.:sd7qi6tiw+N5fK3mGNDNJU9TwIju+1ye7r2shgfkxIg=
> zone dynamic.myzone.example.
> server 127.0.0.1
> update add palak.dynamic.myzone.example. A 90 192.168.50.2
> send
% dig @127.0.0.1 palak.dynamic.myzone.example. A

## Slide 37: Interaction with DHCP
See the following URL for in-depth information
  http://ops.ietf.org/dns/dynupd/secure-ddns-howto.html

## Slide 38: How DHCP and DynUp Look
Mirchi.net.
32.7.275.in-addr.arpa.
leases for 275.7.32.0-127
DNS
DHCP
apnic16.apnic.net
32.43.320.in-addr.arpa.
leases for 320.43.32.0-127
DNS
DHCP
Home
@APNIC 16
chawla.mirchi.net

## Slide 39: How This Happens, part 1
Host has a TSIG/SIG(0) to update the entry
  chawla.mirchi.net. A 275.7.32.17
Home DHCP can change 32.7.275.in-addr.arpa. (via TSIG/SIG(0))
  17.32.7.275.in-addr.arpa PTR chawla.mirchi.net.
APNIC16 DHCP can change 32.43.320.in-addr.arpa.
  17.32.43.320.in-addr.arpa PTR chawla.mirchi.net.

## Slide 40: At Lease Change Time
When releasing home address
  Home DHCP removes the PTR record
  Host alters/removes its A RR
  Done via scripts (depends on DHCP software)
When gaining APNIC 16 lease
  APNIC 16 DHCP adds a PTR record
  Host registers an A RR with the home server

## Slide 41: Questions?