## Slide 1: Flow tools
  APRICOT 2008
Network Management
Taipei, Taiwan
February 20-24, 2008

## Slide 2: Flow-tools
Collection of programs to post process Cisco NetFlow compatible flows.
Written in C, designed to be fast (scales to large installations).
Includes library (ftlib) for custom applications.
Installation with configure;make;make install on most platforms (FreeBSD, Linux, Solaris)...

## Slide 3: flow-capture
Collect NetFlow exports and stores to disk.
Built in compression.
Manages disk space by expiring older flow files at configurable limits.
Detects lost flows by missing sequence numbers and stores with flow metadata.

## Slide 4: flow-fanout
Replicate NetFlow UDP streams from one source to many destinations.
Destination may be a multicast address.

## Slide 5: flow-expire
Expire (remove) old flow files based on disk usage.
Same functionality built in to flow-capture.
Used when managing disk space in a distributed environment.

## Slide 6: Collector Placement and configuration
NetFlow is UDP so the collector should ideally be directly connected to the router to minimize packet loss and IP spoofing risks.
No flow control. Undersized collector will drop flows. Monitor netstat –s | grep buf and configure syslog so dropped flows will be logged.

## Slide 7: flow-print
Formatted output of flow files.
eng1:% flow-print < ft-v05.2002-01-21.093345-0500 | head -15
srcIP dstIP prot srcPort dstPort octets packets
131.238.205.199 194.210.13.1 6 6346 40355 221 5
192.5.110.20 128.195.186.5 17 57040 33468 40 1
128.146.1.7 194.85.127.69 17 53 53 64 1
193.170.62.114 132.235.156.242 6 1453 1214 192 4
134.243.5.160 192.129.25.10 6 80 3360 654 7
132.235.156.242 193.170.62.114 6 1214 1453 160 4
130.206.43.51 130.101.99.107 6 3226 80 96 2
206.244.141.3 128.163.62.17 6 35593 80 739 10
206.244.141.3 128.163.62.17 6 35594 80 577 6
212.33.84.160 132.235.152.47 6 1447 1214 192 4
132.235.157.187 164.58.150.166 6 1214 56938 81 2
129.1.246.97 152.94.20.214 6 4541 6346 912 10
132.235.152.47 212.33.84.160 6 1214 1447 160 4
130.237.131.52 130.101.9.20 6 1246 80 902 15

## Slide 8: flow-cat
Concat many flow files or directories of files.
eng1:% ls
ft-v05.2002-01-21.160001-0500 ft-v05.2002-01-21.170001-0500
ft-v05.2002-01-21.161501-0500 ft-v05.2002-01-21.171501-0500
ft-v05.2002-01-21.163001-0500 ft-v05.2002-01-21.173001-0500
ft-v05.2002-01-21.164501-0500 tmp-v05.2002-01-21.174501-0500
eng1:% flow-cat . | flow-print
srcIP dstIP prot srcPort dstPort octets packets
138.26.220.46 192.5.110.20 17 62242 33456 40 1
143.105.55.23 18.123.66.15 17 41794 41794 40 1
129.15.134.66 164.107.69.33 6 1214 2222 4500 3
132.235.170.19 152.30.96.188 6 6346 1475 128 3

## Slide 9: flow-merge
Flow-merge is similar to flow-cat except it maintains relative ordering of flows when combining the files.
Typically used when combining flows from multiple collectors.

## Slide 10: flow-filter
Filter flows based on port, protocol, ASN, IP address, ToS bits, TCP bits, and tags.
eng1% flow-cat . | flow-filter -P119 | flow-print | head -10
srcIP dstIP prot srcPort dstPort octets packets
155.52.46.50 164.107.115.4 6 33225 119 114 2
128.223.220.29 129.137.4.135 6 52745 119 1438382 1022
155.52.46.50 164.107.115.4 6 33225 119 374 6
164.107.115.4 192.58.107.160 6 60141 119 5147961 8876
128.223.220.29 129.137.4.135 6 52745 119 1356325 965
128.223.220.29 129.137.4.135 6 52714 119 561016 398
130.207.244.18 129.22.8.64 6 36033 119 30194 121
155.52.46.50 164.107.115.4 6 33225 119 130 2
198.108.1.146 129.137.4.135 6 17800 119 210720652 216072

## Slide 11: flow-split
Split flow files into smaller files.
Typically used with flow-stat and graphing. For example if flow files are 1 hour and want 5 minute data points in graph, flow-split can take the 1 hour flow files and generate 5 minute files.

## Slide 12: flow-tag
Adds a tag field to flows based on IP exporter, IP prefix, Autonomous System, or next hop.
Like flow-filter used with other tools.
Used to manage groups of prefixes or ASN’s.

## Slide 13: flow-header
Display meta information in flow file.
eng1:% flow-header < ft-v05.2002-01-21.093345-0500
#
# mode: normal
# capture hostname: eng1.oar.net
# exporter IP address: 0.0.0.0
# capture start: Mon Jan 21 09:33:45 2002
# capture end: Mon Jan 21 09:45:01 2002
# capture period: 676 seconds
# compress: on
# byte order: little
# stream version: 3
# export version: 5
# lost flows: 0
# corrupt packets: 0
# sequencer resets: 0
# capture flows: 341370
#

## Slide 14: flow-stat
Generates reports from flow files.
Output is readable and easily imported into graphing programs (gnuplot, etc).
IP Address, IP address pairs, ports, packets, bytes, interfaces, next hop, Autonomous System, ToS bits, exporter, and tags.

## Slide 15: flow-stat - summary
Total Flows : 24236730
Total Octets : 71266806610
Total Packets : 109298006
Total Time (1/1000 secs) (flows): 289031186084
Duration of data (realtime) : 86400
Duration of data (1/1000 secs) : 88352112
Average flow time (1/1000 secs) : 11925.0000
Average packet size (octets) : 652.0000
Average flow size (octets) : 2940.0000
Average packets per flow : 4.0000
Average flows / second (flow) : 274.3201
Average flows / second (real) : 280.5177
Average Kbits / second (flow) : 6452.9880
Average Kbits / second (real) : 6598.7781

## Slide 16: flow-stat – Source AS % Total
#
# src AS flows octets packets duration
#
NSFNETTEST14-AS 6.430 6.582 7.019 5.693
ONENET-AS-1 2.914 4.417 3.529 3.566
UONET 0.600 4.052 2.484 1.979
UPITT-AS 1.847 3.816 2.697 2.552
CONCERT 1.786 2.931 2.391 1.955
OHIOU 3.961 2.601 2.140 1.655
CMU-ROUTER 1.962 2.577 2.349 2.075
BOSTONU-AS 1.503 2.126 1.665 1.914
PURDUE 2.185 1.994 2.157 2.507
STANFORD 2.124 1.950 2.270 2.636
UR 1.809 1.919 1.652 1.532
UMN-AGS-NET-AS 1.612 1.895 1.788 1.938
RISQ-AS 1.086 1.849 1.378 1.367
PENN-STATE 2.845 1.641 2.666 2.190
RIT-ASN 0.796 1.601 1.414 0.830

## Slide 17: flow-stat – Dest AS % Total
#
# dst AS flows octets packets duration
#
NSFNETTEST14-AS 6.202 9.564 8.005 6.762
PENN-STATE 2.037 3.774 2.712 2.153
CONCERT 2.628 3.133 2.888 2.326
ONENET-AS-1 2.818 2.434 2.906 3.000
STANFORD 1.915 2.360 2.122 2.195
JANET 2.508 2.319 2.150 2.485
0 0.831 2.187 2.431 2.910
DFN-WIN-AS 2.349 2.099 1.938 2.359
CMU-ROUTER 1.383 2.090 1.972 1.960
UONET 0.537 2.067 1.699 1.397
PURDUE 2.029 1.934 1.983 2.177
UMN-AGS-NET-AS 1.608 1.784 1.664 1.681
UPITT-AS 1.507 1.707 2.067 2.288
MIT-GATEWAYS 0.677 1.425 1.175 0.806
RIT-ASN 0.644 1.313 1.243 0.868
INDIANA-AS 0.899 1.285 0.996 0.781

## Slide 18: flow-stat – Src/Dest AS % Total
#
# src AS dst AS flows octets packets duration
#
GEORGIA-TECH PENN-STATE 0.030 0.965 0.459 0.071
NWU-AS 0 0.008 0.734 0.379 0.170
UONET CONCERT 0.064 0.698 0.438 0.290
UCLA NSFNETTEST14-AS 0.037 0.568 0.269 0.111
CONCERT UONET 0.052 0.543 0.364 0.221
BCNET-AS MIT-GATEWAYS 0.019 0.538 0.274 0.134
UONET 0 0.015 0.536 0.318 0.200
MIT-GATEWAYS STANFORD 0.032 0.477 0.245 0.073
ONENET-AS-1 NSFNETTEST14-AS 0.140 0.451 0.263 0.159
UONET PENN-STATE 0.019 0.439 0.200 0.063
NOAA-AS NOAA-FSL 0.018 0.438 0.255 0.031
DENET UONET 0.032 0.410 0.189 0.188
NSFNETTEST14-AS UC-DOM 0.022 0.365 0.244 0.081
ITALY-AS UONET 0.016 0.358 0.228 0.117
NSFNETTEST14-AS CONCERT 0.322 0.349 0.335 0.228
UONET ITALY-AS 0.022 0.349 0.210 0.130

## Slide 19: flow-dscan
DoS detection / network scanning tool.
Flag hosts which have flows to many other hosts.
Flag hosts which are using a large number of TCP/UDP ports.
Works better on smaller networks or with flow-filter to limit traffic. For example filter TCP port 25 to detect hosts infected with e-mail worm.

## Slide 20: flow-gen
Debugging tool to generate flows.
eng1:% flow-gen -V8.1 | flow-print | head -10
srcAS dstAS in out flows octets packets duration
0 65280 0 65280 2 1 1 4294901760
1 65281 1 65281 4 2 2 4294901760
2 65282 2 65282 6 3 3 4294901760
3 65283 3 65283 8 4 4 4294901760
4 65284 4 65284 10 5 5 4294901760
5 65285 5 65285 12 6 6 4294901760
6 65286 6 65286 14 7 7 4294901760
7 65287 7 65287 16 8 8 4294901760
8 65288 8 65288 18 9 9 4294901760

## Slide 21: flow-send
Transmit flow files with NetFlow protocol to another collector.
Can be used to take flow-tools files and send them to other NetFlow compatible collector.

## Slide 22: flow-receive
Like flow-capture but does not manage disk space. Output is to standard out and can be used directly with other flow-tools programs.
Typically used for debugging.
eng1:% flow-receive 0/0/5555 | flow-print
flow-receive: New exporter: time=1011652474 src_ip=199.18.112.114
dst_ip=199.18.97.102 d_version=8
srcPrefix srcAS dstPrefix dstAS input output flows
143.105/16 600 128.9/16 4 48 25 1
140.141/16 600 150.216/16 81 48 25 4
132.235/16 17135 130.49/17 4130 38 25 25
131.123/16 11050 129.59/16 7212 42 25 1
206.21/16 600 128.239/16 11975 48 25 2
199.218/16 600 128.255/16 3676 48 25 1

## Slide 23: flow-import
Import flows from other formats into flow-tools.
Currently supports ASCII and cflowd formats.

## Slide 24: flow-export
Export flows from flow-tools files to other formats.
Currently supports ASCII and cflowd formats.
ASCII output can be used with perl or other scripting languages (with a performance penalty).

## Slide 25: flow-xlate
Translate flows among NetFlow versions.
Originally intended for use with Catalyst switches since they export some flows in version 7 and others in version 5 format.

## Slide 26: Front End applications
Flow-tools is good at collecting raw flows
You may need additional tools to generate customized reports
Perl applications are very popular.
  flowscan.pm
  Cflow.pm
  CuGrapher.pl
Integration with RRDTool, MRTG etc. makes it more useful

## Slide 27: References
flow-tools: http://www.splintered.net/sw/flow-tools
NetFlow Applications http://www.inmon.com/technology/netflowapps.php
Netflow HOW-TO http://www.linuxgeek.org/netflow-howto.php
IETF standards effort: http://www.ietf.org/html.charters/ipfix-charter.html

## Slide 28: References
Abilene NetFlow page http://abilene-netflow.itec.oar.net/
Flow-tools mailing list: flow-tools@splintered.net
Cisco Centric Open Source Community http://cosi-nms.sourceforge.net/related.html