## Slide 1: An Introduction
  APRICOT 2008
  Network Management Workshop
  February 20-25 – Taipei, Taiwan
  Hervey Allen & Phil Regnauld

## Slide 2: Where Does Nagios Fit?
Nagios, in some ways, ties it all together. We've seen things like:
  SNMP
  MRTG
  RRDTool
  Rancid
  Cacti
  Smokeping
You can and will use all this functionality in Nagios.
It is a monolithic tool:
Big
Complex
Powerful

## Slide 3: Why Nagios
Open source
Relatively scalable, Manageable, Secure and more
Best documentation available
Good log and database system
Nice, informative and attractive web interface
Very flexible
Alerts automatically sent if condition changes
Various notification options (Email, pager, mobile phone)‏

## Slide 4: Why Nagios
Avoidance of “Too many red flashing lights”
“Just the facts” – only want root cause failures to be reported, not cascade of every downstream failure.
also avoids unnecessary checks
e.g. HTTP responds, therefore no need to ping
e.g. power outage, no ping response, so don’t bother trying anything else
Services are running fine no need to do check if the host itself is alive

## Slide 5: What Can it Do?
  Individual node status
  Is it up?
  What is its load?
  What is the memory and swap usage?
  NFS and network load?
  Are the partitions full?
  Are applications and services running properly?
  How about ping latency?
  Aggregated node status
  Same info, but across groups of nodes

## Slide 6: What Can it Do?
A lot, including:
Service monitoring
Alerts from SNMP traps
Monitoring redundancy
Detection of primary failure to avoid multiple like alerts.
Notifications via email, pager, etc.
Notifications to individuals or defined groups
Log information
Use databases to store history
Graph generation from MRTG
Very extensible via plug-ins, add-ons and local scripts.
Can scale to large installations
Allows for redundant monitoring
Aggregation of like-data across multiple nodes.
Ability to escalate alerts
Runs on multiple Unices
Licensed under GPL v2

## Slide 7
Check ping
Check ping
Web Client At NOC
Web UI
Gateway
Sample Setup
Check bandwidth
Web Client At NO
Gateway
Check host alive
Check dns
Check disk
Check memory
Check load

## Slide 9: Nagios Configuration

## Slide 10
Remaining Slides
Dhruba Raj Bhandari
(CCNA)‏
Additions by Phil Regnauld
bhandari.dhruba@scp.com.np

## Slide 11
  Nagios Status Detail screen

## Slide 12
Tactical Overview Of Nagios

## Slide 13
Service Detail of Nagios

## Slide 14
Service Types

## Slide 15
Status Map of MC Network From Nagios

## Slide 16
Status Overview from nagios

## Slide 17
Status Summary Based On Hostgroup

## Slide 18
Host Trends or Status History

## Slide 19
Histogram Of Host

## Slide 20
Event Logs

## Slide 21
Who is Notified?

## Slide 22
Notification Email Sample
From: nagios@thuldai.mos.com.np
To: "ishwars@mos.com.np" <ishwars@mos.com.np>
Subject: Host DOWN alert for WORLDBANK-L!
Date: 05/02/04 11:09
***** Nagios *****
Notification Type: PROBLEM
Host: WORLDBANK-L
State: DOWN
Address: 202.52.239.70
Info: PING CRITICAL - Packet loss = 100%
Date/Time: Thu Feb 5 11:06:38 NPT 2004

## Slide 23: Nagios configuration files
Located in /etc/nagios2/
Important files:
  cgi.cfg controls the Web Interface options security
  commands.cfg commands that Nagios uses to notify
  nagios.cfg main Nagios configuration file
  conf.d/* the core of the config files

## Slide 24: Nagios configuration files
Under conf.d/*, files “xxxx_nagios2.cfg”:
contacts users and groups
generic-host “template” host (default)‏
generic-service “template” service
hostgroups host group definitions
services which services to check
timeperiods when to check and notify

## Slide 25: Nagios plugin configuration
/etc/nagios-plugins/config/
apt.cfg ntp.cfg dhcp.cfg ping.cfg
disk.cfg procs.cfg dummy.cfg real.cfg
ftp.cfg ssh.cfg http.cfg tcp_udp.cfg
load.cfg telnet.cfg mail.cfg users.cfg
news.cfg

## Slide 27: Concepts: parents
Hosts can have parents
  Allows one to specify which dependencies there are in the network
  Avoid sending alarms if we cannot know the state of a host...

## Slide 29: Nagios – working principles

## Slide 30
Questions?