## Slide 1: Flow-tools Tutorial
Mark Fullmer
maf@splintered.net

## Slide 2: Agenda
Network flows
Cisco / Juniper implementation – NetFlow
Cisco / Juniper Configuration
flow-tools programs overview and examples from Abilene and Ohio-Gigapop

## Slide 3: Network Flows
Packets or frames that have a common attribute.
Creation and expiration policy – what conditions start and stop a flow.
Counters – packets,bytes,time.
Routing information – AS, network mask, interfaces.

## Slide 4: Network Flows
Unidirectional or bidirectional.
Bidirectional flows can contain other information such as round trip time, TCP behavior.
Application flows look past the headers to classify packets by their contents.
Aggregated flows – flows of flows.

## Slide 5: Unidirectional Flow with Source/Destination IP Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP
10.0.0.1 10.0.0.2
10.0.0.2 10.0.0.1

## Slide 6: Unidirectional Flow with Source/Destination IP Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP
10.0.0.1 10.0.0.2
10.0.0.2 10.0.0.1
% ping 10.0.0.2
ICMP echo reply

## Slide 7: Unidirectional Flow with IP, Port,Protocol Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP prot srcPort dstPort
10.0.0.1 10.0.0.2 TCP 32000 23
10.0.0.2 10.0.0.1 TCP 23 32000
10.0.0.1 10.0.0.2 ICMP 0 0
10.0.0.2 10.0.0.1 ICMP 0 0
% ping 10.0.0.2
ICMP echo reply

## Slide 8: Bidirectional Flow with IP, Port,Protocol Key
10.0.0.1
10.0.0.2
% telnet 10.0.0.2
login:
Active Flows
Flow Source IP Destination IP prot srcPort dstPort
10.0.0.1 10.0.0.2 TCP 32000 23
10.0.0.1 10.0.0.2 ICMP 0 0
% ping 10.0.0.2
ICMP echo reply

## Slide 9: Application Flow
10.0.0.1
10.0.0.2
% netscape http://10.0.0.2/9090
Content-type:
Active Flows
Flow Source IP Destination IP Application
10.0.0.1 10.0.0.2 HTTP
Web server on
Port 9090

## Slide 10: Aggregated Flow
Flow Source IP Destination IP prot srcPort dstPort
10.0.0.1 10.0.0.2 TCP 32000 23
10.0.0.2 10.0.0.1 TCP 23 32000
10.0.0.1 10.0.0.2 ICMP 0 0
10.0.0.2 10.0.0.1 ICMP 0 0
Source/Destination IP Aggregate
Flow Source IP Destination IP
10.0.0.1 10.0.0.2
10.0.0.2 10.0.0.1
Main Active flow table

## Slide 11: Flow Descriptors
A Key with more elements will generate more flows.
Greater number of flows leads to more post processing time to generate reports, more memory and CPU requirements for device generating flows.
Depends on application. Traffic engineering vs. intrusion detection.

## Slide 12: Flow Accounting
Accounting information accumulated with flows.
Packets, Bytes, Start Time, End Time.
Network routing information – masks and autonomous system number.

## Slide 13: Flow Collection
Passive monitor.
Router other existing network device.

## Slide 14: Passive Monitor Collection
Workstation A
Workstation B
Campus
Flow probe connected
to switch port in
“ traffic mirror” mode

## Slide 15: Router Collection
Flow collector
stores exported flows from router.
LAN
LAN
LAN
LAN
Internet

## Slide 16: Passive Monitor
Directly connected to a LAN segment via a switch port in “mirror” mode, optical splitter, or repeated segment.
Generate flows for all local LAN traffic.
Must have an interface or monitor deployed on each LAN segment.
Support for more detailed flows – bidirectional and application.

## Slide 17: Router Collection
Router will generate flows for traffic that is directed to the router.
Flows are not generated for local LAN traffic.
Limited to “simple” flow criteria (packet headers).
Generally easier to deploy – no new equipment.

## Slide 18: Cisco NetFlow
Unidirectional flows.
IPv4 unicast and multicast.
Aggregated and unaggregated.
Flows exported via UDP.
Supported on IOS and CatIOS platforms.
Catalyst NetFlow is different implementation.

## Slide 19: Cisco NetFlow Versions
4 Unaggregated types (1,5,6,7).
14 Aggregated types (8.x).
Each version has its own packet format.
Version 1 does not have sequence numbers – no way to detect lost flows.
The “version” defines what type of data is in the flow.
Some versions specific to Catalyst platform.

## Slide 20: NetFlow v1
Key fields: Source/Destination IP, Source/Destination Port, IP Protocol, ToS, Input interface.
Accounting: Packets, Octets, Start/End time, Output interface
Other: Bitwise OR of TCP flags.

## Slide 21: NetFlow v5
Key fields: Source/Destination IP, Source/Destination Port, IP Protocol, ToS, Input interface.
Accounting: Packets, Octets, Start/End time, Output interface.
Other: Bitwise OR of TCP flags, Source/Destination AS and IP Mask.
Packet format adds sequence numbers for detecting lost exports.

## Slide 22: NetFlow v8
Aggregated v5 flows.
3 Catalyst 65xx specific that correspond to the configurable flow mask.
Much less data to post process, but lose fine granularity of v5 – no IP addresses.

## Slide 23: NetFlow v8
AS
Protocol/Port
Source Prefix
Destination Prefix
Prefix
Destination (Catalyst 65xx)‏
Source/Destination (Catalyst 65xx)‏
Full Flow (Catalyst 65xx)

## Slide 24: NetFlow v8
ToS/AS
ToS/Protocol/Port
ToS/Source Prefix
ToS/Destination Prefix
Tos/Source/Destination Prefix
ToS/Prefix/Port

## Slide 25: NetFlow Packet Format
Common header among export versions.
All but v1 have a sequence number.
Version specific data field where N records of data type are exported.
N is determined by the size of the flow definition. Packet size is kept under ~1480 bytes. No fragmentation on Ethernet.

## Slide 26: NetFlow v5 Packet Example
NetFlow
v5 header
v5 record
IP/UDP packet
v5 record
…
…

## Slide 27: NetFlow v5 Packet (Header)‏
struct ftpdu_v5 {
/* 24 byte header */
u_int16 version; /* 5 */
u_int16 count; /* The number of records in the PDU */
u_int32 sysUpTime; /* Current time in millisecs since router booted */
u_int32 unix_secs; /* Current seconds since 0000 UTC 1970 */
u_int32 unix_nsecs; /* Residual nanoseconds since 0000 UTC 1970 */
u_int32 flow_sequence; /* Seq counter of total flows seen */
u_int8 engine_type; /* Type of flow switching engine (RP,VIP,etc.) */
u_int8 engine_id; /* Slot number of the flow switching engine */
u_int16 reserved;

## Slide 28: NetFlow v5 Packet (Records)‏
/* 48 byte payload */
struct ftrec_v5 {
u_int32 srcaddr; /* Source IP Address */
u_int32 dstaddr; /* Destination IP Address */
u_int32 nexthop; /* Next hop router's IP Address */
u_int16 input; /* Input interface index */
u_int16 output; /* Output interface index */
u_int32 dPkts; /* Packets sent in Duration */
u_int32 dOctets; /* Octets sent in Duration. */
u_int32 First; /* SysUptime at start of flow */
u_int32 Last; /* and of last packet of flow */
u_int16 srcport; /* TCP/UDP source port number or equivalent */
u_int16 dstport; /* TCP/UDP destination port number or equiv */
u_int8 pad;
u_int8 tcp_flags; /* Cumulative OR of tcp flags */
u_int8 prot; /* IP protocol, e.g., 6=TCP, 17=UDP, ... */
u_int8 tos; /* IP Type-of-Service */
u_int16 src_as; /* originating AS of source address */
u_int16 dst_as; /* originating AS of destination address */
u_int8 src_mask; /* source address prefix mask bits */
u_int8 dst_mask; /* destination address prefix mask bits */
u_int16 drops;
} records[FT_PDU_V5_MAXFLOWS];
};

## Slide 29: NetFlow v8 Packet Example (AS Aggregation)‏
NetFlow
v8 header
v8 record
IP/UDP packet
v8 record
…
…

## Slide 30: NetFlow v8 AS agg. Packet
struct ftpdu_v8_1 {
/* 28 byte header */
u_int16 version; /* 8 */
u_int16 count; /* The number of records in the PDU */
u_int32 sysUpTime; /* Current time in millisecs since router booted */
u_int32 unix_secs; /* Current seconds since 0000 UTC 1970 */
u_int32 unix_nsecs; /* Residual nanoseconds since 0000 UTC 1970 */
u_int32 flow_sequence; /* Seq counter of total flows seen */
u_int8 engine_type; /* Type of flow switching engine (RP,VIP,etc.) */
u_int8 engine_id; /* Slot number of the flow switching engine */
u_int8 aggregation; /* Aggregation method being used */
u_int8 agg_version; /* Version of the aggregation export */
u_int32 reserved;
/* 28 byte payload */
struct ftrec_v8_1 {
u_int32 dFlows; /* Number of flows */
u_int32 dPkts; /* Packets sent in duration */
u_int32 dOctets; /* Octets sent in duration */
u_int32 First; /* SysUpTime at start of flow */
u_int32 Last; /* and of last packet of flow */
u_int16 src_as; /* originating AS of source address */
u_int16 dst_as; /* originating AS of destination address */
u_int16 input; /* input interface index */
u_int16 output; /* output interface index */
} records[FT_PDU_V8_1_MAXFLOWS];
};

## Slide 31: Cisco IOS Configuration
Configured on each input interface.
Define the version.
Define the IP address of the collector (where to send the flows).
Optionally enable aggregation tables.
Optionally configure flow timeout and main (v5) flow table size.
Optionally configure sample rate.

## Slide 32: Cisco IOS Configuration
interface FastEthernet0/0/0
ip address 10.0.0.1 255.255.255.0
no ip directed-broadcast
ip route-cache flow
interface ATM1/0/0
no ip address
no ip directed-broadcast
ip route-cache flow
interface Loopback0
ip address 10.10.10.10 255.255.255.255
no ip directed-broadcast
ip flow-export version 5 origin-as
ip flow-export destination 10.0.0.10 5004
ip flow-export source loopback 0
ip flow-aggregation cache prefix
export destination 10.0.0.10 5555
enabled

## Slide 33: Cisco IOS Configuration
krc4#sh ip flow export
Flow export is enabled
Exporting flows to 10.0.0.10 (5004)‏
Exporting using source IP address 10.10.10.10
Version 5 flow records, origin-as
Cache for prefix aggregation:
Exporting flows to 10.0.0.10 (5555)‏
Exporting using source IP address 10.10.10.10
3176848179 flows exported in 105898459 udp datagrams
0 flows failed due to lack of export packet
45 export packets were sent up to process level
0 export packets were punted to the RP
5 export packets were dropped due to no fib
31 export packets were dropped due to adjacency issues
0 export packets were dropped due to fragmentation failures
0 export packets were dropped due to encapsulation fixup failures
0 export packets were dropped enqueuing for the RP
0 export packets were dropped due to IPC rate limiting
0 export packets were dropped due to output drops

## Slide 34: Cisco IOS Configuration
krc4#sho ip ca fl
IP packet size distribution (106519M total packets):
1-32 64 96 128 160 192 224 256 288 320 352 384 416 448 480
.002 .405 .076 .017 .011 .010 .007 .005 .004 .005 .004 .004 .003 .002 .002
512 544 576 1024 1536 2048 2560 3072 3584 4096 4608
.002 .006 .024 .032 .368 .000 .000 .000 .000 .000 .000
IP Flow Switching Cache, 4456704 bytes
36418 active, 29118 inactive, 3141073565 added
3132256745 ager polls, 0 flow alloc failures
Active flows timeout in 30 minutes
Inactive flows timeout in 15 seconds
last clearing of statistics never
Protocol Total Flows Packets Bytes Packets Active(Sec) Idle(Sec)‏
-------- Flows /Sec /Flow /Pkt /Sec /Flow /Flow
TCP-Telnet 2951815 0.6 61 216 42.2 26.6 21.4
TCP-FTP 24128311 5.6 71 748 402.3 15.0 26.3
TCP-FTPD 2865416 0.6 916 843 611.6 34.7 19.8
TCP-WWW 467748914 108.9 15 566 1675.8 4.9 21.6
TCP-SMTP 46697428 10.8 14 370 159.6 4.0 20.1
TCP-X 521071 0.1 203 608 24.7 24.5 24.2
TCP-BGP 2835505 0.6 5 94 3.3 16.2 20.7

## Slide 35: Cisco IOS Configuration
krc4#sho ip ca fl
TCP-other 1620253066 377.2 47 631 18001.6 27.3 23.4
UDP-DNS 125622144 29.2 2 78 82.5 4.6 24.7
UDP-NTP 67332976 15.6 1 76 22.0 2.7 23.4
UDP-TFTP 37173 0.0 2 76 0.0 4.1 24.6
UDP-Frag 68421 0.0 474 900 7.5 111.7 21.6
UDP-other 493337764 114.8 17 479 1990.3 3.8 20.2
ICMP 243659509 56.7 3 166 179.7 3.3 23.3
IGMP 18601 0.0 96 35 0.4 941.4 8.1
IPINIP 12246 0.0 69 52 0.1 548.4 15.2
GRE 125763 0.0 235 156 6.9 50.3 21.1
IP-other 75976755 17.6 2 78 45.4 3.9 22.8
Total: 3176854246 739.6 33 619 24797.4 16.2 22.6
SrcIf SrcIPaddress DstIf DstIPaddress Pr SrcP DstP Pkts
AT5/0/0.4 206.21.162.150 AT1/0/0.1 141.219.73.45 06 0E4B A029 507
AT4/0/0.10 132.235.174.9 AT1/0/0.1 137.99.166.126 06 04BE 074C 3
AT4/0/0.12 131.123.59.33 AT1/0/0.1 137.229.58.168 06 04BE 09BB 646
AT1/0/0.1 137.99.166.126 AT4/0/0.10 132.235.174.9 06 074C 04BE 3

## Slide 36: Juniper Configration
Sample packets with firewall filter and forward to routing engine.
Sampling rate is limited to 7000pps. Fine for traffic engineering, but restrictive for DoS and intrusion detection.
Juniper calls NetFlow cflowd.

## Slide 37: Juniper Configration
firewall {
filter all {
term all {
then {
sample;
accept;
}
}
}
}
forwarding-options {
sampling {
input {
family inet {
rate 100;
}
}
output {
cflowd 10.0.0.16{
port 2055;
version 5;
}
}
}
}
Firewall filter Enable sampling / flows

## Slide 38: Juniper Configration
interfaces {
ge-0/3/0 {
unit 0 {
family inet {
filter {
input all;
output all;
}
address 192.148.244.1/24;
}
}
}
Apply firewall filter to each interface.

## Slide 39: Flow-tools
Collection of programs to post process Cisco NetFlow compatible flows.
Written in C, designed to be fast (scales to large installations).
Includes library (ftlib) for custom applications.
Installation with configure;make;make install on most platforms (FreeBSD, Linux, Solaris, BSDi, NetBSD).

## Slide 40: flow-capture
Collect NetFlow exports and stores to disk.
Built in compression.
Manages disk space by expiring older flow files at configurable limits.
Detects lost flows by missing sequence numbers and stores with flow metadata.

## Slide 41: flow-fanout
Replicate NetFlow UDP streams from one source to many destinations.
Destination may be a multicast address.

## Slide 42: flow-expire
Expire (remove) old flow files based on disk usage.
Same functionality built in to flow-capture.
Used when managing disk space in a distributed environment.

## Slide 43: Abilene Configuration
Collect and process flows for Abilene routers.
Use sampled NetFlow.
Distribute flows to Asta and Arbor Networks.
Nightly usage reports.
Archive of raw anonymized flows.

## Slide 44: Collector Placement and configuration
NetFlow is UDP so the collector should ideally be directly connected to the router to minimize packet loss and IP spoofing risks.
No flow control. Undersized collector will drop flows. Monitor netstat –s | grep buf and configure syslog so dropped flows will be logged.

## Slide 45: flow-print
Formatted output of flow files.
eng1:% flow-print < ft-v05.2002-01-21.093345-0500 | head -15
srcIP dstIP prot srcPort dstPort octets packets
131.238.205.199 194.210.13.1 6 6346 40355 221 5
192.5.110.20 128.195.186.5 17 57040 33468 40 1
128.146.1.7 194.85.127.69 17 53 53 64 1
193.170.62.114 132.235.156.242 6 1453 1214 192 4
134.243.5.160 192.129.25.10 6 80 3360 654 7
132.235.156.242 193.170.62.114 6 1214 1453 160 4
130.206.43.51 130.101.99.107 6 3226 80 96 2
206.244.141.3 128.163.62.17 6 35593 80 739 10
206.244.141.3 128.163.62.17 6 35594 80 577 6
212.33.84.160 132.235.152.47 6 1447 1214 192 4
132.235.157.187 164.58.150.166 6 1214 56938 81 2
129.1.246.97 152.94.20.214 6 4541 6346 912 10
132.235.152.47 212.33.84.160 6 1214 1447 160 4
130.237.131.52 130.101.9.20 6 1246 80 902 15

## Slide 46: flow-cat
Concat many flow files or directories of files.
eng1:% ls
ft-v05.2002-01-21.160001-0500 ft-v05.2002-01-21.170001-0500
ft-v05.2002-01-21.161501-0500 ft-v05.2002-01-21.171501-0500
ft-v05.2002-01-21.163001-0500 ft-v05.2002-01-21.173001-0500
ft-v05.2002-01-21.164501-0500 tmp-v05.2002-01-21.174501-0500
eng1:% flow-cat . | flow-print
srcIP dstIP prot srcPort dstPort octets packets
138.26.220.46 192.5.110.20 17 62242 33456 40 1
143.105.55.23 18.123.66.15 17 41794 41794 40 1
129.15.134.66 164.107.69.33 6 1214 2222 4500 3
132.235.170.19 152.30.96.188 6 6346 1475 128 3

## Slide 47: flow-merge
Flow-merge is similar to flow-cat except it maintains relative ordering of flows when combining the files.
Typically used when combining flows from multiple collectors.

## Slide 48: flow-filter
Filter flows based on port, protocol, ASN, IP address, ToS bits, TCP bits, and tags.
eng1% flow-cat . | flow-filter -P119 | flow-print | head -10
srcIP dstIP prot srcPort dstPort octets packets
155.52.46.50 164.107.115.4 6 33225 119 114 2
128.223.220.29 129.137.4.135 6 52745 119 1438382 1022
155.52.46.50 164.107.115.4 6 33225 119 374 6
164.107.115.4 192.58.107.160 6 60141 119 5147961 8876
128.223.220.29 129.137.4.135 6 52745 119 1356325 965
128.223.220.29 129.137.4.135 6 52714 119 561016 398
130.207.244.18 129.22.8.64 6 36033 119 30194 121
155.52.46.50 164.107.115.4 6 33225 119 130 2
198.108.1.146 129.137.4.135 6 17800 119 210720652 216072

## Slide 49: flow-split
Split flow files into smaller files.
Typically used with flow-stat and graphing. For example if flow files are 1 hour and want 5 minute data points in graph, flow-split can take the 1 hour flow files and generate 5 minute files.

## Slide 50: flow-tag
Adds a tag field to flows based on IP exporter, IP prefix, Autonomous System, or next hop.
Like flow-filter used with other tools.
Used to manage groups of prefixes or ASN’s.

## Slide 51: flow-header
Display meta information in flow file.
eng1:% flow-header < ft-v05.2002-01-21.093345-0500
#
# mode: normal
# capture hostname: eng1.oar.net
# exporter IP address: 0.0.0.0
# capture start: Mon Jan 21 09:33:45 2002
# capture end: Mon Jan 21 09:45:01 2002
# capture period: 676 seconds
# compress: on
# byte order: little
# stream version: 3
# export version: 5
# lost flows: 0
# corrupt packets: 0
# sequencer resets: 0
# capture flows: 341370
#

## Slide 52: flow-stat
Generates reports from flow files.
Output is readable and easily imported into graphing programs (gnuplot, etc).
IP Address, IP address pairs, ports, packets, bytes, interfaces, next hop, Autonomous System, ToS bits, exporter, and tags.

## Slide 53: flow-stat - summary
Total Flows : 24236730
Total Octets : 71266806610
Total Packets : 109298006
Total Time (1/1000 secs) (flows): 289031186084
Duration of data (realtime) : 86400
Duration of data (1/1000 secs) : 88352112
Average flow time (1/1000 secs) : 11925.0000
Average packet size (octets) : 652.0000
Average flow size (octets) : 2940.0000
Average packets per flow : 4.0000
Average flows / second (flow) : 274.3201
Average flows / second (real) : 280.5177
Average Kbits / second (flow) : 6452.9880
Average Kbits / second (real) : 6598.7781

## Slide 54: flow-stat – Source AS % Total
#
# src AS flows octets packets duration
#
NSFNETTEST14-AS 6.430 6.582 7.019 5.693
ONENET-AS-1 2.914 4.417 3.529 3.566
UONET 0.600 4.052 2.484 1.979
UPITT-AS 1.847 3.816 2.697 2.552
CONCERT 1.786 2.931 2.391 1.955
OHIOU 3.961 2.601 2.140 1.655
CMU-ROUTER 1.962 2.577 2.349 2.075
BOSTONU-AS 1.503 2.126 1.665 1.914
PURDUE 2.185 1.994 2.157 2.507
STANFORD 2.124 1.950 2.270 2.636
UR 1.809 1.919 1.652 1.532
UMN-AGS-NET-AS 1.612 1.895 1.788 1.938
RISQ-AS 1.086 1.849 1.378 1.367
PENN-STATE 2.845 1.641 2.666 2.190
RIT-ASN 0.796 1.601 1.414 0.830

## Slide 55: flow-stat – Dest AS % Total
#
# dst AS flows octets packets duration
#
NSFNETTEST14-AS 6.202 9.564 8.005 6.762
PENN-STATE 2.037 3.774 2.712 2.153
CONCERT 2.628 3.133 2.888 2.326
ONENET-AS-1 2.818 2.434 2.906 3.000
STANFORD 1.915 2.360 2.122 2.195
JANET 2.508 2.319 2.150 2.485
0 0.831 2.187 2.431 2.910
DFN-WIN-AS 2.349 2.099 1.938 2.359
CMU-ROUTER 1.383 2.090 1.972 1.960
UONET 0.537 2.067 1.699 1.397
PURDUE 2.029 1.934 1.983 2.177
UMN-AGS-NET-AS 1.608 1.784 1.664 1.681
UPITT-AS 1.507 1.707 2.067 2.288
MIT-GATEWAYS 0.677 1.425 1.175 0.806
RIT-ASN 0.644 1.313 1.243 0.868
INDIANA-AS 0.899 1.285 0.996 0.781

## Slide 56: flow-stat – Src/Dest AS % Total
#
# src AS dst AS flows octets packets duration
#
GEORGIA-TECH PENN-STATE 0.030 0.965 0.459 0.071
NWU-AS 0 0.008 0.734 0.379 0.170
UONET CONCERT 0.064 0.698 0.438 0.290
UCLA NSFNETTEST14-AS 0.037 0.568 0.269 0.111
CONCERT UONET 0.052 0.543 0.364 0.221
BCNET-AS MIT-GATEWAYS 0.019 0.538 0.274 0.134
UONET 0 0.015 0.536 0.318 0.200
MIT-GATEWAYS STANFORD 0.032 0.477 0.245 0.073
ONENET-AS-1 NSFNETTEST14-AS 0.140 0.451 0.263 0.159
UONET PENN-STATE 0.019 0.439 0.200 0.063
NOAA-AS NOAA-FSL 0.018 0.438 0.255 0.031
DENET UONET 0.032 0.410 0.189 0.188
NSFNETTEST14-AS UC-DOM 0.022 0.365 0.244 0.081
ITALY-AS UONET 0.016 0.358 0.228 0.117
NSFNETTEST14-AS CONCERT 0.322 0.349 0.335 0.228
UONET ITALY-AS 0.022 0.349 0.210 0.130

## Slide 57: flow-stat – Src Port % Total
#
# port flows octets packets duration
#
1214 31.480 25.875 22.251 24.554
ftp-data 0.325 4.043 2.417 1.240
http 2.386 2.855 1.729 1.040
6346 4.124 2.224 3.619 5.886
unidata-ldm 0.105 0.893 0.526 0.384
synoptics-trap 0.214 0.844 0.994 1.016
ftp 0.326 0.616 0.386 0.324
6347 0.573 0.572 0.617 0.856
4662 0.293 0.505 0.363 0.524
0 0.015 0.460 0.217 0.099
ssh 0.117 0.411 0.329 0.173
873 0.014 0.371 0.173 0.086
5501 0.008 0.322 0.161 0.092
6701 0.008 0.320 0.153 0.085
aol 0.048 0.316 0.257 0.159
6699 0.106 0.280 0.215 0.269
nntp 0.995 0.234 2.960 2.637

## Slide 58: flow-stat – Dst Port % Total
#
# port flows octets packets duration
#
nntp 0.731 15.726 6.860 2.894
1214 32.274 11.156 20.411 21.875
6346 4.032 2.701 4.155 6.625
synoptics-trap 0.301 2.109 1.104 1.167
ftp-data 0.246 1.088 1.160 0.674
5020 0.003 0.892 0.359 0.023
55524 0.374 0.863 1.665 2.492
6347 0.680 0.488 0.643 0.972
vlsi-lm 0.016 0.447 0.190 0.029
42002 0.103 0.381 0.467 0.679
6699 0.196 0.332 0.300 0.382
4662 0.229 0.301 0.260 0.338
3534 0.013 0.243 0.109 0.037
netview-aix-3 0.024 0.221 0.102 0.048

## Slide 59: flow-stat – IP protocol % Total
#
# protocol flows octets packets duration
#
tcp 93.877 97.143 93.326 91.589
udp 4.257 2.466 5.932 8.286
icmp 1.337 0.368 0.576 0.117
169 0.500 0.019 0.155 0.002
gre 0.010 0.002 0.006 0.005
pim 0.012 0.002 0.004 0.001
ipv6 0.004 0.000 0.001 0.000
ax.25 0.001 0.000 0.000 0.000
ipencap 0.001 0.000 0.000 0.000
igmp 0.000 0.000 0.000 0.000
ospf 0.001 0.000 0.000 0.000
rsvp 0.000 0.000 0.000 0.000

## Slide 60: flow-stat –Src/Dst Prefix % Total
#
# Source Prefix Destination Prefix flows octets packets duration
#
130.207/16 128.186/16 0.016 3.091 1.321 0.100
130.207/16 130.203/16 0.019 2.110 0.904 0.113
198.108/24 130.207/16 0.023 2.097 0.855 0.194
169.232/16 128.169/16 0.086 1.420 0.644 0.428
134.79/16 65.118.160/20 0.008 1.158 0.467 0.031
18/8 130.207/16 0.030 1.042 0.572 0.141
129.171.96/19 128.223/16 0.019 0.848 0.341 0.142
138.26/16 193.190/15 0.006 0.574 0.245 0.046
128.109/16 146.229/16 0.014 0.558 0.231 0.078
128.109/16 170.140/16 0.014 0.536 0.221 0.063
130.207/16 18/8 0.034 0.493 0.416 0.134
128.223/16 130.207/16 0.017 0.476 0.200 0.118
128.109/16 131.96/16 0.018 0.463 0.190 0.096

## Slide 61: flow-stat – ifIndex % Total
#
# in out flows octets packets duration
#
3 2 12.556 12.568 12.574 11.991
2 3 9.557 11.644 10.313 9.716
4 2 8.172 8.896 8.274 8.528
6 4 14.815 8.712 10.820 11.394
2 4 9.131 8.033 8.565 9.162
4 6 9.433 6.797 7.526 8.197
8 3 2.085 3.245 2.317 2.105
2 75 0.055 3.110 1.382 0.158
6 2 2.759 3.024 2.855 2.950
9 3 1.792 2.992 2.133 1.908
3 91 1.002 2.361 1.595 1.284
9 4 2.057 2.132 1.967 2.105
2 6 2.301 1.698 2.463 3.010
3 9 1.713 1.447 1.760 1.697
3 8 1.614 1.311 1.639 1.698

## Slide 62: flow-stat – Next-Hop % Total
#
# IPaddr flows octets packets duration
#
0.0.0.0 37.738 43.011 41.829 41.883
198.32.8.66 30.848 22.665 25.417 26.778
198.32.8.41 16.807 22.348 18.870 17.164
198.32.8.33 13.363 9.943 11.361 12.582
199.77.193.9 0.775 1.037 1.697 1.069
192.80.53.46 0.132 0.532 0.279 0.108
192.80.53.42 0.073 0.211 0.185 0.159
131.247.47.246 0.103 0.100 0.105 0.080
192.111.110.5 0.044 0.079 0.052 0.050
198.32.252.253 0.082 0.059 0.182 0.105
192.208.151.9 0.022 0.012 0.018 0.018
131.95.1.25 0.008 0.003 0.004 0.004
192.208.151.13 0.002 0.001 0.001 0.000
192.80.53.44 0.000 0.000 0.000 0.000
131.247.47.244 0.000 0.000 0.000 0.000
198.32.11.72 0.000 0.000 0.000 0.000

## Slide 63: flow-stat – Multicast S,G % Total
#
# src IPaddr dst IPaddr flows octets packets duration
#
141.117.45.72 233.2.171.38 2.455 13.233 4.169 3.734
198.49.215.223 224.2.177.155 2.437 8.630 5.859 4.433
131.193.77.102 224.2.177.155 2.249 8.369 4.340 4.066
192.88.194.131 224.2.177.155 2.278 6.381 4.407 4.059
206.75.91.24 224.2.177.155 2.241 6.111 4.876 4.086
128.163.209.73 233.2.171.38 1.304 5.784 3.349 2.546
140.221.8.157 224.2.177.155 2.280 5.245 4.435 4.085
128.3.10.50 224.2.177.155 2.261 5.177 4.660 4.071
128.135.152.209 224.2.177.155 2.281 4.716 4.494 4.111
130.111.39.202 224.2.177.155 1.222 3.876 2.696 2.345
129.79.245.225 233.2.171.38 1.125 3.715 2.521 2.063
199.104.137.2 224.2.177.155 2.283 2.964 4.461 4.096
192.231.212.52 224.2.177.155 0.560 2.865 1.319 1.007
128.182.61.42 233.2.171.38 1.691 2.687 3.267 3.012

## Slide 64: flow-stat – ToS % Total
#
# ToS flows octets packets duration
#
0 96.178 93.067 93.752 94.926
32 1.196 2.230 2.524 1.788
64 1.031 1.822 1.475 1.675
16 0.324 1.535 0.838 0.427
8 0.104 0.698 0.588 0.321
96 0.166 0.182 0.147 0.093
36 0.349 0.149 0.226 0.275
128 0.117 0.070 0.108 0.151
224 0.130 0.036 0.079 0.100
192 0.221 0.033 0.087 0.022
200 0.004 0.016 0.009 0.006
232 0.001 0.014 0.007 0.005
244 0.012 0.012 0.013 0.024
236 0.012 0.009 0.011 0.020
24 0.010 0.008 0.008 0.013

## Slide 65: flow-stat – ToS 0010000xx % Total
#
# Source Prefix Destination Prefix flows octets packets duration
#
128.186/16 131.193/16 0.270 8.619 3.243 1.344
146.201/16 141.213/16 0.547 7.105 2.689 2.444
128.186/16 129.252/16 0.349 5.958 2.455 1.609
128.186/16 152.7/16 0.638 3.960 1.592 0.848
128.186/16 141.213/16 0.314 3.037 1.240 1.152
128.186/16 129.21/16 1.280 2.416 2.132 1.632
128.186/16 128.239/16 0.824 2.394 1.050 0.806
128.186/16 130.207/16 1.679 2.322 29.290 7.148
128.186/16 199.240/18 0.151 2.082 0.785 0.719
128.186/16 130.108/16 0.295 2.036 0.767 1.213
128.186/16 128.227/16 0.569 2.034 0.988 1.375
128.186/16 139.78/16 0.321 1.962 1.047 0.938

## Slide 66: flow-dscan
DoS detection / network scanning tool.
Flag hosts which have flows to many other hosts.
Flag hosts which are using a large number of TCP/UDP ports.
Works better on smaller networks or with flow-filter to limit traffic. For example filter TCP port 25 to detect hosts infected with e-mail worm.

## Slide 67: flow-gen
Debugging tool to generate flows.
eng1:% flow-gen -V8.1 | flow-print | head -10
srcAS dstAS in out flows octets packets duration
0 65280 0 65280 2 1 1 4294901760
1 65281 1 65281 4 2 2 4294901760
2 65282 2 65282 6 3 3 4294901760
3 65283 3 65283 8 4 4 4294901760
4 65284 4 65284 10 5 5 4294901760
5 65285 5 65285 12 6 6 4294901760
6 65286 6 65286 14 7 7 4294901760
7 65287 7 65287 16 8 8 4294901760
8 65288 8 65288 18 9 9 4294901760

## Slide 68: flow-send
Transmit flow files with NetFlow protocol to another collector.
Can be used to take flow-tools files and send them to other NetFlow compatible collector.

## Slide 69: flow-receive
Like flow-capture but does not manage disk space. Output is to standard out and can be used directly with other flow-tools programs.
Typically used for debugging.
eng1:% flow-receive 0/0/5555 | flow-print
flow-receive: New exporter: time=1011652474 src_ip=199.18.112.114
dst_ip=199.18.97.102 d_version=8
srcPrefix srcAS dstPrefix dstAS input output flows
143.105/16 600 128.9/16 4 48 25 1
140.141/16 600 150.216/16 81 48 25 4
132.235/16 17135 130.49/17 4130 38 25 25
131.123/16 11050 129.59/16 7212 42 25 1
206.21/16 600 128.239/16 11975 48 25 2
199.218/16 600 128.255/16 3676 48 25 1

## Slide 70: flow-import
Import flows from other formats into flow-tools.
Currently supports ASCII and cflowd formats.

## Slide 71: flow-export
Export flows from flow-tools files to other formats.
Currently supports ASCII and cflowd formats.
ASCII output can be used with perl or other scripting languages (with a performance penalty).

## Slide 72: flow-xlate
Translate flows among NetFlow versions.
Originally intended for use with Catalyst switches since they export some flows in version 7 and others in version 5 format.

## Slide 73: References
flow-tools: http://www.splintered.net/sw/flow-tools
NetFlow Applications http://www.inmon.com/technology/netflowapps.php
Netflow HOW-TO http://www.linuxgeek.org/netflow-howto.php
IETF standards effort: http://ipfix.doit.wisc.edu

## Slide 74: References
flow-tools: http://www.splintered.net/sw/flow-tools
Abilene NetFlow page http://www.itec.oar.net/abilene-netflow
Flow-tools mailing list: flow-tools@splintered.net
Cisco Centric Open Source Community http://cosi-nms.sourceforge.net/related.html