## Slide 1: Cisco configuration elelements
  APRICOT 2008
Network Management
Taipei, Taiwan
February 20-24, 2008

## Slide 2: Overview
Basic things that we need to make sure are configured on a Cisco router (and switch) to do proper network management
These apply to other network equipment manufacturers of course, and to servers and workstations

## Slide 3: Elements
Hostname hostname of the device
SSH enable secure shell
DNS domain name lookup
NTP time synchronization
Syslog syslog messages
SNMP SNMP configuration
SNMP traps and where to send traps
CDP Cisco discovery protocol

## Slide 4: Hostname
Use the FQDN preferably.
In config mode: hostname gw|sw-XYZ[.domain.name]

## Slide 5: DNS configuration
Config mode: ip domain-name mgmt.conference.apricot.net ip name-server 169.223.2.2

## Slide 6: NTP + time configuration
In config mode: ntp server pool.ntp.org clock timezone CWT 8
If needed: clock summer-time XXX recurring last Sun Mar 2:00 last Sun Oct 3:00
Verify: show clock

## Slide 7: SSH
Only crypto version of IOS/CatOS have support for SSH – there are export restrictions... In config mode: aaa new-model crypto key generate rsa username inst secret 0 xxxxxxxxx
... above is required to be allowed to enable SSH. Verify creation with: sh crypto key mypubkey rsa
Use at least 768 bits

## Slide 8: SSH (2)‏
Enforce ssh (disabling telnet) on vty lines: host# conf t host(config)# line vty 0 4 host(config-line)# transport input ssh ^Z host#
SSH is now enabled, and the telnet disabled

## Slide 9: Syslog
In config mode: logging noc.mgmt.conference.apricot.net logging facility local5 logging trap debugging

## Slide 10: SNMP
In config mode: snmp-server community xxxxxxxxx RW snmp-server community apric0t08 RO snmp-server location Taipei, room 403 snmp-server enable traps config snmp-server enable traps envmon snmp-server enable traps config snmp-server enable traps syslog snmp-server host xxx (see cisco doc)‏

## Slide 11: CDP
Cisco Discovery Protocol
Normally enabled by default nowadays
Otherwise, enabled with ”cdp enable”
tcpdump and tools like cdpr will show you CDP announcements